## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Multi-millisecond Ranging]
Date Submitted: [29th March 2022]
Source: [Billy Verso, Carl Murray, Michael McLaughlin, Jarek Niewczas, Igor Dotlic, Ciaran McElroy ] Company [Qorvo, Inc.]
Address [ ]
E-Mail:[billy.verso (at) qorvo.com]
Re: [Long-range two-way ranging for the TG4ab next generation UWB project]
Abstract: [Discussion on Multi-millisecond Ranging.]
Purpose: [Discussion on Multi-millisecond Ranging and the need for a tightly coupled narrowband radio.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Multi-millisecond ranging
UWB energy output is restricted by regulation to 37 nJ per millisecond per 500 MHz
This imposes limitations on what can be achieved in terms two-way-ranging (TWR) performance at long-range, or where the direct (shortest) path is severely attenuated.
To improve ranging performance, in 15-21-0409 and its successors, Ersen et al. proposed a multi-millisecond ranging technique combining multiple 37nJ sequence fragments.
A key element of this is being able to acquire and lock the receiver to the remote transmitter’s carrier/timing to prime the receiver for the reception/accumulation of subsequent fragments.
Submission 15-21-0409 proposed that this initial (T0) be fulfilled by a “tightly-coupled” narrowband radio.
The CZC codes Michael proposes in 15-22-0178 can also be used for this purpose.
Using CZC codes has the potential to give a UWB only solution to long-range (multi-millisecond) ranging.
  Some implementers may prefer to avoid the additional complexity of a narrowband radio.

## Slide 3: Data need not be the bottleneck
While many ranging use cases are short range like the access control distance bounding case, there are two cases to consider where multi-millisecond UWB ranging comes into play:
  Case (a) Long range line-of-sight, and case (b) Short range highly attenuated first path.
When first path sensitivity is greater than data sensitivity, a fixed reply time is the ideal solution for case (a), here even a few ns of fixed reply time error is a small fraction of the LOS TOF operating range, and a message to convey Treply is unnecessary.
For case (b), there are generally stronger reflected paths via which to receive a data message (D0) carrying an accurate Treply measurement to yield a precise TOF result.
  Message D0 can be sent using UWB.
  In cases where message D0 is not received the fixed reply time gives a reasonable TOF result and distance estimate.

## Slide 4: Other use cases for Narrowband
Some thoughts on the other proposed uses of the narrowband radio:
The other proposed use cases for a narrowband radio seem not to need the “tight coupling” of clocks, etc.
So, can these can be implemented by existing radios specified in 802.15.4, or Bluetooth etc. ?
Also, perhaps they are more naturally specified above the MAC and so more properly addressed in forums like FiRa, CCC, CSA, etc., where the upper layer protocols are defined.

## Slide 5: Conclusion
The UWB based proposals already presented at TG4ab represent significant advancement over 4z performance
  Wake-up radio, multi-millisecond fragmented ranging, CZC codes, longer range lower data rates, data coding, etc.
A high performing UWB-only solution may be possible, and there are many use cases where the inclusion of another (a third?) radio may be undesirable, however we accept that there are use cases where a narrowband radio will bring real utility…
So, we would like to see the group work together to study the trade-offs of these approaches and agree the optimum solution for the use cases we are trying to address.

## Slide 6
THE END