## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Review of UWB Coex Contributions]
Date Submitted: [09 May, 2022]
Source: [Shang-Te Yang, Robert Golshan] Company [Apple]
Re: [Input to the Working Group]
Abstract: [Presentation, UWB in 802.15, coex]
Purpose: []
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
PAR Objective | Proposed Solution (how addressed)
Safeguards so that the high throughput data use cases will not cause significant disruption to low duty-cycle ranging use cases | Review coex mitigations mentioned in contributions
Interference mitigation techniques to support higher density and higher traffic use cases | 
Other coexistence improvement | 
Backward compatibility with enhanced ranging capable devices (ERDEVs) | 
Improved link budget and/or reduced air-time | 
Additional channels and operating frequencies | 
Improvements to accuracy / precision / reliability and interoperability for high-integrity ranging | 
Reduced complexity and power consumption | 
Hybrid operation with narrowband signaling to assist UWB | 
Enhanced native discovery and connection setup mechanisms | 
Sensing capabilities to support presence detection and environment mapping | 
Low-power low-latency streaming | 
Higher data-rate streaming allowing at least 50 Mbit/s of throughput | 
Support for peer-to-peer, peer-to-multi-peer, and station-to-infrastructure protocols | 
Infrastructure synchronization mechanisms | 

## Slide 3: UWB Coexistence Challenges
UWB devices are increasingly used in a growing number of applications: Time-of-Flight (ToF), Sensing and Data Streaming
  Mitigations to managing UWB interference is needed across devices and applications.
  Success will depend on a wide adoption of a common set of techniques.
Sensing coex needs broader consideration, including sensing-to-sensing and sensing-to-ranging.
  The radar equation example in [1] is using 4.4ms airtime every 5ms (88%) indefinitely to measure human heartbeat at 10m.
  Band stitching in [2] implies more spectrum-time usage, thus creating more interference while more susceptible to interference.

## Slide 4: Mitigations from Contributions
Coordinated mitigations
  DL-TDoA and multi-static sensing share similar Tx/Rx patterns thus a joint Ranging-Sensing network could potentially coordinate all operations using TDMA [2].
    May be less applicable for many co-located mono-static sensing devices and ranging networks.
Uncoordinated mitigations
  Some flavor of CCA with some flavor of backoff [3].
  Use different preamble code for data streaming application [4].
  Pulse Repetition Frequency Domain Multiple Access (PRFDMA) by dithering chip rate [800ppm step up to +/-2%] but keeping carrier frequency the same [5].
    Q. Is this idea somewhat related to the staggered PRF?
  Leverage different preamble codes for sensing, such as using Ipatov sequences with multiple spreading factors (i.e., PRFs {499, ..., 4} MHz) [2].
    Q. Is it going to false trigger legacy packets?
    The PRF could be much higher than the monostatic example shown in [1]. Is this geared toward multi-static scenario only?

## Slide 5: Summary
We consider UWB ranging to be a low-duty cycle application and mostly a victim of other high-duty cycle UWB activities.
Many ideas have been mentioned and this is an open request for further elaboration. We have no preference at this moment.
Suggest future coex mitigation proposals to clearly state the impact to legacy 4z systems, 4ab ranging systems, high-data rate systems, and sensing systems.
  As an IEEE group, we need to agree on benchmark coex scenarios and define metric of coex performance.

## Slide 6: References
[1] D. Wisland, K. Granhaug, D. Neirynck, “UWB sensing concepts,” Jan 2022, doc.: <15-22-0083-01>
[2] D. Wisland et al., “Sensing Device,” Mar 2022, doc.: <15-22-0175-00>
[3] F. Nabki, “MAC layer considerations for UWB data streaming,” Jan 2022, doc.: <15-22-0047-01>
[4] C. Aldana, “Preamble codes for Data Communications,” Oct 2021, doc.: <15-21-0377-02>
[5] F. Leong, W. Küchler, R. Pirhonen, “Ranging QoS,” Nov 2021, doc.: <15-21-0590-00>