## Slide 1
Project: IEEE P802.15 Working Group for Wireless Specialty Networks
Submission Title: Channel Model for Wearable and Implant BAN in use case of BMI and BCI
Date Submitted: July 13th , 2022
Source: Takumi Kobayashi, Minsoo Kim, Marco Hernandez, Ryuji Kohno
Company: (1)Yokohama National University (2) YRP International Alliance Institute
Address: (1)79-5 Tokiwadai, Hodogaya-ku, Yokohama, 240-8501 Japan,
(2) YRP1 Blg., 3-4 HikarinoOka, Yokosuka-City, Kanagawa, 239-0847 Japan
Voice:[+81-90-5408-0611] E-Mail:[minsoo@minsookim.com, kobayashi-takumi-ch@ynu.ac.jp, marco.hernandez@ieee.org, kohno@ynu.ac.jp, Kohno@yrp-iai.jp]
Re: In response to call for technical contributions
Abstract: This provides draft of channel and environmental model and its classification for vehicle body area network(VBAN) of amendment of IEEE802.15.6-2012 for wireless body area network(BAN) with enhanced dependability.
Purpose: Material for discussion in P802.15.6ma TG corresponding to comments in EC Meeting
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Channel Model for Wearable and Implant BAN in use case of BMI and BCI
Takumi Kobayashi (1,2), Marco Hernandez (2), Minsoo Kim (2), Ryuji Kohno(1,2)
(1)Yokohama National University, (2)YRP-International Ariane Institute

## Slide 3: Classification of Channel and Environment Models for Human and Vehicle Body Area Networks (HBAN&VBAN)
Note:
HBAN-model:
-Environment with co-existing systems is not considered.
VBAN model:
Key-less entry system
Localization in-body, on-body
Most dominant model should be defined and separatory defined as Mandatory and Optional.
Channel model
HBAN model
VBAN model
In-body (Implant)
On-body
Around body
Outdoor
Indoor
Home
Office
Medical (e.g. Hospital)
In-vehicle
On-vehicle
Around vehicle
Engine compartment
Cabin
Through Engine compartment and cabin
Roof
Side Right/Left/Front/back
Bottom
Static vehicle
Moving vehicle
※Covered by IEEE 802.15.6-2012
※Around means;
Desk, WiFi AP in the room etc.
Channel model
With environment
※
※
※
※
※
Implanted BCI model
※not covered in 2012
On skull BCI model
capsule endoscopy

## Slide 4: Channel models and scenarios in IEEE802.15.6-2012
IEEE 802.15.6-2012 channel models considered
Fading ( Small scale/ large scale)
Path loss
Shadowing
Power delay profile
In-body (implant)
On-body (body surface)
CM1, 2, 3, 4
Scenario 1, to Scenario 7. (S1 – S7)
IEEE P802.15-08-0780-12-0006-TG6

## Slide 5: Channel models and scenarios in IEEE802.15.6ma
Fading ( Small scale/ large scale)
Path loss
Shadowing
Power delay profile
In-body (implant)
On-body (body surface)
In-body (BCI)
On-body (BCI)
capsule endoscopy
Need to discuss standard antenna issues.
Scenario | Description | Frequency Band | Channel Model
S1 | Implant to Implant | 402-405 MHz, 3.1-10.6 GHz UWB | CM1
S2 | Implant to Body Surface | 402-405 MHz, 3.1-10.6 GHz UWB | CM2
S3 | Implant to External | 402-405 MHz, 3.1-10.6 GHz UWB | CM2
S4 | Body Surface to Body Surface (LOS) | 400, 600, 900 MHz 2.4, 3.1-10.6 GHz | CM3
S5 | Body Surface to Body Surface (NLOS) | 400, 600, 900 MHz 2.4, 3.1-10.6 GHz | CM3
S6 | Body Surface to External (LOS) | 900 MHz 2.4, 3.1-10.6 GHz | CM4
S7 | Body Surface to External (NLOS) | 900 MHz 2.4, 3.1-10.6 GHz | CM4
Specific use cases |  |  | 
Implant to Body Surface for BCI | Implant to Body Surface for BCI |  | 
Implant to External for BCI | Implant to External for BCI |  | 
Body Surface to External for BCI | Body Surface to Body Surface for BCI |  | 
Implant to body surface for capsule endoscopy | Implant to External capsule endoscopy |  | 

## Slide 6: Channel models and scenarios in use case of BMI and BCI
Specific use cases
Implant to Body Surface for BCI
Implant to External for BCI
Body Surface to External for BCI
Implant to Body surface for capsule endoscopy
Implant to Body Surface for BCI
Body Surface to External for BCI
Wired connection
Implant to External for BCI
Body Surface to Body Surface for BCI
We will define what is BCI and BMI.

## Slide 7: Suggestion from Prof. Hirata
Arm
Implant to implant model for next Gen.

## Slide 8: BCI implanted device configuration
Brain
Skin
Skull bone
Skull bone
Skin
Skull bone
Brain
Device
Brain
Skull bone
Device
Skin
Skull bone
Device
Skin
Brain
electrodes
<10mm
Brain

## Slide 9: 1st generation
Brain
Skin
Skull bone
Skull bone
Transmitter Device
electrodes
<10mm
Wired connection
Receiver
Device

## Slide 10: 1.5 Gen.
Transmitter Device
Brain
Skull bone
Skin
Skull bone
electrodes
Receiver
Device
<10mm
Receiver can be placed any where on body like on arm, wrist, neck etc.

## Slide 11: 1.5 Gen.
Receiver
Device
Transmitter Device
Brain
Skull bone
Skin
Skull bone
electrodes
Receiver
Device
<10mm
Receiver can be placed any where on body like on arm, wrist, neck etc.

## Slide 12: Ideal 2nd generation
Brain
Skin
Skull bone
Skull bone
Transmitter
electrodes
<10mm
Receiver

## Slide 13: Titanium courted implanted device
RF
RF
Ant.
RF
Ant.
Ant.
Metal e.g. Titanium
Metal e.g. Titanium
Metal e.g. Titanium
Non-metallic material
Whole body of an implanted device is covered by metallic material.
Partially non-metallic window is on the surface of the implant devices.
Antenna is outside of metallic chassis

## Slide 14: Channel models and scenarios in use case of capsule endoscopy
Specific use cases
Implant to Body Surface for BCI
Implant to External for BCI
Body Surface to External for BCI
Implant to body surface for capsule endoscopy
Gastrointestinal tract
Implant to Body Surface for Capsule Endoscopy
capsule endoscopy
Transceiver on body surface

## Slide 15: Whole-body voxel human models for numerical simulation
Development of whole-body voxel human models
https://emc.nict.go.jp/bio/model/model01_1_e.html
Whole-body voxel human models for numerical simulation is ready to use to develop and analyze channel and environmental model around human brain numerically.

## Slide 16
Channel model
Large scale fading
Small scale fading
HBAN
Channel model
VBAN
Channel model
Path loss
Shadowing
In-body
On-body
Surrounding body
In-vehicle
On-vehicle
Surrounding vehicle
From 15.6-2012
From 15.4a
UWB Channel model
Simulation methodology
HBAN
Channel model
In-body
On-body
Surrounding body
VBAN
Channel model
In-vehicle
On-vehicle
Surrounding vehicle
15.4a Indoor residential
15.4 outdoor
15.4 Indoor residential
15.4 outdoor
Marco san provided
15.8
From 15.4ab

## Slide 17: Channel and Environmental Models
Path loss
Reflection
Multipath
Fading
LOS / NLOS model
White Gaussian noise
Interference from co-existing wireless systems e.g. Bluetooth, IEEE 802.11, IEEE 802.15.4 etc.
Interference from the other BANs.
Interference from the other electric systems, devices and components (Electro-magnetic interference; EMI from electric motors, spark plugs in vehicles, etc.
Electro-magnetic compatibility; EMC. Possibility to affect to the other systems and human body.
VBAN  HBAN interference
VBAN and HBAN  Vehicle control and human body impacts.
Colored noise (Impulse noise, spike noise, ignition noise etc.)
Time-varying channel and interference modeling (Statistic, non-static, pseudo static model)
※optional
or
?
Environment model
Channel model
Channel model
EMI EMC
Colored noise
Other wireless systems
Environment model
Time-varying modeling
※mandatory
※mandatory
※mandatory
※mandatory
※optional
※optional
※optional
※IEEE802.15.6-2012
※will be defined in this amendment
※mandatory
or
?
※mandatory
※Comments in May 2021.

## Slide 18
RF
ANT
Propagation Model （based on S-V Model）
Interference from the other BAN
Interference from the other UWB (not BAN)
+
EMI from vehicle system
Colored noise
EV Switching noise
Ignition noise
etc…
RF
ANT
Channel model
Distance dependent function
Distance dependent function
Standard antenna
Standard antenna
Environmental model
Interference from the other Wireless systems
We propose to define environmental models including antenna effect. Parameter measurements will be performed by using standard antennas which will be defined separately.

## Slide 19
HBAN coordinator to HBAN coordinator
Body surface to body surface
Cannot be considered similar
Body surface to body surface
Body surface to ANOTHER body surface
Need to consider SAR issues

## Slide 20: Thank you for your attention