## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [High Data Rates and Coding]
Date Submitted: [11 May, 2022]
Source: [Carlos Aldana, Chunyu Hu, Kangjin Yoon, Claudio da Silva (Meta), Billy Verso, Jarek Niewczas, Carl Murray, Michael McLaughlin (Qorvo), Frank Leong, Riku Pirhonen, Wolfgang Küchler, Abdul Wahid Abdul Kareem, Jianxuan Du (NXP Semiconductors)]
Re: [Input to the Working Group]
Abstract: [Presentation, UWB in 802.15, high data rates, coding]
Purpose: []
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
PAR Objective | Proposed Solution (how addressed)
Safeguards so that the high throughput data use cases will not cause significant disruption to low duty-cycle ranging use cases | 
Interference mitigation techniques to support higher density and higher traffic use cases | 
Other coexistence improvement | 
Backward compatibility with enhanced ranging capable devices (ERDEVs) | Re-use of existing PHY elements
Improved link budget and/or reduced air-time | Reduced air-time via high data rates
Additional channels and operating frequencies | 
Improvements to accuracy / precision / reliability and interoperability for high-integrity ranging | 
Reduced complexity and power consumption | 
Hybrid operation with narrowband signaling to assist UWB | 
Enhanced native discovery and connection setup mechanisms | 
Sensing capabilities to support presence detection and environment mapping | 
Low-power low-latency streaming | Low latency via high data rates
Higher data-rate streaming allowing at least 50 Mbit/s of throughput | Data rates higher than 50 Mbit/s
Support for peer-to-peer, peer-to-multi-peer, and station-to-infrastructure protocols | 
Infrastructure synchronization mechanisms | 

## Slide 3: High Data Rates and Coding

## Slide 4: Consensus among Co-authors (I)
We agree that a convincing case can be made in support of inclusion of high data rates in the 15.4ab amendment, beyond the data rates currently available in the 15.4z amendment
  Assuming coding rate of 1/2, we agree on a data rate of 62.4 Mbit/s (minor changes in coding rate and correspondingly in data rate may apply)
  Assuming coding rate of 1/2, pending outcome of further study, we consider additionally a data rate of 124.8 Mbit/s (minor changes in coding rate and correspondingly in data rate may apply)
  We agree that additional modulation schemes shall not significantly increase implementation complexity compared to the schemes available in 15.4z
  Associated modulation schemes to be agreed and added as HPRF modes, pending outcome of further study
We agree that these higher data rates shall be based on considerations in line with those underlying the 15.4z HPRF modulation schemes
We agree that a convincing case can be made in support of inclusion of lower data rates in the 15.4ab amendment
  Assuming coding rate of 1/2, we agree to adding new HPRF lower data rate mode(s) to offer a significant link budget gain compared to 4z HPRF 7.8 Mbit/s mode, details pending further study

## Slide 5: Consensus among Co-authors (II)
We agree that new data rates shall apply to both PHR and PSDU
  Changes to the PHR format are under consideration to accommodate the new PHY rate(s) and/or advanced coding schemes
We agree to include a single optional advanced coding scheme
  The advanced coding scheme shall have nominal coding rate 1/2
    Due to the PHR being very short, in this scheme the PHR (assumed similar in length to the 15.4z HPRF PHR) shall be encoded using K=7 convolutional coding, resulting in the desired combination of “stronger PHR than PSDU” due to PHR CC tail bits
  Primary candidate is the 802.11n LDPC code with block lengths {648,1296,1944}
    This scheme is well-known, field-tested, and supported by available implementations of known implementation loss, complexity, energy consumption, and latency
    Alternative schemes shall be evaluated for packet lengths of {30,100,1500} bytes at 1% PER, and may be disqualified if (worst-case) coding efficiency (also at any specific packet lengths other than the ones previously listed), implementation complexity, energy consumption, or latency are significantly worse than the 802.11n LDPC code
We agree that a convincing case can be made in support of inclusion of additional preamble schemes in the 15.4ab amendment
  Detailed schemes to be agreed, pending outcome of further study