## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Narrowband Channel Allocation for NBA-MMS-UWB]
Date Submitted: [6 July, 2022]
Source: [Alexander Krebs, Yong Liu, Lochan Verma, Jinjing Jiang, Tianqi Wang (Apple), Rias (Ghiath) Al-kadi, Frank Leong, Wolfgang Kuechler, Riku Pirhonen (NXP)]
Re: [Input to the Working Group]
Abstract: [This document presents rationale and simulation results for optimized spectral efficiency of narrowband O-QPSK PHY radio 2.5 MHz channel grid allocation in UNII-3 and UNII-5 bands and coexistence aspects of 802.11 radio.]
Purpose: []
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
PAR Objective | Proposed Solution (how addressed)
Safeguards so that the high throughput data use cases will not cause significant disruption to low duty-cycle ranging use cases | 
Interference mitigation techniques to support higher density and higher traffic use cases | 
Other coexistence improvement | 
Backward compatibility with enhanced ranging capable devices (ERDEVs) | 
Improved link budget and/or reduced air-time | O-QPSK occupied bandwidth based channel spacing optimization for spectral efficiency
Additional channels and operating frequencies | Allocation band map of NB channels in UNII-3/5
Improvements to accuracy / precision / reliability and interoperability for high-integrity ranging | 
Reduced complexity and power consumption | 
Hybrid operation with narrowband signaling to assist UWB | This describes the NB part
Enhanced native discovery and connection setup mechanisms | 
Sensing capabilities to support presence detection and environment mapping | 
Low-power low-latency streaming | 
Higher data-rate streaming allowing at least 50 Mbit/s of throughput | 
Support for peer-to-peer, peer-to-multi-peer, and station-to-infrastructure protocols | 
Infrastructure synchronization mechanisms | 

## Slide 3: NB O-QPSK Spectrum
Legacy 802.15.4 O-QPSK [1] channel allocation is not optimized
  O-QPSK 99% occupied bandwidth (OBW) [2] less than 2.4 MHz
  Below graphs compare 802.15.4 O-QPSK vs BLE 2M GMSK PHY (dashed line)
  Notably, BLE uses 2 MHz spacing, whereas legacy O-QPSK uses 5 MHz
OBW < 2.4 MHz
OBW > 2 MHz

## Slide 4: NB Channels
2.5 MHz channel spacing results in
  250 channels in aggregated UNII-3+5 (~229 permitted in most regions world wide)
  Center frequencies we investigate currently (aligned vs. unaligned)
    Aligned
    Unaligned

## Slide 5: NB Performance 1/2
Simulation parameters
  K Tx-Rx pairs randomly placed in 100m x 100m square, isotropic ant., P_out=10dBm
  Randomly selected channels within 125 MHz of total BW, 10 byte PSDU, B2B packets
  ACI via sum of FSPLs at 5.8GHz, PER via inverse SINR waterfall curves from [3]
+94%
Data Rate = 250kbps: Preamble length = 128us, SFD length = 32us, PHR length = 32us, Payload length = 320us, Total packet duration: 512us

## Slide 6: NB Performance 2/2
Additional O-QPSK modes proposed in [4]
250 kbps
1000 kbps
500 kbps
5 MHz 2.5 MHz
Data Rate = 500kbps
  Note both PHR and the payload go through the rate-1/2 convolutional code with generator polynomials (133, 171) as specified in Clause 21.3.6 of IEEE 802.15.4-2020 or in Clause 15.3.3 of IEEE 802.15.4z-2020
  Preamble length = 64us
  SFD length = 32us
  PHR length = 28us
  Payload length = 172us
  PHR carries (8+6)x2 = 28 coded bits
  Payload carrier (80+6)x2 = 172 coded bits
  Total packet duration: 296us
Data Rate = 1000kbps
  Preamble length = 64us
  SFD length = 32us
  PHR length = 8us
  Payload length = 80us
  Total packet duration: 184us

## Slide 7: Summary
Given the analyzed spectral properties of 802.15.4 O-QPSK modulation, we propose allocation of a total of 250 NB channels in UNII-3 and UNII-5 bands with channel spacing of 2.5 MHz, in order to increase spectral efficiency over the 5 MHz channel spacing used in legacy 802.15.4 at 2.4 GHz.
Simulations results show potential for increase in maximum network throughput for the legacy 250kpbs O-QPSK PHY, as well as the newly proposed 500 kbps CC r=1/2 K=7, and uncoded 1 Mbps modes, over both low and high density deployment use cases.
The proposed channel spacing targets current and prospected regulatory requirements in most regions world wide, under particular consideration of the occupied bandwidth criteria from ETSI and guard band requirements from FCC.

## Slide 8: References
[1] “IEEE 802.15.4-2020 Standard for Low-Rate Wireless Networks”, LAN/MAN Standards Working Group.
[2] ETSI EN 302 867 Draft 1, April 2022.
[3] S. Lanzisera and K. S. J. Pister, "Theoretical and Practical Limits to Sensitivity in IEEE 802.15.4 Receivers” 14th IEEE International Conference on Electronics, Circuits and Systems, 2007, pp. 1344-1347.
[4] X. Luo (Apple Inc), F. Leong (NXP), M. Lee (Samsung Electronics), et. al., “NBA-UWB Technical Framework Proposal”, 15-22-0262-01-004ab.