## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Narrowband Channel Access and Interference Mitigation for NBA-MMS-UWB]
Date Submitted: [11 July, 2022]
Source: [Alexander Krebs, Yong Liu, Lochan Verma, Jinjing Jiang, SK Yong (Apple)]
Re: [Input to the Working Group]
Abstract: [This documents presents proposed methods for signaling of coordinated NB access between NBA-MMS-UWB initiator and responder, frequency diversity achieving methods in coexistence with 802.11 radio, and proposal of LBT access methods for regulatory compliance.]
Purpose: []
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
PAR Objective | Proposed Solution (how addressed)
Safeguards so that the high throughput data use cases will not cause significant disruption to low duty-cycle ranging use cases | 
Interference mitigation techniques to support higher density and higher traffic use cases | PRNG randomized channel access, Wi-Fi aware channel switching mechanism
Other coexistence improvement | CCA-ED based LBT channel access
Backward compatibility with enhanced ranging capable devices (ERDEVs) | 
Improved link budget and/or reduced air-time | 
Additional channels and operating frequencies | 
Improvements to accuracy / precision / reliability and interoperability for high-integrity ranging | 
Reduced complexity and power consumption | 
Hybrid operation with narrowband signaling to assist UWB | This describes the NB part
Enhanced native discovery and connection setup mechanisms | 
Sensing capabilities to support presence detection and environment mapping | 
Low-power low-latency streaming | 
Higher data-rate streaming allowing at least 50 Mbit/s of throughput | 
Support for peer-to-peer, peer-to-multi-peer, and station-to-infrastructure protocols | 
Infrastructure synchronization mechanisms | 

## Slide 3: NB Channel MAC Signaling 1/2
Concept for coordinating access to 250 NB channels in aggregated UNII-3+5 with 2.5 MHz adjacent channel spacing [1]
  Enumeration of commonly used macNbaUwbChannelAllowList[] presets
  Presets macNbaUwbChannelAllowList[][0] and [1] as empty, and full set of channels as start off point for macNbaUwbChannelAllowListUpdate()
  Additional presets, e.g., to fit regulatory/custom applications aspects
Example application: coordination of common set of allowed channels between devices from different regulatory domains, and band support

## Slide 4: NB Channel MAC Signaling 2/2
… (continued)
  macNbaUwbChannelAllowListUpdate() method for adding/removing channels wrt. to known interference characteristics prior, or during NBA-MMS-UWB session lifetime
  Bitmask and TLV based encoded message formats for channel maps
  Per use-case optimized signaling (in-band/out-of-band)
Example application: coordination of internal 802.11 and 802.15.4 radio

## Slide 5: NB Channel Switching 1/5
Channel switching sequence for 4z block based access via AES-128-CTR [2], with pre-shared key/nonce among RAN participants
AES based switching achieves white noise a-like frequency diversity over set of macNbaUwbChannelAllowList[]
  reuses secure ranging dynamic STS generator implementation from 4z
  can be operated simulatuously with 4z block based “round hopping”
Basic PRNG based NB channel selection mode:
NbaUwbChannelSelected[idx] = macNbaUwbChannelAllowList[ AES128CTR(key,nonce,ctr=idx) % L]
where L=length(macNbaUwbChannelAllowList[]) and idx=ranging block index

## Slide 6: NB Channel Switching 2/5
Wifi 11bgn,ac,ax is OFDM block structured, adjacent NB channel interference is not i.i.d., purely random access is not optimal
AES output can be deterministically biased to optimize coexistence
Biased PRNG based NB channel selection mode:
  Example method 1: Update macNbaUwbChannelAllowList[] to temporarily exclude overlapping 802.11 channels (e.g. B=20 MHz) from previous NB channel selection

## Slide 7: NB Channel Switching 3/5
Example method 2
  Rotate NbaUwbChannelSelected[idx] by L/2=length(macNbaUwbChannelAllowList[])/2 when NbaUwbChannelSelected[idx-1] is overlapping the same 802.11 channel
  NB channel access candidates
    c1[idx] = macNbaUwbChannelAllowList[AES128CTR(key,nonce,ctr=idx) % L]
    c2[idx] = macNbaUwbChannelAllowList[(AES128CTR(key,nonce,ctr=idx) + L/2) % L]
  Guard bandwidth switching test (e.g., guard bandwidth B=20MHz)
    If |c1[idx] - NbaUwbChannelSelected[idx-1]| * 2.5 MHz < B
      NbaUwbChannelSelected[idx] = c1[idx]
    Else
      NbaUwbChannelSelected[idx] = c2[idx]

## Slide 8: NB Channel Switching 4/5
Example: macNbaUwbChannelAllowList[] = [1,…, 50]
c1 (selected)
c1 (not selected)
c2 (selected)

## Slide 9: NB Channel Switching 5/5
Resulting non-i.i.d. channel statistics for biased channel selection mode

## Slide 10: NB Access: CCA-EDT LBT 1/3
Required for UNII-5 by ETSI for narrowband access
Clear Channel Assessment (CCA) + Energy Detection Threshold (EDT)
  Low complexity CCA-ED to determine IDLE/BUSY status of NB medium
  NB medium BUSY when received signal strength measured over CCA-ED duration exceeds EDT. Otherwise, medium IDLE.
  EDT = -75 dBm/MHz, and >= 9us for Frame Based Equipment (FBE) [2]
  MMS structure fits FBE requirements with, e.g., FFP=1ms, COT<900us
NBA-MMS-UWB initiator/responder operate as independent FBE transmitters

## Slide 11: NB Access: CCA-EDT LBT 2/3
Ranging control phase NB access is required for UWB-MMS
  CCA-ED busy state of NB channel at either Poll, or Response NB packet leads to loss of synchronization for ranging phase
  UWB fragments will not be transmitted, if either NB Poll/Resp slots are CCA-ED busy
  No in-block retry of transmission in favor of reliable UWB scheduling & energy savings
  NBA-MMS-UWB will retry/commence in next ranging block

## Slide 12: NB Access: CCA-EDT LBT 3/3
Report Phase NB access succeeds Ranging Phase UWB-MMS
  NB Report packets convery data elements for ToF calculations
  Loss of NB Reports due to busy CCA-ED state prevents ToF calculation
  Deferred (out-of-band) retransmission of report packets possible without affecting current, or future scheduling

## Slide 13: Summary
We propose adding indexed presets of commonly used NB channels macNbaUwbChannelAllowList[], and macNbaUwbChannelAllowListUpdate() methods to enable efficient coordination of a mutually agreed set of NB channels for NBA-MMS-UWB between initiator and responder during the setup phase.
We propose AES-128-CTR as the baseline PRNG to obtain frequency diversity by switching NB channels between NBA-MMS-UWB blocks, and biasing of the output to obtain non-repeating NB channel access within neighboring Wi-Fi channels for better coexistence.
We propose CCA-ED LBT channel access as a low complexity, easy solution to comply with regularity requirements for UNII-5, and definition of a ruleset for skipping transmission of UWB fragments in case of CCA busy state during ranging control phase, to enable low complexity scheduling, and low energy consumption.

## Slide 14: References
[1] A. Krebs (Apple), F. Leong (NXP), et al., “Narrowband Channel Allocation for NBA-MMS-UWB”, 15-22-0339-00-004ab, July 2022.
[2] “6 GHz WAS/RLAN; Harmonised Standard for access to radio spectrum”, Draft ETSI EN 303 687 V1.0.0, April 2022.
[3] SP 800-38A Recommendation for Block Cipher Modes of Operation: Methods and Techniques”, National Institute of Standards and Technology (NIST), December 2001.