## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [ Coexistence with Wi-Fi by using Narrowband Mirroring Channel]
Date Submitted: [08 07, 2022]
Source: [Mingyu Lee, Taeyoung Ha, Youngwan So, Aniruddh Rao Kabbinale, Ankur Bansal, Clint Chaplin] Company [Samsung Electronics]
Address: [34, Seongchon-gil, Seocho-gu, Seoul, Korea]
E-Mail: [mg0218.lee@samsung.com]
Abstract: [Explain the necessity of collision avoidance between UWB and Wi-Fi, and Propose the considerations for the band of NB mirroring channel]
Purpose: [ ]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the authoring individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The authors(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
PAR Objective | Proposed Solution (how addressed)
Safeguards so that the high throughput data use cases will not cause significant disruption to low duty-cycle ranging use cases | 
Interference mitigation techniques to support higher density and higher traffic use cases | Reserve the UWB channel corresponding to the dedicated NB mirroring channel
Other coexistence improvement | Announce the use of UWB channel overlapped with Wi-Fi 6GHz channel
Backward compatibility with enhanced ranging capable devices (ERDEVs) | 
Improved link budget and/or reduced air-time | 
Additional channels and operating frequencies | Utilize one specific NB channel (among the NB channels) as NB Mirroring Channel
Improvements to accuracy / precision / reliability and interoperability for high-integrity ranging | 
Reduced complexity and power consumption | 
Hybrid operation with narrowband signaling to assist UWB | Exploit tightly coupled concurrent operation of NB to help UWB
Enhanced native discovery and connection setup mechanisms | Provide collision avoidance scheme based on the energy detection and the transmission of channel usage information
Sensing capabilities to support presence detection and environment mapping | 
Low-power low-latency streaming | 
Higher data-rate streaming allowing at least 50 Mbit/s of throughput | 
Support for peer-to-peer, peer-to-multi-peer, and station-to-infrastructure protocols | 
Infrastructure synchronization mechanisms | 

## Slide 3: Contents
Motivation
Overview of NB Mirroring Channel
Candidate Bands for NB Mirroring Channel
Conclusions

## Slide 4: Motivation
UWB Channels are less congested compared to other band because potential narrow-band jammers are in other far away channels [1]
However, 6GHz UWB channels are being overlapped other narrow-band, Wi-Fi 6GHz
8GHz UWB channel (CH 9) may not be secured in the future as in 6GHz channel (CH 5)
In addition, 4z devices are being deployed in the market and 4ab device may occupy the UWB channels more to increase the link budget or to introduce wake up feature
In summary, both the intra interference between UWB devices and inter interference between UWB devices and Wi-Fi 6GHz are increasing
UWB CH5
UWB CH9
7737.6
8236.8
5925
6425
7125
?
Wi-Fi
Wi-Fi (US/KOR/India)
6240
6739.2
Overlapped
Notes: [1] 15-22-0282-00-04ab-the-advantages-of-uwb-wakeup

## Slide 5: Motivation
Intra interference between UWB devices might be reduced by introducing 4ab feature, e.g., new preamble sequences
However, other parts which are not orthogonal at all (e.g., STS, PHR, payload) cannot be avoid the interference
The interference leads the failure of transmissions, the multiple trials of re-transmissions, and the service interruption if there is no method to avoid it
Since UWB devices utilize Pure Aloha and Wi-Fi devices use higher power than UWB devices, an efficient coexistence scheme by mitigating the interferences is required
As a method for reducing the interference between 4ab devices, NB Mirroring Channel has been proposed.
By using the operation in a NB Mirroring Channel, a 4ab device can reserve the corresponding UWB channel to avoid the interference from other 4ab device.
NB Mirroring Channel may be used for avoiding the interference from Wi-Fi devices by selecting a proper band with avoidance operations
Notes: [1] 15-22-0282-00-04ab-the-advantages-of-uwb-wakeup

## Slide 6: Overview of NB Mirroring Channel [2]
Controller transmits an advertisement packet at every active ranging block/round in NB mirroring channel dedicated to specific UWB channel
This packet is used for notifying the occupation status of the corresponding UWB channel to other devices
This packet includes the information about the usage of the corresponding UWB channel
  Start time of ranging rounds, Length of Ranging Block, Number of Ranging Rounds, Index of Active Round etc.
This packet may provide the information about the PHY parameters (e.g., BPRF/HRPF)
  Controller scans the mirroring channels before establishing UWB connection to find the available period and avoid collisions
  If the controller finds an idle period, it can send an advertisement packet for reserving the period in the corresponding UWB channel
Notations
A : Advertisement
Notes: [2] 15-22-0180-00-04ab_narrowband-uwb-coupling-mac-recap

## Slide 7: Candidate Bands for NB Mirroring Channel (1/4)
Candidate bands for NB are UNII-3 and UNII-5
Both bands have been used for Wi-Fi
However, the definition of prioritized NB channel in UNII-3 can avoid the inference because the band is not included as the band for Wi-Fi channels
For example, as in [3], 5730-5735MHz: 5MHz, 5725-5730MHz (part of Ch#144): 5MHz
The prioritized NB channel can avoid the interference from Wi-Fi in UNII-3
If NB Mirroring channel is introduced, the intra interference between NBs can be avoided
However, the interference from Wi-Fi to UWB in UNII-5 is not avoidable
Notes: [3] 15-22-0261-00-04ab-coexistence-discussion-on-nb-assisted-uwb

## Slide 8: Candidate Bands for NB Mirroring Channel (2/4)
Since UNII-3 and/or UNII-5 are overlapped with Wi-Fi bands
Hopping between NB channels can be considered
  4ab device can select the NB channels non-occupied by Wi-Fi and hop the NB channels to avoid the interference from Wi-Fi same as BLE in 2.4 GHz
  Interference from Wi-Fi in NB channels can be avoided
  Collisions between NB packets can be avoided
However, if multiple ranging setups in different NB channels at the same time happens, it may lead the collisions in UWB channel
The interference from Wi-Fi to UWB in UNII-5 is not avoidable
[UWB Ch5]
[NB 1]
[NB 2]
[NB 3]
Session Setup 1
Session Setup 2
Session Setup 3
Ranging Session 1
Ranging Session 2
Ranging Session 3
Overlapped
Session Setup 4
Session Setup 5
Overlapped
Ranging Session 4
Failure

## Slide 9: Candidate Bands for NB Mirroring Channel (3/4)
NB Mirroring Channel can be defined 1) in the band which is not used by Wi-Fi UNII-3 or UNII-5, 2) OR one of Wi-Fi channels in UNII-5
4ab devices transmit their advertisements in the NB Mirroring Channel
Wi-Fi AP/STA continuously monitor the NB Mirroring Channel for holding their transmission during the period specified in the advertisements in NB packet
In other words, NB Mirroring Channel is the channel for coexistence between 4ab and Wi-Fi 6GHz by letting Wi-Fi 6GHz devices avoid their transmission in the band overlapped with UWB CH5
Other NB channels for NB based data transmissions can be defined in the band for UWB CH5 which is overlapped with Wi-Fi channels
To avoid the intra/inter interference between NB-to-NB and NB-to-Wi-Fi, LBT can be introduced
Hopping is still can be used for NB data channels
Notes: [3] 15-22-0261-00-04ab-coexistence-discussion-on-nb-assisted-uwb

## Slide 10: Candidate Bands for NB Mirroring Channel (4/4)
Wi-Fi 6GHz need to use the NB Mirroring channel as (fast) scanning channel always
This concept may applied to the new NBs in other bands for the coexistence with UWB
UNII-5 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | UNII-6 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  | 1 |  | 5 |  | 9 |  | 13 |  | 17 |  | 21 |  | 25 |  | 29 |  | 33 |  | 37 |  | 41 |  | 45 |  | 49 |  | 53 |  | 57 |  |  | 61 |  |  |  | 65 |  |  |  | 69 |  |  |  | 73 |  |  |  | 77 |  |  |  | 81 |  |  |  | 85 |  |  |  | 89 |  |  |  | 93 |  |  |  | 97 |  |  |  | 101 |  |  |  | 105 |  |  |  | 109 |  |  |  | 113 |  |  | 
 |  |  |  | 3 |  |  |  | 11 |  |  |  | 19 |  |  |  | 27 |  |  |  | 35 |  |  |  | 43 |  |  |  | 51 |  |  |  | 59 |  |  |  |  |  |  | 67 |  |  |  |  |  |  |  | 75 |  |  |  |  |  |  |  | 83 |  |  |  |  |  |  |  | 91 |  |  |  |  |  |  |  | 99 |  |  |  |  |  |  |  | 107 |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  | 7 |  |  |  |  |  |  |  | 23 |  |  |  |  |  |  |  | 39 |  |  |  |  |  |  |  | 55 |  |  |  |  |  |  |  |  |  |  | 71 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 87 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 103 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  | 15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 47 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 79 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 111 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
UNII-7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | UNII-8 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
117 |  |  |  | 121 |  |  |  | 125 |  |  |  | 129 |  |  |  | 133 |  |  |  | 137 |  |  |  | 141 |  |  |  | 145 |  |  |  | 149 |  |  |  | 153 |  |  |  | 157 |  |  |  | 161 |  | 165 |  | 169 |  | 173 |  | 177 |  | 181 |  | 185 |  | 189 |  | 193 |  | 197 |  | 201 |  | 205 |  | 209 |  | 213 |  | 217 |  | 221 |  | 225 |  | 229 |  | 233 | 
 |  |  |  | 123 |  |  |  |  |  |  |  | 131 |  |  |  |  |  |  |  | 139 |  |  |  |  |  |  |  | 147 |  |  |  |  |  |  |  | 155 |  |  |  |  |  |  |  | 163 |  |  |  | 171 |  |  |  | 179 |  |  |  | 187 |  |  |  | 195 |  |  |  | 203 |  |  |  | 211 |  |  |  | 219 |  |  |  | 227 |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  | 135 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 151 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 167 |  |  |  |  |  |  |  | 183 |  |  |  |  |  |  |  | 199 |  |  |  |  |  |  |  | 215 |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  | 143 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 175 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 207 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
115
119
UWB
In addition to the prioritized channel in [3],
this band could be considered for NB Mirroring Channel
if the requirements in regulatory are satisfied
If the prioritized channel is not available ,
this band could be considered as NB Mirroring Channel
and NB Data Channels

## Slide 11: Conclusions
The interference from 4z/4ab and Wi-Fi 6GHz to UWB Ch5 is expected
No method to mitigate the interference even for UWB Ch9
For the coexistence between UWB devices and other (new) NBs, the candidate approach for NB Mirroring channel is proposed
The approach requires the specific operation of Wi-Fi AP/STA
  Especially, for AP, Scanning NB Mirroring Channel and avoiding RU allocation are required
  If there are multiple NB channels for presenting UWB channel status, Wi-Fi cannot support the collision avoidance operations
This concept could be considered when a new NB is introduced for UWB Ch9 in the future, if required
If NB Mirroring Channel is being used for UWB and Wi-Fi, intra/inter interference could be reduced eventually
Notes: [3] 15-22-0261-00-04ab-coexistence-discussion-on-nb-assisted-uwb

## Slide 12: References
[1] 15-22-0282-00-04ab The Advantages of UWB Wake Up
[2] 15-22-0180-00-04ab Recap of Narrowband / UWB Coupling MAC
[3] 15-22-0261-00-04ab Coexistence Discussion on NB Assisted UWB

## Slide 13: Thank You