## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Inter Frame Spacing for HRP UWB PHY]
Date Submitted: [11 July, 2022]
Source: [Kangjin Yoon, Chunyu Hu, Carlos Aldana, Claudio Da Silva] Company [Meta Platforms, Inc.]
Address [1 Hacker Way, Menlo Park, CA 94025]
E-Mail:[{kyoon, chunyuhu, caldana, claudiodasilva}@fb.com]
Re: [Input to TG4ab]
Abstract: [If IFS values should be updated, new PHY features and immediate Ack should be considered.]
Purpose: [Start a discussion on IFS values for 4ab.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
PAR Objective | Proposed Solution (how addressed)
Safeguards so that the high throughput data use cases will not cause significant disruption to low duty-cycle ranging use cases | 
Interference mitigation techniques to support higher density and higher traffic use cases | 
Other coexistence improvement | 
Backward compatibility with enhanced ranging capable devices (ERDEVs) | 
Improved link budget and/or reduced air-time | 
Additional channels and operating frequencies | 
Improvements to accuracy / precision / reliability and interoperability for high-integrity ranging | 
Reduced complexity and power consumption | 
Hybrid operation with narrowband signaling to assist UWB | 
Enhanced native discovery and connection setup mechanisms | 
Sensing capabilities to support presence detection and environment mapping | 
Low-power low-latency streaming | IFS values should be small enough to keep low-latency
Higher data-rate streaming allowing at least 50 Mbit/s of throughput | AIFS value should be small enough to have immediate Ack for reliable data communication
Support for peer-to-peer, peer-to-multi-peer, and station-to-infrastructure protocols | 
Infrastructure synchronization mechanisms | 

## Slide 3: Previous Contributions Related To Ack Inter Frame Spacing (AIFS)
DCN 173r0 (Mar 2022) “Ack for data communication”
  Discussed the usage of immediate ACK for data comm
  Summarized legacy AIFS values defined in 15.4-2020
DCN 296r1 (May 2022) “A Higher Data Rate Proposal For UWB”
  Suggested investigation on AIFS, and expected AIFS >= 64 usec

## Slide 4: Recap: IFS in 15.4 & 15.4z
AIFS: Minimum separation between data frame and ack frame
SIFS: Minimum separation which shall come after short data frame (up to 18 Byte MPDU)
LIFS: Minimum separation which shall come after long data frame (over 18 B MPDU)
AIFS = SIFS = 12 preamble symbols (Ref: 15.4-2020, pp. 61, 454)
LIFS = 40 preamble symbols (Ref: 15.4-2020, p. 454)
 | Preamble symbol duration (ns) | AIFS = SIFS (us) | LIFS (us)
HPRF | 729.17 | 8.75 | 29.17
BPRF | 993.6 | 11.92 | 39.74
 | 1017.6 | 12.21 | 40.70
 | 3974.4 | 47.70 | 158.98

## Slide 5: Thoughts on IFS Values in 15.4 & 15.4z
Numbers looks reasonable
  TX-RX turnaround time of products on market is around 10 us [1]
  5 GHz 802.11 has 16 us for SIFS
  BLE defines 150 us IFS for data-ack spacing
Discussion:
  Need to update IFS values to realistic yet performance-efficient values
  Explore options to settle on IFS values to progress
  Think forward:
    Expect the implementation will be improved and smaller values will be possible
[1] DW1000 datasheet, link: https://www.decawave.com/sites/default/files/resources/dw1000-datasheet-v2.09.pdf

## Slide 6
Need to be big enough to support new PHY features
  e.g., advanced coding (LDPC) may increase decoding time
Need to be small to reduce overhead: Impact can be significant
  Enhance spectrum efficiency
  Reduce idle time to save power consumption
Need to be small enough to complete a data/ack frame exchange in a slot for typical usage
  Operating PHY rate/coding, PSDU size, and slot duration, etc. need to be taken into account
Choosing Right Values for IFS
AIFS
Data
ACK
Ranging Slot
LIFS

## Slide 7: Options
Option 1: Utilize legacy IFS values in 15.4-2020
  Best performance and use baseline text
Option 2: Agree on a new IFS value
  A few choices to throw on the table, for HPRF SIFS (=AIFS), e.g.,
    +/- 16 us (a little more or less of 16 usec)
    +/- 32 us
    +/- 64 us
Option 3: Provide a {rate, code, anything else?} specific AIFS values:
  Look-up table determined value
  E.g., two different values for LDPC ON/OFF
Option 4 (least preferred): Set up IFS value per session configuration (based on handshake?)
  Devices can negotiate IFS values when they join the session
  Pros: Provide flexibility
  Cons: Unnecessary complexity, and more chances for interoperability issue

## Slide 8: Summary
We need to investigate whether legacy IFS values are realistic to support 4z and 4ab features
If existing IFS values do not suit 4ab design, we need resolution with alternative values with solid rationale for the proposed values (otherwise legacy values will stay and be used)
New IFS values should be small enough to support immediate ACK within a slot duration in typical configuration

## Slide 9: Straw Poll
Which option do you prefer for the choice of AIFS:
  Option 1: Use legacy IFS values
  Option 2: Find new fixed IFS values
  Option 3: Have different IFS values for different PHY usage
  Option 4: Make IFS values negotiable
  Abstain

## Slide 10: Thank You