## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [UWB Interference Considerations]
Date Submitted: [ July, 11, 2022]
Source: [Shang-Te Yang] Company [Apple Inc.]
Re: [Input to the Working Group]
Abstract: [An Example of interference analysis and considerations]
Purpose: []
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
PAR Objective | Proposed Solution (how addressed)
Safeguards so that the high throughput data use cases will not cause significant disruption to low duty-cycle ranging use cases | Revisit assumptions in the design of block-based ranging
Interference mitigation techniques to support higher density and higher traffic use cases | Using two examples to show various design considerations.
Other coexistence improvement | 
Backward compatibility with enhanced ranging capable devices (ERDEVs) | 
Improved link budget and/or reduced air-time | 
Additional channels and operating frequencies | 
Improvements to accuracy / precision / reliability and interoperability for high-integrity ranging | 
Reduced complexity and power consumption | 
Hybrid operation with narrowband signaling to assist UWB | 
Enhanced native discovery and connection setup mechanisms | 
Sensing capabilities to support presence detection and environment mapping | 
Low-power low-latency streaming | 
Higher data-rate streaming allowing at least 50 Mbit/s of throughput | 
Support for peer-to-peer, peer-to-multi-peer, and station-to-infrastructure protocols | 
Infrastructure synchronization mechanisms | 

## Slide 3: Noise vs. Interference Limiting
We need to clearly define the scenario under consideration.
Noise limiting scenario:
  Signal-of-Interest is nominally below thermal noise.
  All interference UWB signal are below thermal noise.
  The main concern is preamble false locking.
Interference limiting scenario:
  Interference signal either is very close physically and/or using high instantaneous power per pulse (gating gain and/or low PRF).
  In general, shorter packet is better, and we don’t lose much link budget! [1]

## Slide 4: UWB Use Case Considerations
Ranging, sensing, and data streaming use cases seems all gravitate toward block-based operation.
  The deterministic nature of block-based MAC keeps implementation simple.
  No conditional re-transmission in 4z block-based MAC.
  Ranging slot size is determined by processing latency, instead of packet duration.
Two use case examples:
  RAN A: Ten 250us BPRF UWB packets every 288ms. Combined packet duty cycle 0.87%
  RAN B: Unicast (streaming) 127 Byte @ HPRF #3 (~63us, 31.2Mbps) every 5ms = 1.24%
Simplified analysis:
  Assuming both are using 5ms slot size, and any partial collision causes total packet lost.
  Assuming uniform random start time, the chance of collision is (250us + 63us)/5ms = 6.3%.
    RAN A: 6.3% chance all packet are lost, and 93.8% chance zero packet is lost. Restart is the only way out.
    RAN B: 6.3% * (10*5/288) = 1.08% chance all packets are lost for 50ms. Other 99% is clean.
    Clear failure signature, which may be used to trigger restart.

## Slide 5: How about different slot size?
Same two use cases but using different slot sizes.
  RAN A: Ten 250us BPRF packets every 288ms using 3ms slot.
  RAN B: Unicast (streaming) 127 Byte @ HPRF #3 (~63us, 31.2Mbps) every 5ms.
A simplified timing diagram (1ms scale) when both RANs are active.
  RAN A and RAN B are uncoordinated, and the rows show different RAN B starting time.
  RAN A: 32% chance lose 2 of 10 packets for 30ms, 69% no issue.
  RAN B: (32% * 10.4%) block could collide and lose 2 of 6 packets for 30ms, 96.7% no issue.
  Both RAN may choose to tolerate the lost or restart, but there is no clear failure signature.
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27
A |  |  | A |  |  | A |  |  | A |  |  | A |  |  | A |  |  | A |  |  | A |  |  | A |  |  | A
B |  |  |  |  | B |  |  |  |  | B |  |  |  |  | B |  |  |  |  | B |  |  |  |  | B |  | 
 | B |  |  |  |  | B |  |  |  |  | B |  |  |  |  | B |  |  |  |  | B |  |  |  |  | B | 
 |  | B |  |  |  |  | B |  |  |  |  | B |  |  |  |  | B |  |  |  |  | B |  |  |  |  | B
 |  |  | B |  |  |  |  | B |  |  |  |  | B |  |  |  |  | B |  |  |  |  | B |  |  |  | 
 |  |  |  | B |  |  |  |  | B |  |  |  |  | B |  |  |  |  | B |  |  |  |  | B |  |  | 

## Slide 6: The Reality
Existing use cases using 4z:
  Not all use cases have the same slot size.
  Packets with various modulation and duration could be on the air.
Clock drift and block duration:
  100ppm accurate MAC = 1/ 58/ 2000 us uncertainty with 5ms/ 288ms/ 10s cadence.
  For long block application, the uncertainty is dominated by ppm.
  Bigger the Rx uncertainty window, potentially more susceptible to preamble false locking.
We need clear reliability requirement per use case.
  Ranging is mostly a low reliability use case, but it cannot be wiped out.
  How reliable does streaming use case need to be?
  How to define reliability for sensing?

## Slide 7: Summary
There is a very good reason why we saw so many preamble proposals.
  Avoiding preamble false locking for noise limiting scenario is very important.
Recommend framework for interference study:
  Identify use case slot, block, and reliability requirement (PERs and durations).
  Sensing using 4z packet format can be treated in the same way. However, longer sensing waveform with low PRF probably needs to be treated differently.
Tradeoff between performance and complexity
  Slot level hopping or coprime slot choice mitigate the worst case by making the median ones worse than without them.
  Coordination (centralized or distributed) will sustain better at light to moderate load but need complex mechanisms to catch worst scenarios. All these operations consume resources.
  4ab ranging most likely follow the 4z block-based design, without specific mitigation.
  Mitigation implemented in highly reliable use cases will also help less reliable use cases.

## Slide 8: References
[1] K. Akhavan, “IR-UWB link budget analysis and comparison with NB signaling,” May 2022, doc.: <15-22-0394-02>