## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: NB-assisted UWB channel access follow-up
Date Submitted: July 11, 2022
Source: Huan-Bang Li, Takeshi Matsumura (NICT, Japan), Mingyu Lee (Samsung).
Address: 3-4 Hikarino-oka, Yokosuka-shi, Kanagawa, 239-0847 Japan
E-Mail: {lee, matsumura}@nict.go.jp, mg0218.lee@samsung.com
Abstract: Clarify some concerns on NB-assisted UWB channel access.
Purpose: To improve coexistence among UWB systems.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the authoring individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The authors(s) reserve(s) the right to add, amend or withdraw material contained herein.

## Slide 2
PAR Objective | Proposed Solution (how addressed)
Safeguards so that the high throughput data use cases will not cause significant disruption to low duty-cycle ranging use cases | Effective and efficient CCA reduce disruption between UWB devices
Interference mitigation techniques to support higher density and higher traffic use cases | Use NB radio to facilitate CCA so as to improve coexistence.
Other coexistence improvement | Use NB radio to improve coexistence among UWB devices.
Backward compatibility with enhanced ranging capable devices (ERDEVs) | 
Improved link budget and/or reduced air-time | 
Additional channels and operating frequencies | 
Improvements to accuracy / precision / reliability and interoperability for high-integrity ranging | 
Reduced complexity and power consumption | 
Hybrid operation with narrowband signaling to assist UWB | Exploiting pilot NB PHY and concurrent operation with UWB to assist UWB channel access
Enhanced native discovery and connection setup mechanisms | 
Sensing capabilities to support presence detection and environment mapping | 
Low-power low-latency streaming | 
Higher data-rate streaming allowing at least 50 Mbit/s of throughput | 
Support for peer-to-peer, peer-to-multi-peer, and station-to-infrastructure protocols | 
Infrastructure synchronization mechanisms | 

## Slide 3: Contents
Motivations
Example of operation
Pros and cons
Address some concerns

## Slide 4: Motivations
In TG 15.4ab, various applications and use cases are proposed and they can be classified into several categories such as,
(See 15-22-0315-01-04ab and 15-22-0316-01-04ab)
- TWR (TOA, AOA)
- Data Communication Enhancement.
- Sensing.
Six CCA modes are specified in IEEE 802.15.4-2020. However, coexistence between different UWB schemes are challenging for some reasons, e.g.,
- CCA of sensing energy or carrier may be verry difficult because of the
inherent extremely low PSD and noise-like property of UWB.
- CCA of sensing preamble of UWB frames may require a UWB device to
sense multiple preambles if different UWB schemes exist in surroundings,
that greatly increase complexity or sensing time.

## Slide 5: Motivations - continue
UWB-only medium access methods
- Coordinated TDMA (e.g. DL-TDoA and multi-static sensing )
- Modifying current CCA modes to facilitate UWB.
- Taking advantage of preamble codes.
- PRF domain multiple access
Each method has pros and cons, but none of them solves difficulties of CCA
addressed in the previous slide.
As alternative, NB radio assisted CCA can solve the problem(15-22-0275-00-04ab)
- CCA is performed at NB channel where UWB occupancy information is
broadcasted using NB radio.

## Slide 6: Example Illustration of Operation
Transmission of NB radio and UWB are time deterministic.
(Transmission can start together or with pre-determined time interval )

## Slide 7: Pros and Cons
NB CCA may only sense energy or sense carriers by properly associating UWB task with NB-PHY features (15-22-0275-00-04ab).
  Sensing NB energy or carriers is much easier and with much higher probability of success than that for UWB.
  Even multiple UWB schemes operate in surroundings, the same NB CCA mechanism can be commonly applied to avoid interference.
  Have better match with NB assisted multi-millisecond UWB by associating UWB related information with NB radio.
Need a NB radio.
  Off-the-shelf chips/modules are available.
  Simple to implement with legacy NB CCA

## Slide 8: When to Enable NB assisted CCA Mode
The NB radio assisted CCA is proposed as an optional mode in addition to the six CCA modes specified in IEEE 802.15.4-2020.
  A compliant device can switch-off this mode if it is experiencing a good UWB channel, e.g., the device achieves high success rate when conducting UWB tasks. (the effect of interference is negligible)
  A compliant device should switch-on this mode if it is experiencing a crowded UWB channel, e.g., the device achieves low success rate when conducting UWB tasks. (the effect of interference is non-negligible)
*In principle, this mode is useful for dense deployment environment.
Reality of such environment may increase dynamically as more and
more portable devices are implementing UWB.

## Slide 9: Some Concerns
How long does a NB radio need to perform CCA for contending channel?
  The default CCA duration should cover the period from a NB radio starting transmission until a coupled UWB completing UWB task.
  A NB radio can terminate CCA whenever it already successfully acquired necessary sensing information.
Does NB unnecessarily shut up devices in a very big range and reduce the utilization of the UWB channel?
  To avoid such phenomena, proper NB radio CCA gain compared to UWB needs to be designed by either reducing NB TX power or determining suitable CCA threshold.
  To avoid shut up by other systems operating in the same NB channel, the NB radio needs to hold own features to be distinguished from others.
Does NB increase power consumption?
  On one hand, Yes. On another hand it may reduce UWB re-transmission so as to decrease power consumption.

## Slide 10: Some Concerns (continue)
How to select and use narrow bands?
  It is desired to use globally available frequency bands.
  Coexistence between NB and other existed radios are necessary.
Do other existed radios stop UWB?
  To avoid UWB being stopped by other radios, NB should be of distinct features to differentiate from other radios.
  To avoid NB being stopped by other radios, NB needs to be operated with condition that are of less regulatory restrictions.
  Otherwise, coexistence measures need to be taken (see 22-0261-00)