## Slide 1
Project: P802.15 Working Group for Wireless Specialty Networks
Submission Title: Joint session 6ma, 4ab, 14
Date Submitted: July 12th, 2022
Source: Marco Hernandez, Ryuji Kohno, Takumi Kobayashi, Minsoo Kim
Company: YRP-AIA, YNU, Japan
Address: 3-4 Hikarino-oka, Yokosuka, 239-0847, Japan
Voice: +81 46-847-5439 Fax: +81 46-847-5431 E-Mail:
Re: In response to call for technical contributions
Abstract:
Purpose: In response to the call for technical contributions
Notice: This document has been prepared to assist P802.15.6ma. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.6ma.

## Slide 2: Recap
PHY Spec. Parameter | 15.6a requirement | 15.4 (z and ab) capability | Comments
Throughput & Data Rate | Throughput of at least 40 Mb/s, operating at a maximum data rate of 50 Mb/s* (500 MHz channel) under a Packet Success Ratio of 99% measured at the MAC-SAP. | The new data rates proposed in 15.4ab of 62.4 Mb/s and 124.8 Mb/s look promising | Maybe Covered w/802.15.4 UWB
Range | Transmission range of at least 3m for backward compatibility (from use cases doc.). | Up to 100m | Covered w/802.15.4 UWB
Reliability & Interference Immunity | Transmission reliability under congested communication environments including interference from other 15.6 BANs (intra-interference) and other wireless systems (inter-interference): PDR was measured at the MAC-SAP. | Many capabilities either existing or being developed | Needs further discussion w.r.t. particular .6a needs
Latency | End-to-end latency in the interval 250 msec for x QOS 1 sec for y QOS QoS def. is being worked on Critical use cases include end-to-end latency bounded to 100 msec. | Low latency is one of the areas being worked on in .4ab | 4 msec for critical .6a use cases is under study.
Ranging Data Rate | Ranging with a data rate of 500 kb/s. | Supported with sub-centimeter accuracy | 

## Slide 3: Towards harmonization
The current UWB specifications in the15.4 Std and amendments seem OK for the 6ma PHY.
  6ma looks to increase the link reliability via PHY and MAC mechanisms, support a mode with a high data rate communication, and all modes in a dense environment.
  Ranging is desirable, but not a priority.
Hence, 6ma is checking reliability performance. Maybe some tweaks will be necessary.
In general, 4ab proposals look very promising. However, we need to have certainty about which proposals will make it to the Std.

## Slide 4: Collaboration
Something we can collaborate on at the moment is on checking mutual coexistence while supporting high dependability and a mode for high data rate.
  Potential problems, how to solve them, etc.

## Slide 5: Comments, suggestions?