## Slide 1
doc.: IEEE 802.15-22-0389-00-06ma
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs) Submission Title: [Overview of IG-DEP, SG6a, TG6a, and TG15.6ma for Revision of IEEE802.15.6-2012 Wireless BAN with Enhanced Dependability]
Date Submitted: [12 July 2022]
Source: [Ryuji Kohno, Takumi Kobayashi] [1;Yokohama National University(YNU), 2;YRP International Alliance Instiitute(YRP-IAI)]
Address [1; 79-5 Tokiwadai, Hodogaya-ku, Yokohama, Japan 240-8501
2; YRP1 Blg., 3-4 HikarinoOka, Yokosuka-City, Kanagawa, Japan 239-0847 ] Voice:[1; +81-90-5408-0611], FAX: [+81-45-383-5528],
Email:[1: kohno@ynu.ac.jp, kobayashi-takumi-ch@ynu.ac.jp, 2:kohno@yrp-iai.jp, kobayashi-takumi@yrp- iai.jp]
Abstract: [This document summarizes IG-DEP, SG15.6a , TG6a, and TG6ma activity for revision amendment of IEEE802.15.6 - 2012 Medical Body Area Network(BAN) corresponding to increasing for enhanced dependability in wireless sensing and controlling human and car bodies for medical healthcare and automotive uses. After quick overview of IEEE802.15.6 -2012, necessity of the amendment is described in such critical use cases that various types of interference such as intra BAN interference in multiple overlaid BANs, interference among BAN and other PANs in some overlaid frequency band etc. Extension of BAN from human body for medical healthcare to car body for automotive uses and their combination are discussed as a common standard.]
Purpose: [information]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
Slide 1
Ryuji Kohno, Takumi Kobayashi(YNU/YRP-IAI)

## Slide 2
doc.: IEEE 802.15-22-0389-00-06ma
Overview of IG-DEP, SG6a, TG6a and TG15.6ma for Revision of IEEE 802.15.6-2012 Wireless BAN with Enhanced Dependability
Slide 2
Ryuji Kohno, Takumi Kobayashi(YNU/YRP-IAI)
Ryuji Kohno, Takumi Kobayashi Yokohama National University, Japan(YNU)
YRP International Alliance Institute, Japan(YRP-IAI)
July 2022

## Slide 3: Agenda
Submission
Demand for WBAN for Emergent Medical Healthcare Use and Huge Market of Automotive Use
Short Review of WBAN Standard IEEE802.15.6-2012
Necessity and Uniqueness for Amendment of BAN with Enhanced Dependability
Available Technologies in PHY and MAC Layers for the Focused Amendment of std 15.6 BAN with Enhanced Dependability
Technical Requirement for the Amendment of Std. 15.6 to Enhance Dependability
3
Ryuji Kohno, Takumi Kobayashi(YNU/YRP-IAI)
July 2022

## Slide 4
1. Demand for WBAN for Emergent Medical Healthcare Use and Huge Market of Automotive Use
Slide 4
doc.: IEEE 802.15-21-0389-00-06ma
July 2022

## Slide 5
1.1 Demand of BAN for Medical Uses
C. Approach:
R&D of Enable Technologies for Pandemic and Daily QoL
Promote International Standard of Wireless Body Network（BAN) and Integrated Platform of BAN/5G/AI for Global Marketing
Regulatory Compliance of Medical Devices & Services to Ensure Safety, Reliability, Security, i.e. Dependability by Regulatory Science
Emergent Problems over the world：
  1-4% of total population in a world may be suffered by COVID-19, that is a global pandemic.
  Clinic are overloaded and many business are damaged seriously.
COVID-19 Pandemic Population Ageing
Slide 5
Challenging but Feasible Solutions:
  Provide Remote Vital Sensing and Therapy Using ICT and AI
 Prevent Epidemic and Maintain Safe and Efficient Diagnosis
Promote Global Business of Medical ICT and Data Science
doc.: IEEE 802.15-22-0389-00-06ma
July 2022

## Slide 6: 1.2 Medical Inspection and Treatment by BAN
6
information
ervices
r node Electronic medical card way
omatic recording medical treatments
and nursing
• Patients’ condition monitoring
•Warning information • Medical
•Medical information
Senso
⇒sensor Recognition Recognition Gate
nodes Details Medical data Aut
of
Nursing Treatment
Stock information
Medication
Condition of patients
Medical Healthcare Using BAN can perform remote real-time medical diagnosis and therapy
To prevent pandemic against COVID-19 and medical care incident etc. in daily life.
> Remote sensing vital sign and monitoring symptoms
> Evidence based medicine for clinical and nursing actions
•To support safe and efficient medical care for clinical staffs and patients etc.
> Online diagnosis, PCR and other inspection
> Protect clinical staffs and care givers with network
Server on Medical S
WBAN can apply for
preventing pandemic and supporting daily care by remote sensing and therapy in digital healthcare.
Symptoms of COVID-19
Slide 6
July 2022

## Slide 7: 1.3 Wireless BAN: Body Area Network
Submission
7
Implant BAN
Tele-control of Medical Equipment and Devices
Wearable BAN
Tele-metering or sensing
vital signs with various sensors
ECG EEG SPO2
Blood Pressure Heartbeat
Body temperature Glocuse level
Medical images(X-ray, MRI) and video
etc.
Pace Maker with ICD
Novel Concept Intelligent Network of Vital
Sensors, eHR, Medical Robots etc.
Wireless Capsule Endoscope
July 2022

## Slide 8: 1.4 BAN- Use Cases for Remote Medical Services
Data mining
BAN
切替
Satellite Networks
Medical Data Server for Data Mining with Machine Learning
Medical Center and General Hospitals
8
BAN
Moble
Station
Medical support
for developing countries
BAN
VSAT
BAN
Satellite Link
Big Data
Internet
Cellular Network
Network Cloud
Slide 8
doc.: IEEE 802.15-22-0389-00-06ma

## Slide 9: 1.5 BAN-base Universal Platform with Network Cloud, Data Mining Server for Medical Healthcare
Node
Node
Elderly people
Therapist, Nurses, Care givers
Data storage server; DBMS
Hospital, Rehabilitation center, or Clinicians
Gateway
Network cloud (5G. 6G)
Body Area Network (BAN)
Coordinator
Data mining or Analysis
like Watson
Node
physical assistant and surgery robots
lide 9
doc.: IEEE 802.15-22-0389-06ma

## Slide 10: 1.6 Universal Platform Based on BAN, Cloud Network, and AI Data Server for General Social Infrastructure beyond Medical Services
Submission
10
Ryuji Kohno, Takumi Kobayashi(YNU/YRP-IAI)
July 2022

## Slide 11
1.7 Extension of Use Cases of BAN beyond Medical Healthcare
On Chip Antenna and Wireless Network in chio
MMIC
(Flip Chip)
Multi-layer BCB
Silicon Base
Wearable BAN
Tele-metering vital data
EEG. ECG,
Blad Pressure Temperatute MRI images
Etc.
Pacemaker with IAD
Dependable Network among vital sensors, actuators, robots
Capsule Endoscope
Implant BAN
Tele-controlling implant devices
UWB can solve
such a problem
that radio interferes
a human body and
medical equipments
Collision Avoidance and safe driving by inter-vehicle networks
A車
Collision Avoidance
Using inter-vehicle and
roadside networks
Road to car networks
Inter-vehicle networks
Inter-module wireless Networks
Dependable Wireless Sensing & Controlling for Manufacturing (CIM)
Silicon Bsee
Micor Machine Fablication
Dependable Wireless System Clock in Micro Circuit & Network in Devices
Dependable Wireless Networks for Transportation
Factory Automation (FA)
Car Navigation & Collision Avoidance Radar
Car LAN & Wireless Harness
Dependable BAN for Medical Healthcare
Submission Slide 11
Ryuji Kohno, Takumi Kobayashi(YNU/YRP-IAI)
doc.: IEEE 802.15-22-0389-00-06ma
July 2022

## Slide 12
Submission
Wireless channeWl ith
controller Pump
Clinician
Patient
sensor
Insulin Pump
Blood-sugar level (Glucose) HbA1c
Wireless Feedback Sensing and Controlling Loop for Diabetes Patients
K
Wireless channel
Bd 1/S
Ad
u[k]
r[k]
x[k]
x[k]
y[k]
^
u^ [k]
+
+
+
-
Controller
Human Model of Glucose vs Insulin
Automatic Remote Sensing Glucose and Controlling Insulin Pump for Diabetes Patients Using Wireless BAN
Feedback Delay Loop Model with Motion Equation
doc.: IEEE 802.15-22-0389-00-06ma
July 2022

## Slide 13
Submission
1.8 Demand of BAN for Automotive Uses
C. Approach:
R&D of Enable Technologies for Smart Vehicle and City
Promote International Standard of Wireless Body Network（BAN) and Integrated Platform of BAN/5G/AI for Global Marketing for both Medical and Automotive uses
Regulatory Compliance of Devices & Services to Ensure Safety, Reliability, Security,
i.e. Dependability by Regulatory Science
Increasing Demands in a world：
  New business promotion by applying wireless ICT to vehicle by huge alliance between automotive and telecom industries such as smart key, wireless harness
  Autonomous car driving and safety controlling of elderly drivers by ICT and data science
Smart Vehiles EV and HV
Challenging but Feasible Solutions:
  Provide Remote Sensing and Controlling Using ICT and AI
 Prevent Traffic Accidents , Jam and Co2 Emission
Promote a New Global Business of Automotive , ICT, and Electronics
doc.: IEEE 802.15-22-0389-00-06ma
July 2022

## Slide 14
Submission
controller
Wireless channel
Axel/Brake
Driver or AI
Own Car
Radar
For Autonomous Driving
For Collision Avoidance and Inter- Vehicle Communication
Wireless Feedback Sensing and Controlling Loop for Autonomous Driving
K
Wireless channel
Bd 1/S
Ad
u[k]
r[k]
x[k]
x[k]
y[k]
^
u^ [k]
+
+
+
-
Controller
Car Axel/Brake Model and Radar System
1.9 Use of BAN for Autonomous Car Driving
Feedback Delay Loop Model with Motion Equation
Car Running Ahead
doc.: IEEE 802.15-22-0389-00-06ma
July 2022

## Slide 15: 1.10 Remote Localization and Rescue of Missing Victims Using Wireless Dependable BAN of Things/M2M
Submission
controller
Wireless channel
Navigation
Rescue Team
UAVs/Drones
For Remote Controlling UAVs
Localization
By Using GNSS and Localization
K
Wireless channel
Bd 1/S
Ad
u[k]
r[k]
x[k]
x[k]
y[k]
^
u^ [k]
+
+
+
-
Controller
of UAVs/Drones
Wireless Feedback Sensing and Controlling Loop for Rescue of Victims
UAVs/Drones Model and Localizing
System
Feedback Delay Loop Model with Motion Equation
Missing Victims
July 2022

## Slide 16
Submission
Ryuji Kohno, Takumi Kobayashi(YNU/YRP-IAI)
16
1.11 Body Area Network(BAN) of Vehicle Body
5
1
2
3
4
6
Engine diagnostic sensor and controller
Air pressure sensor, wheel health sensor and controller
Transmission monitoring sensor and controller
Cabin environment sensor (temperature, brightness, humidity etc.)
Sheet sensor, health care sensors for driver
Sheet sensor, health care sensors for passenger
Use case of Vehicle Body Area Network(VBAN) for Cabin Room
https://media.istockphoto.com/photos/transparent-car-design-wire-model3d-illustration-my-own-car- design-picture-id594040008?k=6&m=594040008&s=612x612&w=0&h=XE8LiBjpM51aB4pH2CFt6- MT6IvALRPnlxPcac0RXhg=
Motivation to extend human BAN(HBAN) to VBAN is to promote much dependable services by interaction between HBAN and VBAN.
Use case of Vehicle Body Area Network(VBAN) for Engine Room
doc.: IEEE 802.15-21-0022-0389-00-06ma
July 2022

## Slide 17
1.12 Use case in Factory Manufacturing Line; Detection of Twist and Cut of Cables
In order to improve QoS of controlling robots in factory lines, real-time sensing and controlling with permissible feedback control loop must be important requirement
Prediction and Real-time Detection of twist and cut in signal and power cables
doc.: IEEE 802.15-22-0389-00-06ma
July 2022

## Slide 18
2. Short Review of WBAN Standard IEEE802.15.6-2012
doc.: IEEE 802.15-22-0389-00-06ma

## Slide 19: 2.1 Standard of Medical Wireless Body Area Network(BAN);IEEE802.15.6
Submission
802.15.4b
Revision & Modification of 15.4 MAC
802.15.3
PHY for High Rate WPAN
IEEE802.11
Wireless LAN
802.15.2
Coexistence between WPAN and WLAN
802.15.5
WPAN
Mesh Network
IEEE802.15
Wireless PAN
802.15.1
Bluetooth
802.15.4
PHY for Low Rate WPAN
802.15.3a
Alternative PHY of 15.3
802.15.3c
PHY in Millimeter wave band
802.15.3b
Maintenance of 15.3
802.15.4a
Low rate UWB PAN Alternative PHY of 15.4
IEEE802
IEEE802.16
Wireless MAN
802.15.4c
Chinese WPAN
802.15.4d
Japanese WPAN
2007.3
Standard Completed
802.15.6
Wireless Medical BAN
2012.2 Standard was Completed
19
July 2022

## Slide 20: 2.2 Top View of IEEE Std 802.15.6
UWB: Ultra-wideband
HBC: Human body communication
IEEE 802.15.6
Narrow band PHY on-body & in-body
UWB PHY
on-body
Common MAC
（for all PHY）
Modulation: GMSK
•& DPSK
TX range: ~3m
Data rate: ~ some Mbps
Modulation:IR-UWB & FM-UWB
TX range: ~3m
Bands: MICS,WMTS,ISM • Band: UWB band
Data rate: ~10Mbps
Beacon-base- TDMA
Group Superframe
Priority support
Non-beacon mode
HBC PHY
on-body
Frequency Selective
• 10-50MHz
125kbps- 2Mbps
July 2022

## Slide 21
2.3 User Priority Mapping
Priority level | Traffic designation | Data type
7 | Emergency or medical event report | Data
6 | High priority medical data or network control | Data or management
5 | Medical data or network control | Data or management
4 | Voice | Data
3 | Video | Data
2 | Excellent effort | Data
1 | Best effort | Data
0 | Background | Data
July 2022
doc.: IEEE 802.15-22-0389-00-06ma

## Slide 22: 2.4 Three Channel Access Modes
Channel access mode | Time reference-based (superframe structure) | Beacon | Notes
I | Yes | Yes | Coordinator sends beacon in each superframe except for inactive superframes.
II | Yes | No | Coordinator establishes time reference but doesn’t send beacon.
III | No | No | There is not time reference.
July 2022

## Slide 23: 2.5 Time-referenced Superframe w/ Beacon
Clock and position of each access phase
May obtain contended allocation for highest priority
B
B2
EAP1
RAP1
MAP
EAP2 RAP2
MAP
CAP
One superframe
EAP: exclusive access phase RAP: random access phase MAP: managed access phase CAP: contention access phase
July 2022

## Slide 24: 2.6 Worldwide UWB Regulations in 2012
doc.: IEEE 802.15-22-0389-00-06ma

## Slide 25: 2.7 Radio Outdoor Uses in the Frequency Band 7.25-9.00GHz (January 2021)
RAS
Public uses (Fixed & Mobile Satellites
Radio Amatur e
Planed Band for Fixed Satellites
Public uses (Fixed & Mobile Satellites
UWB High Band Systems
Space Research
Public/Civi l Uses
Fixed Broadcast
Public/Civil Uses Fixed Broadcast
Fixed & Mobile Broadca st
EESS
Airplane s
(PAR)
Various Radars
Geolocation VLBI
Various Radars
RAS
Boardcast
Expected Permitted Outdoor Band in Jan. 2021
Red lines indicate channels defined by IEEE802.15.4a.
Although Ch 9 in 7.587-8.4GHz Blue line was allowed for outdoor use in May 2019, MIC has started investigation to allow wider band 7.25-9.00 GHz Green line wand it is expected to allow it for outdoor use in January 2021
Permitted Outdoor Band in May 2019
July 2022

## Slide 26: 2.8 Summary of IEEE802.15.6-2012 A standard, IEEE Std 802.15.6TM was completed and published in Feb. 2012. In which, specifications of three PHY and common MAC are defined to support various medical and non-medical consumer applications.
Commercial products of BAN have been sold as an enable technology supporting personal healthcare as a consumer electronics but not much approved for medical equipment.
In PHY, ultra-wide band(UWB) is applied for high QoS use case but radio regulation for UWB results in restricting use cases.
In MAC, hybrid contention base and free protocol can perform flexible delay and throughput for variable QoS levels of packets but its implementation complexity is too high for its complete protocol.
July 2022

## Slide 27
3. Necessity and Uniqueness for Amendment of BAN with Enhanced Dependability
July 2022
doc.: IEEE 802.15-22-0389-00-06ma

## Slide 28: 3.1 Necessity for Enhanced Dependability in 15.6 BAN
In case of coexistence of multiple BANs
  Current existing standard IEEE802.15.6 has not been designed to manage contention and interference among overlaid BANs. The more BAN uses in dense area, the more contention and inference cause performance degradation.
  Amendment of PHY and MAC for resolving these problems in coexistence of BANs is necessary.
In case of coexistence with other radios
  For enhanced dependability, UWB PHY of BAN should be updated to avoid performance degradation due to interference with coexisting other narrow band and UWB networks in overlapped frequency band.
In case of feedback sensing and controlling loop
  Remote medical diagnosis with vital sensing and therapy and control actuators and robotics need more dependable and efficient protocol.
Usability and Implementation Complexity
  Interoperability with other radio networks, more flexible network topology,
  Transparency with other standards such as ETSI SmartBAN
  Capability of ranging and positioning in UWB is required for mobility and security.
July 2022

## Slide 29: 3.2 Technical Challenges for Enhanced Dependability
Submission
First of all, we should recognize that any technology in PHY and MAC cannot guarantee full dependability in every use case.
However, we can design a new standard which can guarantee a certain level of enhanced dependability in a specific defined use case.
As an analogy of informed consent in medical doctor to a patient, a manufacturer of a dependable wireless network can describe such a specific defined use case that the manufacture can guarantee a defined level of dependability showing necessary cost and remained uncertainty. This is an honest manner and much better than no guarantee for any use case.
Therefore, an expecting standard describes a specific use case in which worst performance can be guaranteed enough high while most of exiting standards have been designed with average performance base.
Technical requirement for the specific use case can be guaranteed.
July 2022

## Slide 30: 3.3 Uniqueness different from existing standards (1/2)
MAC protocol for around packets and recursive access for feedback loop in remote sensing and controlling;
Level of dependability can be defined with showing necessary cost and remained uncertainty. This is an honest manner and much better than no guarantee for any use case.
Worst performance can be guaranteed enough high while most of exiting standards have been designed with average performance base.
Others
July 2022

## Slide 31: 3.3 Uniqueness different from existing standards (2/2)
PHY technologies to satisfy technical requirement for enhanced dependability in the focused use cases
  In feedback loop for remote monitoring sensors or radars and feedback controlling actuators, real-time cognition of varying condition on site and adaptive reconfiguration in relatively messy, small, and dense areas are requested to guarantee worst performance with permissible delay and errors.
  Within a permissible limited feedback delay, propagation paths connecting between nodes and coordinator should be found to keep connectivity by diversity, channel switching etc. .
  For such a dynamic environment and QoS requirement changing situation, sophisticated PHY technologies are requested to guarantee minimum requirement of performance.
July 2023

## Slide 32: 3.4 Focused Issues in Amendment of std 15.6 BAN with Enhanced Dependability
MAC Protocol in case of coexistence of multiple BANs
  Amendment of MAC for resolving these problems in coexistence of BANs is necessary.
  Specified MAC protocol for feedback sensing and control loop between coordinator and nodes.
PHY Interference Mitigation In case of coexistence with other radios
  For enhanced dependability, UWB PHY of BAN should be updated to avoid performance degradation due to interference with coexisting other narrow band and UWB networks in overlapped frequency band.
Usability and Implementation Complexity
  Interoperability with narrow band and UWB PHY
  more flexible network topology,
  Transparency with other standards such as ETSI SmartBAN
Ranging and Positioning Capability of UWB-BAN
  Mobile nodes and coordinator of BAN need ranging and positioning of UWB-BAN
July 2022

## Slide 33
4. Available Technologies in PHY and MAC Layers for the Focused Amendment of std 15.6 BAN with Enhanced Dependability
July 2022
doc.: IEEE 802.15-22-0389-00-06ma

## Slide 34
4.1 Intra and Inter System Interference among BAN and Other PANs
Inter-user interference
IR-UWB uses the same pulse as all users signal in the same standard.
Other users signal and/or the other network signal would be interference.
Inter-system interference
Interference from the other wreless system using overlapped frequency band. ⇒ Unknown
＊ 802.11a (wi-fi) （5GHz） overlaps
user C
user ？
user B
User A wants to connect to“B”.
UWB-WBAN
IEEE 802.15.6
Other UWB system.
e.g. IEEE 802.15.4a
user ？
user ？
interference
interference
July 2022
doc.: IEEE 802.15-22-0389-00-06ma

## Slide 35: 4.2 Approach for Intra and Inter System Interference among BAN and Other PANs
Sparate and Recognize each interference from different source.
* Apply suitable interference mitigation method according to source of interference.
Using both of Spatial and Temporal signal processing.
Remove
Interference canceller
Recognize and demodulate
Pulse shape multiple access Multi-user detection
Inter-user interference
“IUI” in this presentation
Interference from a system using the same pulse
Inter-system interference
“ISI” in this presentation
Interference from a system using overlapped frequency
known
unknown
July 2022

## Slide 36
consists a matched filter （MF1） and MF Group（MFG）
Tap coefficients of MF1 are the same as sequence of desired signal.
Coefficients of MF1 and each MFk that constituting MFG are orthogonal.
Desired signal does not through MF2～K-1 because orthogonality.
→only interference can through.
MFG makes replica of interference signal by lenear combination with weight vector w of linear combiner; LC.
Subtract interference replica from the output of MF1 .
Principle of OMF
OMF can remove interference without any pre-knowledge of interference.
4.3 Time Domain Interference Mitigation
OMF； orthogonal matched filter
July 2022
doc.: IEEE 802.15-22-0389-00-06ma

## Slide 37: 4.4 Space Domain Interference Mitigation
TDL-AA；Tapped delay line array antenna
Array antenna by using multiple antenna elements and tapped delay line.
Each antenna branch has coefficients.
Transfer function of this antenna has parameters of signal incoming angle;θ and frequency; ω.
⇒has characteristics of both of spatial and time domain.
Principle of TDL-AA
（Tapped delay line array antenna）
TDL-AA can work as interference canceller on both of time and space domains
July 2022

## Slide 38
2.4GHz
5.2GHz
∝ 1
τ m
ω0
Time（sec）
Frequency（Hz) Time（sec）
(a) Time Waveform of Pulse (right figure) and its Frequency Spectrum with notches in 2.4 and 5.2GHz for WLAN (left figure)
Frequency（Hz)
802.15-03/097r1, March 3, 2003.
Slide 38
4.5 Interference Mitigation among Other Radios
(b) Time Waveform of Pulse (right figure) and its Frequency Spectrum satisfying spectrum mask (left figure)
Ref. R.Kohno, H.Zhang, H.Nagasaka, "Ultra Wideband impulse radio using free-verse pulse waveform shaping , Soft-Spectrum adaptation, and local sine template receiving," doc.: IEEE
July 2022
doc.: IEEE 802.15-22-0389-00-06ma

## Slide 39: 4.6 Integrated Terminal to Avoid Mutual Interference in case of overlaid coexisting BAN and other Radios such as UWB-BAN and 4G/5G
Cellular Base Station
(Primary BS)
BAN Node (Secondary User)
Cellular Terminal (Primary User)
2047-3338 (Online) , Vol. 11, Issue 02, pp.8-15, March 2020
Integrated Terminal
= (Cellular Terminal + BAN Coordinator)
= (Primary User + Secondary BS)
M. Kim, T. Kobayashi, C.Sugimoto, R Kohno, ”Transmission Power Control of UWB -WBAN for Avoidance of Interference to Cellular Networks Using Integrated Terminal for Both Networks,” International Journal of Computer Science and Telecommunications, ISSN
July 2022

## Slide 40: 4.7 ICT & Data Science Platform for Infrastructure with BAN, 5G/6G Cloud, and Data Servers Based on Regulatory Science
3G, 4G, 5G
and 6G Cellular Wi-Fi
WiMAX etc.
Cloud Network
IEEE802.15
Coordinator
Windows
Android
iOS
Data Mining
Cloud Server/Data Center System Operation
Network Operator For 4G, 5G, and 6G
Data Server & repository For Data Mining with AI
Remote Diagnosis & Therapy
General Hospital
Regulatory Science Center
Regulatory Compliance Test, R&D, Standardization of Healthcare
ECG Sensor
Glucose Sensor
Rehabilitation Robot
& Wheel Chair
Surgery Robot
Multiple Sensor (SPo2 EEG, etc.)
ECG Sensor
BAN for User 1
BAN for User 60
….
Cdata Science Center
Cthree PHY with a common MAC in IEEE802.15.6
Slide 40
IEEE802.11
Coordinator Local 5G
doc.: IEEE 802.15-22-0389-00-06ma

## Slide 41
Submission
4.8 Contention among Overlaid BANs
Interference problem in the case where multiple BANs overlap (specifically, situations where people with BAN approaching)
Because the schedule adjustment between the coordinators has not been done
Issue
Solution
Negotiation between coordinators, scheduling between different BANs, to prevent deterioration due to inter-BAN interference
What is interference at the MAC layer
Sensor nodes within the communication range try to transmit packets at the same timing, causing collisions, making it impossible to communicate correctly
41 Ryuji Kohno, Takumi Kobayashi(YNU/YRP-IAI)
Node 1
Desired Packet
Desired Packet
Interfering Packet
Interfering Packet
Coordinator 1
Node
2
BAN1 BAN2
In case of negotiation of Coordinators of overlapped BANs, contention can be resolved
Coordinator 1
Coordinator 2
Coordinator 2
Node 1
Node 2
BAN1 BAN2
In case of no negotiation of Coordinators of overlapped BANs, contention happens among packets from nodes of f the BANs
Ref. R.Kohno, S.Ogawa, “MAC Protocol with Interference Mitigation Using Negotiation among Coordinators in Multiple Wireless Body Area Networks (BANs),” IEEE802.15 doc.#15-19-0119-00- 0dep-ig-dep, Vancouver, Canada, March 12, 2019
July 2022
doc.: IEEE 802.15-22-0389-00-06ma

## Slide 42: Demands of Dependable BAN of Things in IoT/M2M for Sustainable Social Services
42
Dependable BAN of Things for SDGs
Healthcare Service(Medical ICT)
Energy Network(Smart Grid)
CO2 Reduction, Green Innovation
Public Safety, National Defense
Global Borderless Economics
Population Ageing & Medical crisis
Integrated BAN/Cloud/AI Platform of Beyond 5G
July 2022

## Slide 43
Application of Dependable BAN of Things to Social Infrastructure
Medical Care
Security
Environmental Risk Management
Agricultural Sensing
Miscellaneous
Network Connection of Distributed Various Sensors
Various Applications could be integrated for global services.
Health Care
Kids Trace
Building Security Control
Safety and Privacy Control
Health Care
Disaster Prevention
Disaster Detection in Nature
Sensing Disaster
Checking Stability of Building and Bridge
Weather Prediction
Polusion Prevention
Plant Surveillance
Health Care
Management of Agricultural Farm
Product Traffic Managent
Product Quality Checking
Control Center
Various Services
Health Cre
Disaster Prevention
43
July 2022

## Slide 44
5. Technical Requirement for the Amendment of Std. 15.6 to Enhance Dependability
July 2022
doc.: IEEE 802.15-22-0389-00-06ma

## Slide 45: 5.1 Update of Technical Requirements for Amendment of BAN
IEEE802.15.6 for Medical BAN was established in Feb.
2012 and has not been updated for successive applications.
IG-DEP has been discussing with ETSI Smart BAN for digital healthcare and further medical applications.
NICT Brain Machine Interface; BMI labs with medical community requests amendment of IEEE802.15.6 for much higher capacity and reliability in IG-DEP, particularly 2nd Generation of ECoG with much more electrodes beyond EEG using UWB technologies.
IG-DEP has decided to include dependable medical BAN with higher capacity and reliability in focused applications.
Then updated technical requirement has been discussed.
The updated requirement will be summarized in next pages.
Slide 45
July 2022

## Slide 46: 5. Concluding Remark
Slide 46
Corresponding request from ETSI smart BAN and smart M2M, IG-DEP and its successive SG15.6a have discussed to focus on internal car network for IoT/M2M connections that is focused on BAN for human and car bodies.
As amendment of IEEE802.15.6, MAC for multiple BANs can be guaranteed to
satisfy permissible delay or back-off time and throughput of high QoS packets for human and vehicle BANs while maintaining average performance.
As amendment of IEEE802.15.6, PHY for UWB radios should be revised for updated UWB regulation. In particular, coexistence among different UWB
radios of IEEE802.15 such as 15.4a, 15.4f, 15.4z can be supported. For instance, during CCA, types or features of these UWB radios can be analyzed to control
access of packets from each radio.
To include new use cases with enhanced dependability such as the 2nd Generation of ECoG for Brain-Machine-Interface(BMI), technical requirement has been updated to cover higher data rate and more units of ECoG sensors .
We focus on amendment of IEEE802.15.6 for enhanced dependability in PHY and MAC and move on TG to complete the amendment.
If you have any question and comment, you are welcome to discussion in SG15.6a and send content contributions to
Ryuji Kohno <kohno@ynu.ac.jp> and Takumi Kobayashi <Kobayashi-takumi- ch@ynu.ac.jp>
July 2022

## Slide 47: Timeline for IEEE802.15.6 Revision (6ma)– Enhanced Dependability Body Area Network (ED-BAN)
Use cases & TRD & Channel model doc: July 2022
Specification Framework Document: November 2022
Draft Specification: January 2023
Call for proposals: September 2022
802.15 Letter ballot: March 2023
SA Sponsor ballot: July 2023
RevCom approval: December 2023
Slide 47

## Slide 48: Contacts and Conference call
Chair; Ryuji Kohno, YNU/YRP-IAI
kohno@ynu.ac.jp, kohno@yrp-iai.jp
Vice-Chair; Marco Hernandez, YRP-IAI/CWC
Marco.Hernandez@ieee.org
3. Secretary; Takumi Kobayashi, YNU/TCU
kobayashi-takumi-ch@ynu.ac.jp
Technical Editor; Minsoo Kim, YRP-IAI
minsoo@minsookim.com
Slide 48

## Slide 49
Thank You !
Any Questions ?
Slide 49