## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Discussion on Advanced Channel Coding for 15.4ab]
Date Submitted: [10th May 2022]
Source: [Wei Lin, Xun Yang, Shimi Shilo] Company [Huawei]
Address [Huawei base, Shenzhen, CHINA & Huawei Israel]
E-Mail:[lin.linwei@huawei.com]
Re: [Study Group 4ab: UWB Next Generation]
Abstract: [Discussion on Advanced Channel Coding for 15.4ab]
Purpose: []
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
Technical Guidance
PAR Objective | Proposed Solution (how addressed)
Safeguards so that the high throughput data use cases will not cause significant disruption to low duty-cycle ranging use cases. | 
Interference mitigation techniques to support higher density and higher traffic use cases | 
Other coexistence improvement | 
Backward compatibility with enhanced ranging capable devices (ERDEVs). | 
Improved link budget and/or reduced air-time | New Channel Coding Schemes can provide improved link budgets and reduced air time
Additional channels and operating frequencies | 
Improvements to accuracy / precision / reliability and interoperability for high-integrity ranging; | 
Reduce complexity and power consumption; | 
Hybrid operation with narrowband signaling to assist UWB; | 
Enhanced native discovery and connection setup mechanisms; | 
Sensing capabilities to support presence detection and environment mapping; | 
Low-power low-latency streaming | 
higher data-rate streaming allowing at least 50 Mbit/s of throughput. | New Channel Coding Schemes with higher rates can support high data rate
Support for peer-to-peer, peer-to-multi-peer, and station-to-infrastructure protocols; | 
Infrastructure synchronization mechanisms. | 

## Slide 3: Related Submissions
[1] 15-21-0506-02-04ab-Advanced Coding for Data Communications in 802.15.4ab, Aldana
[2] 15-21-0592-00-04ab-high-data-rates, C. Murray, et al
[3] 15-22-0181-01-04ab-new-data-rates, C. Murray, et al
[4] 15-22-0050-00-04ab- Channel Coding Considerations for 802.15.4ab, Wei Lin, et al
[5] 15-22-0154-00-04ab-further-considerations-of-advanced-channel-coding-on-15-4ab, Wei Lin, et al

## Slide 4: Discussions on Advanced Channel Coding
The consideration of introducing new advanced coding schemes were discussed in [1]
  [1] proposed to include LDPC codes as an optional solution after an extensive comparison of Turbo, Polar, NR LDPC, and 11n LDPC codes
  [1] states that LDPC codes have been successfully employed in 802.11n and 5G NR as well as other standard bodies, thus is a mature technology that should be considered in IEEE 802.15.4ab
  [1] also showed that LDPC provides substantial coding gains for long payloads and SNR gains for short payloads (e.g., 28 bytes) through extensive simulation results
New advanced coding was also discussed in new-data-rates in [2] and [3]
  [2] proposed to identify suitable candidate advanced codes for high-speed data, e.g., NR LDPC, 11n LDPC, candidates for Turbo and Polar codes and possibly additional LDPC codes
  [2] states that the power consumption at a given performance should be a central selection metric
  [3] summarized Advantages (robustness to noise types, gain for short/long payloads) and Disadvantages (power consumption, new code inclusion) of Advanced Coding
  [3] suggested to consider a base rate of ½, and stated the performance for short (~64-byte) as well as long packets is important

## Slide 5: Discussions on Advanced Channel Coding
In [4], we discussed the candidate rates and lengths for the advanced codes
  The performance of LDPC codes and Polar codes was compared for both short and medium payload sizes
  Besides the basic rate-1/2, one or two additional higher rates may be considered, e.g., R = 2/3
In [5], we further analyzed Polar, LDPC, Turbo and CC codes in terms of computational complexity, error correcting capability (BLER performance) and power consumption
  Both Polar and LDPC codes can achieve a decoding power consumption of <100mW
  No error floor exists for polar code, as list size increases, non-saturated performance is maintained, which is affordable by the ever-developing ASIC technology
  LDPC codes are widely adopted by various standards, and perform well at long code lengths, so they also should be considered

## Slide 6: Further Discussion on Advanced Channel Coding
In [1]-[5], the discussions of new advanced channel coding have been extensively discussed
  LDPC, Polar, Turbo Codes have been extensively evaluated in terms of performance advantages, decoding complexity, power consumption, et al.
  It is beneficial to include an advanced coding scheme according to [1]-[5]
According to previous discussions, we can further converge our candidates to LDPC codes
  LDPC codes have been widely employed in current wireless standards, e.g., 802.11ax, 802.11ay, 5G NR, …
  The performance gain and implementation complexities of LDPC codes are well known in the industry
  Suggest to converge to LDPC code as the only advanced channel coding scheme for 15.4ab
More details related to channel coding should be discussed in the next stage
  coding rate: ½ and 2/3
  Payload size: 20 bytes, 100 bytes, 1500 bytes

## Slide 7
Thank You

## Slide 8: Channel Coding Considerations - Overview
As of today, IEEE 802.15.4z standard supports data communication of relative small amounts of data with throughput of 31.2 mbps.
  No Capacity-Approaching FEC codes (LDPC, Turbo, Polar, etc.) has been adopted yet
IEEE 802.15.4a employed a rate-1/2 convolutional codes of K=3 (4 states) as well as an (63, 55) GF(26) Reed-Solomon Codes
To further enhance the performance, 802.15.4z optionally introduced an standard rate-1/2 convolutional codes of K=7 (64 states)
For the current 802.15.4ab standard, the needs for higher throughput as well as higher reliability have been discussed
  The introduction of advanced-coding has been discussed in [1]-[5]