## Slide 1: PAPR Analysis for Preamble Transmission
2 Sept 2022
DCN 15-22-0454-00-016t

## Slide 2
PAPR ANALYSIS
This analysis has been done to obtain the maximum PAPR value that the signal can have when identical preamble symbols occupy the subchannels. The solution to handle the high PAPR obtained in such a scenario is given in the subsequent slides.

## Slide 3
Number of subchannels (N) | PAPR (dB)
1 | 0
2 | 2.5
3 | 4.12
4 | 5.38
5 | 6.36
6 | 7.13
7 | 7.8
8 | 8.4
9 | 8.9
10 | 9.37
11 | 9.79
12 | 10.18
128 | 20.47
PAPR when same preamble symbol value is used across the subchannels, CP ¼, 8x Sampling

## Slide 4
SOLUTION TO HANDLE THE HIGH PAPR OF IDENTICAL PREAMBLE ACROSS SUBCHANNELS
As we can see from the previous slide, the PAPR increases linearly with the increasing number of subchannels and goes as high as 20 dB for 128 subchannels. So, instead of using the same preamble symbol, different preamble symbols are used across the subchannels. The PAPR analysis for the case when different symbols are used is given in the next slide.

## Slide 5
12 subchannels | Multiple symbols PAPR
With data symbols (QPSK) | 10.035 dB
With preamble | 7.35 dB
PAPR WHEN DIFFERENT SYMBOLS ARE USED
128 subchannels | PAPR
With preamble | Max : 10.3 dB Min : 5.5 dB