## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [A PHY Header Proposal]
Date Submitted: [12th September 2022]
Source: [Billy Verso, Jarek Niewczas, Carl Murray ] Company [Qorvo, Inc.]
Address [ ]
E-Mail:[billy.verso (at) qorvo.com]
Re: [Proposals for TG4ab next generation UWB project]
Abstract: [A proposed PHR for the 4ab HRP UWB PHY enhanced data rates supporting dynamic data rate selection.]
Purpose: [To promote further discussion and convergence on the content for the IEEE 802.15.4ab amendment.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Introduction
TG4ab is considering enhancing the HRP UWB PHY by additional data rates both above and below the current 7.8 Mb/s and 31.2 Mb/s rates.
These are being targeted to support data communications across a wide range of channel conditions, where lower rates may be dynamically selected for longer operating ranges and or when channel SNR deteriorates, or higher rates selected for shorter range operation or better SNR conditions.
In data networking scenarios a coordinator may have a set of neighbor devices wanting to use higher and lower rates without knowing which will be sending to it.
Where channel characteristics can change rapidly making a higher rate unusable, a device may need to drop the data rate at short notice, without being able to inform the remote device using the previously selected higher rate.
In both cases, which can occur together, there is a clear need for the PHR to include the data rate, and this submission proposes an efficient PHR to support variable data payload rates.

## Slide 3: Selecting modulation rate in the PHR
There are clearly scenarios in which including the PHY Payload modulation rate in the PHY header is beneficial.
However, typically to support variable payload modulation rates the PHR needs to be sent at the lowest supported rate.
The drawback of this is that at a lower rate the PHR takes significant airtime for devices/channels where a high data rate is workable and preferred to save time and energy.
  For instance, say we have a lowest rate of 1.95 Mb/s in 4ab, a 19-bit PHR (e.g., as is in 4z) with 6 tail bits for the k=7 convolutional code would be 25 symbols long. This would have a duration of 12.8 µs at 1.95 Msymb/s, which for the proposed 125 Mb/s rate would be equivalent to 200 octets, representing a substantial overhead.

## Slide 4: Efficient selection of modulation rate
This proposal reduces the overhead of having to send the PHR at the lowest supported rate by splitting the PHR into a rate header (PHR1) sent at a low rate and a main header (PHR2) sent at a high rate.
PHR1 can be very short.
  Three bits is sufficient to specify all the rates being considered at TG4ab.
  A fourth bit might be needed to signal LDPC if this affects the modulation of PHR2, otherwise indication of LDPC could be done in PHR2.
Assuming PHR1 is convolutionally encoded and tail symbols are included.
  At 1.95 Mb/s the 4-bit PHR1 with 6 symbol k=7 tail is just 5 µs long.

## Slide 5: PHR performance comparisons
The very short PHR1 has very strong performance when convolutionally coded with tail bits, as shown in the table below, (SNR levels for PER=1%). An example 40-byte payload is selected as a typical MAC frame size. Smaller frames could achieve very high performance due to additional gating gain.
For 40 bytes of data coded using CCK7 option, SNR requirement is 3.5dB. For LDPC at a coding rate of ½ it is 1.9dB and for LDPC-1296 with “full-parity” option (effective coding rate=1/3) it is -0.3dB. Regular length PHR (or PHR2) at 100% data modulation rate can match performance of the first two options. To match the third one, the PHR would need to be transmitted at a lower rate (e.g., 50%).
Short 4-bit PHR1 using CCK7 can match all data options at the same modulation rate.
PHR1 with CCK3 would require its modulation rate to be dropped to 50%.
Sequence | SNR [dB] | Comments
40 bytes data CCK7 | 3.5 | 
40 bytes data advanced coding | 1.9 | LDPC-648, CR=1/2
40 bytes data advanced coding | -0.3 | LDPC-1296, “full-parity”, CR=1/3
19-bit PHR (802.15.4z, +6 tail-bits) CCK7 | 1.9 | at 100% modulation rate
19-bit PHR (802.15.4z, +6 tail-bits) CCK7 | -1.1 | at 50% modulation rate
4-bit PHR1 (4-bits+6 tail-bits) CCK7 | -0.3 | at 100% modulation rate
4-bit PHR1 (4-bits+2 tail-bits) CCK3 | 2.2 | at 100% modulation rate

## Slide 6: Data vs Preamble performance limits
Another consideration is the performance of SYNC and carrier startup…
Contribution 15-20-0037 from J. Hammerschmidt advocated adding a stronger data modulation at 1.95 Mbps to balance the SYNC performance.
  A consequence of this is that schemes that are stronger than 1.95 Mbps with K=7 convolutional code will not be of benefit.
NOTE
The 4-bit PHR1 with 6 tail-bits matches this performance when modulated at 3.9 Mbps.

## Slide 7: Proposed PHR1 and PHR2 rates
The 4-bit PHR1 at 3.9 Mbps is ~2.5 µs long including six tail-bits (CCK7). This is a very small price to pay for the benefit of having fully flexible data rate selection.
PHR2 would be transmitted either at the full 100% rate or at a reduced 50% rate, depending on whether coding scheme used in data mode would be stronger than PHR2 performance, which depends on the advanced coding scheme that will be adopted.

## Slide 8: PHR2 possibilities
With PHR2 being sent at the data rate, it is not too expensive to include additional content that TG4ab thinks is useful / necessary:
  If PHR1 does not need to carry an LDPC indication, we should put it in PHR2
  Suggest to keep A bits and L bits and R bit content from 4z.
  Consider whether to change from SECDED to a pure error check, e.g., maybe an 8-bit CRC ?
  Consider whether to increase the payload length specifier to 14 bits, by adding two L bits or A bits.
Should we add additional items? (4a had a preamble length indication).

## Slide 9: Example packet cost of dynamic data rates
With PHR1 being size optimized and PHR2 being at the data rate, the cost of supporting dynamic data rates is low.

## Slide 10: Possible variants
Clearly a number of similar arrangements are possible following this basic scheme to reduce the overhead of supporting dynamic data rates and increase the flexibility of the PHR.
For example PHR1 could be just two low-rate bits used just to specify the modulation rate of PHR2. Then PHR2 can have modulation rate (and LDPC) bits for the payload.
  This offers more flexibility in rate selection for PHR and Data.
And, as per submission 15-22-0475-01 that Carlos presented, PHR2 can include whatever additional fields TG4ab wants.
  e.g., Sensing bit, Ranging bit, etc.

## Slide 11: Conclusion
This submission presented an efficient way of supporting variable data rate in the PHY header.
This enables the data rate to be dynamically changed across the whole proposed range of 1.95 Mbps to 124.8 Mbps, via data-rate bits included in an initial rate header (PHR1).
A second, main header (PHR2) is transmitted at same rate or lower than the payload modulation rate depending on the required strength.
  PHR1 always being sent at 3.9 Mbps lasts for only 2.5 µs which minimizes the overhead of signaling a variable modulation rate

## Slide 12
THE END.