## Slide 1
Project: IEEE P802.15 Working Group for Wireless Specialty Networks (WSN)
Submission Title: Evolution of 4z enabling optimized many-to-many ranging for dense environments
Date Submitted: September 2022
Source: Jean-Marie André (ST microelectronics), Sven Zeisberg (HTW), Erik Mademann (ZIGPOS)
Contact: ST microelectronics, 19 boulevard de la mer Caspienne, 73372 Le Bourget du Lac, France
E-Mail: jean-marie.andre {at} st.com, sven.zeisberg {at} htw-dresden.de
Re: Call for contributions to IEEE 802.15 TG4ab
Abstract: Evolution of IEEE 802.15.4z enabling efficient scheduled positioning systems
Purpose: Propose evolutionary extensions to IEEE 802.15.4z for scheduled ranging concerning ranging roles in slot assignments and initiator picking of responders.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributors acknowledge and accept that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
PAR Objective | Proposed Solution (how addressed)
Safeguards so that the high throughput data use cases will not cause significant disruption to low duty-cycle ranging use cases | 
Interference mitigation techniques to support higher density and higher traffic use cases | Reduce number of messages in dense positioning systems
Other coexistence improvement | Reduce signal aggregation
Backward compatibility with enhanced ranging capable devices (ERDEVs) | 
Improved link budget and/or reduced air-time | reduce air-time by avoiding transmission duplication and or merging messages of various types
Additional channels and operating frequencies | 
Improvements to accuracy / precision / reliability and interoperability for high-integrity ranging | 
Reduced complexity and power consumption | Less messages will optimize power consumption in dense environments.
Hybrid operation with narrowband signaling to assist UWB | 
Enhanced native discovery and connection setup mechanisms | 
Sensing capabilities to support presence detection and environment mapping | 
Low-power low-latency streaming | 
Higher data-rate streaming allowing at least 50 Mbit/s of throughput | 
Support for peer-to-peer, peer-to-multi-peer, and station-to-infrastructure protocols | The proposed scheme supports infrastructure-based positioning systems.
Infrastructure synchronization mechanisms | The proposed extension allows multiple synchronization schemes

## Slide 3
In dense environments like manufacturing halls or logistics centers a lot of items must be tracked, and multiple location tracking solutions must be implemented (e.g. DL-TDoA, UL-TDoA, TWR) at the same venue.
Multiple sequences of ranging may be required simultaneously:
Ranging between the anchors in order to keep them synchronous
Ranging between the anchors and the tags to run location algorithms
To accommodate as many simultaneous ranging schemes as possible, we suggest to allow several messages to be merged into one single UWB frame. This maximizes the use of available time slots.
Requirements for location tracking in dense environments

## Slide 4
Multiple rangings scheduled sequentially
Ranging between anchors
Ranging with tags
CTRL
INIT
RESP
Anchor 1
Anchor 1
Anchor 2
CTRL
INIT
RESP
Anchor 2
Anchor 2
Anchor 3
RESP
Anchor 3
CTRL
Anchor 1
INIT
Anchor 1
INIT
Anchor 2
INIT
Anchor 2
RESP
Tag 1
RESP
RESP
Tag 2
Tag 3

## Slide 5
Multiple rangings organized simultaneously
CTRL
INIT
RESP
Anchor 1
Anchor 2
Anchor 3
INIT
CTRL
INIT
RESP
CTRL
Anchor synchronization squeezed in 3 time slots

## Slide 6
Multiple rangings organized simultaneously
CTRL
INIT
RESP
Anchor 1
Anchor 2
Anchor 3
RESP
Tag 2
Tag 3
RESP
Tag 1
INIT
CTRL
INIT
RESP
CTRL
RESP
Tag ranging adding only 3 more time slots

## Slide 7
Multiple rangings organized simultaneously
CTRL
INIT
RESP
Anchor 1
Anchor 2
Anchor 3
RESP
Tag 2
Tag 3
RESP
Tag 1
INIT
CTRL
INIT
RESP
CTRL
RESP
OWR Do-L
OWR Do-L
OWR Do-L
OWR Do-L
OWR Do-L
OWR Do-L
OWR Do-L
OWR Do-L
OWR Do-L
OWR Do-L
Infinite number of receivers may pick anchor signals to run DL-TDoA

## Slide 8
Multiple rangings organized simultaneously
CTRL
INIT
RESP
Anchor 1
Anchor 2
Anchor 3
RESP
Tag 2
Tag 3
RESP
Tag 1
INIT
CTRL
INIT
RESP
CTRL
RESP
Cumulating multiple functions into one single UWB frame makes the whole system much more time-efficient (6 time slots vs 14) for dense ranging use cases
Tag 4
OWR Up-L
OWR
Up-L
Tag 5
OWR Do-L
OWR Do-L
OWR Do-L
OWR Do-L
OWR Do-L
OWR Do-L
OWR Do-L
OWR Do-L
OWR Do-L
OWR Do-L

## Slide 9
There are multiple occasions defined in the existing IEEE 802.15.4z where messages can carry multiple roles:
Non-deferred reports: a single message carries the response to an initiation message as well as the report part
RCM & Initiation roles can be merged into one single message in general
DS-TWR realization with 3 messages: the 2nd message carries the role of responder and initiator
Conclusion: the concept of multiple roles for messages is already existing in IEEE 802.15.4z (e.g. section 6.9.7.2)
Allowing messages to carry multiple roles

## Slide 10
The role of frames/slots can be described in the Ranging Control Phase of a Ranging Round, where RCM provide a description of the various messages to be exchanged during the ranging round. Alternatively, it is described in a joint RCM/Init message.
We are suggesting here to extend the identification of the messages in order to allow for more variations of multi-purpose messages.
Allow/clarify in scheduled ranging mode explicitly a double definition of time slots containing a response to a previous initiation and at the same time containing an initiation for potential later response frames in the round.
Consequently allow also extending the already allowed RCM/Initiation merging to become also RCM/Initiation/Response merging in slots.
These extensions/clarifications will be helpful in particular for many-2-many ranging use cases, e.g. in dense DL-TDoA scenarios anchors message exchanges.
Extending managing multiple roles frames

## Slide 11
In a ranging round a Response message is currently associated to one Initiation message as early as either during the RCM message in the Ranging Control Phase or during a joint RCM/Initiation message in the Initiation phase.
For scheduled ranging in case of having more than one initiator we are suggesting to extend this approach by allowing:
  The possibility for a responder to select (multiple) initiation message(s) and include the related timing information into a single response message, hence to gather the selected (multiple) response(s) into one single message on air.
  So the responder selects during operation the initiator, which he is considering in its transmission time slot for placing time relation information
Allow Responders to pick initiators

## Slide 12
Example: Many-2-many with responder selected initiators (based on e.g. radio visibility,…)
CTRL
INIT
Anchor 1
Anchor 2
Anchor 3
INIT
CTRL
INIT
RESP
CTRL
Anchor 4
Anchor 5
Anchor 6
BP
Anchor 7
BP
Anchor 1
Anchor 2
Anchor 3
Anchor 4
Anchor 5
INIT
RESP
CTRL
INIT
RESP
CTRL
INIT
INIT
INIT
RESP
INIT
RESP
INIT
RESP
INIT
RESP
INIT
RESP
slot 1
slot 2
slot 3
slot 4
slot 5
slot 6
slot 7
slot 8
slot 9
slot 10
slot 11
slot 12

## Slide 13
Geo-Map of many-2-many with responder selected initiators (based on e.g. current radio visibility, response calculation time, …)
1
4
3
2
5
OWR Do-L
OWR Do-L
OWR Do-L
OWR Do-L
OWR Do-L
OWR Do-L
OWR Do-L
OWR Do-L
OWR Do-L
OWR Do-L
6
7

## Slide 14
[1] Sven Zeisberg, Jean-Marie André: 802.15.4z upgrade requirements for larger industrial scenarios. IEEE 15-21-0066-00-04ab, 2021-01-20, IEEE 802.15 SG4ab
[2] Zhenzehn Ye: Reverse TDOA Applications and Technical Characteristics. IEEE 15-21-0223-00-04ab, 2021-04-27, IEEE 802.15 TG4ab
[3] Jean-Marie André, Sven Zeisberg: DL-TDOA positioning TDMA scheme. IEEE 15-21-0530-00-04ab, 2021-10-19, IEEE 802.15 TG4ab
[4] Zhenzehn Ye : Downlink TDOA (DL-TDOA) Location Service in 802.15. IEEE 15-21-0488-00-04ab, 2021-09-15, IEEE 802.15 TG4ab
[5] Yongsen Ma, Zhenzhen Ye: Beacon and Ranging Frames to Support Downlink TDOA (DL-TDOA) Location Service in 802.15. IEEE 15-21-0616-01-04ab, 2021-11-16, IEEE 802.15 TG4ab
[6] J.S. Hammerschmidt, Ersen Ekrem, Eren Sasoglu, Xiliang Luo: Narrowband assisted multi-millisecond UWB. IEEE 15-21-0409-00-04ab, 2021-07-20, IEEE 802.15 TG4ab
[7] Jean-Marie André (ST microelectronics), Sven Zeisberg (HTW), Vincent van der Locht (SynchronicIT), Frank Stephan (ZIGPOS), Andreas Schumacher (TRUMPF): TDMA scheme enabling industrial DL-TDoA and UL-TDoA scenarios. IEEE 15-22-0077-00-04ab, 2022-01-2, IEEE 802.15 TG4ab
References

## Slide 15
Thank you for your kind attention.
Are there any questions?