## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: NB CCA follow-up
Date Submitted: September 10, 2022
Source: Huan-Bang Li, Takeshi Matsumura (NICT, Japan), Mingyu Lee (Samsung).
Address: 3-4 Hikarino-oka, Yokosuka-shi, Kanagawa, 239-0847 Japan
E-Mail: {lee, matsumura}@nict.go.jp , mg0218.lee@samsung.com
Abstract: Summary on NB-assisted UWB channel access.
Purpose: To improve coexistence among UWB systems.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the authoring individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The authors(s) reserve(s) the right to add, amend or withdraw material contained herein.

## Slide 2
PAR Objective | Proposed Solution (how addressed)
Safeguards so that the high throughput data use cases will not cause significant disruption to low duty-cycle ranging use cases | Effective and efficient CCA reduce disruption between UWB devices
Interference mitigation techniques to support higher density and higher traffic use cases | Use NB radio to facilitate CCA so as to improve coexistence.
Other coexistence improvement | Use NB radio to improve coexistence among UWB devices.
Backward compatibility with enhanced ranging capable devices (ERDEVs) | 
Improved link budget and/or reduced air-time | 
Additional channels and operating frequencies | 
Improvements to accuracy / precision / reliability and interoperability for high-integrity ranging | 
Reduced complexity and power consumption | 
Hybrid operation with narrowband signaling to assist UWB | Exploiting pilot NB PHY and concurrent operation with UWB to assist UWB channel access
Enhanced native discovery and connection setup mechanisms | 
Sensing capabilities to support presence detection and environment mapping | 
Low-power low-latency streaming | 
Higher data-rate streaming allowing at least 50 Mbit/s of throughput | 
Support for peer-to-peer, peer-to-multi-peer, and station-to-infrastructure protocols | 
Infrastructure synchronization mechanisms | 

## Slide 3: Contents
NB CCA in short
NB CCA proposal summary
Criteria of using NB CCA
Further enhancement on NB CCA

## Slide 4: NB CCA in Short
A pair of coupled NB radio UWB are used. Operation of NB radio and UWB are based on same timer. NB radio carries UWB channel occupancy information.
CCA is performed at NB channel. UWB channel access are performed based on the coupled NB radio’s CCA results.
Same NB CCA mechanism can be commonly applied no matter if different types of UWB schemes are operated at neighbor or not.

## Slide 5: Summary of NB CCA
Add an optional CCA mode to 10.2.8 Clear channel assessment (CCA) of IEEE 802.15.4-2020 as follows (15-22-0275-00-04ab)
An HRP UWB PHY shall implement one CCA Mode 1 through CCA Mode 4 or one of the following methods:
CCA Mode 5: HRP UWB preamble sense based on the SHR of a frame. CCA shall report a busy medium upon detection of a preamble symbol as specified in 15.2.6. An idle channel shall be reported if no preamble symbol is detected up to a period not shorter than the maximum packet duration plus the maximum period for acknowledgment.
CCA Mode 6: HRP UWB preamble sense based on the packet with the multiplexed preamble as specified in 15.6. CCA shall report a busy medium upon detection of a preamble symbol as specified in 15.2.6.
CCA Mode 7: UWB medium access coupled with CCA of narrow-band assisted PHY (NBA-PHY) as specified in 15.x. Transmission or CCA conducted by the coupled NBA-PHY act as indications of the UWB-PHY medium access status. CCA shall report an idle or a busy UWB medium based on the NBA-PHY CCA results.
*Original texts are highlighted in yellow while the proposed add-on texts in blue.

## Slide 6: Summary of NB CCA -- Continue
Add a subclause to IEEE 802.15.4-2020 as follows to define NB CCA (15-22-0275-00-04ab)
Subclause ## Narrow-band assisted CCA
A compliant device shall contain a UWB PHY and a coupled narrow-band assisted PHY (NBA-PHY). The UWB PHY that uses CCA mode 7 as defined in 10.2.8 shall be operated with the NBA-PHY in tightly coupled manner, at least, with synchronized clock or same MAC timer.
On one hand, a compliant device shall perform CCA using the NBA-PHY against narrow-band medium whenever it intends to access a UWB medium. On another hand, a compliant device that intends to execute a UWB task after receiving an idle medium report shall firstly transmit an NBA packet and then execute the UWB task.
……
* The proposed add-on texts are highlighted in blue.

## Slide 7: Example Illustration of Operation
Transmission of NB radio and UWB are time deterministic.
(Transmission can start together or with pre-determined time interval )

## Slide 8: Criteria of Using NB CCA
  A compliant device may switch-off NB CCA if the effect of UWB interference is negligible. An example of making such a decision is that the device achieves high success ratio when conducting UWB tasks.
  A compliant device may switch-on NB CCA if the effect of UWB interference isn’t negligible. An example of making such a decision is that the device achieves low success ratio when conducting UWB tasks.
  When NB CCA is switched on, the default CCA duration should cover the period from a NB radio starting transmission until a coupled UWB completing UWB task.
  A NB radio may terminate CCA procedure whenever it already successfully acquired necessary channel occupancy information.

## Slide 9: Enhancing NB CCA
We assume that the UWB task timing is deterministic and pre-determined. In scenarios where NB radio is sensed but related timing information is not detected. What can we do?
For compliant devices, “deterministic and pre-determined” should be available because parameters are specified in the standard.
A solution for the above scenarios is that we specify two distinctive NB radio sets. One declares start of a UWB task (s-NB) and another declares end of the UWB task (e-NB). If a device senses a s-NB, it shall sense an e-NB before accessing channel. If a device senses an e-NB, it can start accessing channel based on NB CCA.

## Slide 10: Further Attention To Be Paid
Keep the NB packet as short as possible so that NB radio doesn’t cause NB channel stuff.
Allocate proper NB radio TX power as well as NB CCA sensing level so that NB radio doesn’t unnecessarily reduce the utilization of UWB channel.
The coupled NB radio should be designed with distinguished features than the other NB radios so that the other NB radio don’t shut up UWBs.

## Slide 11: Thank you for your attention!