## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: 802.15.4 Privacy Addresses
Date Submitted: 11th of September, 2022
Source: Tero Kivinen Company -
E-Mail: kivinen@iki.fi
Re: September WNG meeting
Abstract:
Discussion about the Privacy Addresses in the IEEE Std 802.15.4
Purpose: Provide information which kind of changes are needed to the standard.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
Privacy Addresses in IEEE Std 802.15.4
September 11, 2022
Tero Kivinen

## Slide 3
Problem
Using static addresses allows efficient way to track people.
People = we do not care that much of machines, tracking of people is the issue
Efficient way = There is always ways to track, we want to make it hard enough that it is too expensive to track everybody

## Slide 4
History
Why this has not been a real issue before
  Quite a lot of IEEE 802.15.4 use has been IoT, industrial, or non-mobile devices.
  If the light fixture is in static location, there is no point of tracking that.
  Even if the device moves around inside the industrial facility it quite often is not tied to specific person.

## Slide 5
What has changed
We are putting more and more 802.15.4 radios to mobile devices, moving with people
  Phones
  Remote controls for devices
  Sensors in body
  Sensors in vechiles (Cars, Bikes etc)
  Trackers in the handbags, luggage

## Slide 6
Types of addressing
Extended addresses
  64-bit MAC addresses
  Global
  Stable
  24-bit CID, 40-bit device part
Short addresses
  16-bit
  Allocted by coordinator during association
  Local to the network
  Temporary

## Slide 7
Why short addresses are not enough
We used to say short addresses solves the privacy issues, as they are not stable and can be changed.
  Good in theory, bad in practice
  There are still stable extended address in devices for joining etc
  Devices will respond to their extended address, and might use it in certain cases, i.e., devices use both short and extended addresses at the same time.
  They are mostly meant to save bytes over the air.

## Slide 8
Why we can do better than for example 802.11
Use of 64-bit addressing allows us to have lots of bits to play around
  We could allocate one 24-bit CID for “privacy addresses” and randomly generate lower 40-bit to generate temporary random extended address
  Our networks are usually small (few dozen devices in same network)
  Meaning that even if the devices change addresses every hour, the probability of collisions is extremely low
  If we want to have probability of collision down to one in million (2-20) we can still have more than √(2×240×2-20) = √(21+40-20) = √(221) = 210.5 = more than 1000 devices in network.

## Slide 9
Issues of changing addresses
Devices often do not have other identity to use
Beacons are recognized by the addresses
Security context is tied to the extended address.
  If we change extended address, we might need to recreate security keys etc.
  We need to reset frame counter to zero, as this is new device (and not doing so would allow attackers to track us by tracking frame counters).
  We most likely need a method of “moving” security context from the previous extended address to new one.

## Slide 10
Other possible attacks
Probing attack
  Attacker sends a packet to your stable extended address and observes whether you respond to it
Probing beacons are another problem
  Attacker sends a “known” beacon and observes whether device react to that.
Traffic patterns are another way to track, but that is outside the scope here.
  There are always ways to track, we want to limit correlation and tracking of the persons.
Ranging can offer even more ways of tracking, and may offer much better ways to track
  Track the exact location of your smartwatch while you are going through the shelves in the shop, and see how long you stay next to each item, trying to find out what interests you and what does not.

## Slide 11
Related work
802.11 is also working to solve these issues
  11-22-1306 for beacon and discovery protection
  11-22-0114 for pre-calculated MAC addresses
  802.11 Requirements are listed in 11-21-1848
This is problem we should try to solve jointly with 802.11.

## Slide 12
What should we do
We should start Study group to form a PAR to define what kind of changes or extensions are needed to support privacy addressing in the IEEE Std 802.15.4.