## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [New Scheduling IE for 4ab applications]
Date Submitted: [13 September, 2022]
Source: [Kangjin Yoon, Chunyu Hu, Carlos Aldana, Claudio Da Silva] Company [Meta Platforms, Inc.]
[Mingyu Lee, Youngwan So, Taeyoung Ha, Aniruddh Rao Kabbinale] Company [Samsung]
E-Mail: [{kyoon, chunyuhu, caldana, claudiodasilva}@fb.com]
[{mg0218.lee, youngwan.so, ty1115.ha, aniruddh.rao}@samsung.com]
Re: [Input to TG4ab]
Abstract: [New Scheduling IE for 4ab applications has been proposed.]
Purpose: [To support new applications in 4ab.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
PAR Objective | Proposed Solution (how addressed)
Safeguards so that the high throughput data use cases will not cause significant disruption to low duty-cycle ranging use cases | 
Interference mitigation techniques to support higher density and higher traffic use cases | 
Other coexistence improvement | 
Backward compatibility with enhanced ranging capable devices (ERDEVs) | 
Improved link budget and/or reduced air-time | Reduced size of the new Scheduling IE can reduce airtime
Additional channels and operating frequencies | 
Improvements to accuracy / precision / reliability and interoperability for high-integrity ranging | 
Reduced complexity and power consumption | Receiver address field in the new Scheduling IE helps devices to enter sleep mode more often
Hybrid operation with narrowband signaling to assist UWB | 
Enhanced native discovery and connection setup mechanisms | 
Sensing capabilities to support presence detection and environment mapping | 
Low-power low-latency streaming | 
Higher data-rate streaming allowing at least 50 Mbit/s of throughput | New Scheduling IE can schedule slots for data communication application efficiently
Support for peer-to-peer, peer-to-multi-peer, and station-to-infrastructure protocols | 
Infrastructure synchronization mechanisms | 

## Slide 3: Previous Contributions
DCN 422r0 (July 2022) “UWB Sensing - Scheduling”
  Introduced options for scheduling sensing fragments
DCN 392r1 (July 2022) “More on Mixed MMS for Ranging Integrity”
  Shared slot usage patterns for multi-millisecond ranging
DCN 404r1 (July 2022) “Co-scheduling ranging and sensing”
  Showed possible scheduling patterns for simultaneous ranging and sensing

## Slide 4: Recap: Ranging Device Management IE
In 15.4z-2020, Ranging Device Management (RDM) IE is used for slot scheduling
RDM IE requires one RDM List element (3 bytes) per one slot scheduling  Size increases linearly with the number of scheduled slots
Bits: 0-7 | 8-14 | 15 | 16 | 17 | 18-23 | Octets: variable
Length | Sub-ID | Type | SIU | Address Size | RDM List Length | RDM List
Variable | Variable | 0 | 1 | 0 | 5 | 5 RDM List elements
RDM List element
RDM IE
Ranging Round
0
1
2
3
4
5
6
7
8
9
10
11
Bits: 0 | 1-7 | Octets: 2
Ranging Role | Slot Index | Address
0/1 | 1 | Device address
Bits: 0 | 1-7 | Octets: 2
Ranging Role | Slot Index | Address
0/1 | 5 | Device address
…
RDM IE

## Slide 5: Motivation
Maybe not a big problem for typical ranging application which does not require many slots
However, some of new 4ab applications (e.g., data communication, multi-millisecond (MMS) ranging) may require many slots to be scheduled and the size of RDM IE will be huge
Examples
  3 MB file transfer may require 2000 scheduled slots
  MMS ranging with integrity fragments may require 10s of scheduled slots

## Slide 6: Proposal: New Scheduling IE
Propose bitmap-based scheduling
  Control field
    Address Size field: 2 bytes address vs. 8 bytes address
    Scheduling List Length field: The number of Scheduling List elements
  Scheduling List elements
    Bitmap Size field: The size of Bitmap field (in the unit of bytes)
    Bitmap field: Bitwise slot scheduling pattern
Thanks to bitmap, we can have only one element per device
Octets: 1 | Variable | … | Variable
Control | Scheduling List element #1 | … | Scheduling List element #N
Bits: 2 | 6 | Octets: Variable | 2 or 8
Bitmap Size | Reserved | Bitmap | Address
Bits: 1 | 7
Address Size | Scheduling List Length

## Slide 7: Proposal: New Scheduling IE
Example of Bitmap Size field
Bits: 2 | 6 | Octets: 1/2/4/8 | Octets: 2 or 8
Bitmap Size | Reserved | Bitmap | Address
Bitmap Size field value | Meaning
0 | 8 bits bitmap
1 | 16 bits bitmap
2 | 32 bits bitmap
3 | 64 bits bitmap
  We can assign more bits if needed
Scheduling List element

## Slide 8: Proposal: New Scheduling IE
Comparison on the size of Scheduling IE
  Legacy RDM IE: 1+S*3 bytes, where S = # of scheduled slots
  New Scheduling IE: 1+N*(3+) bytes, where N = # of devices
Chart: When the number of devices (N) is 2; 2 B MAC address
| 8 | 16 | 32 | 64
New Scheduling IE | 9 | 11 | 15 | 23
Legacy RDM IE | 25 | 49 | 97 | 193
Chart: When the number of devices (N) is 2; 8 B MAC address
| 8 | 16 | 32 | 64
New Scheduling IE | 21 | 23 | 27 | 35
Legacy RDM IE | 73 | 145 | 289 | 577

## Slide 9: Additional Proposal: Receiver Address
Address field in the legacy RDM IE indicates who will be the sender in the slot and no information about receiver
Having Receiver address field in Scheduling List element will help devices to enter sleep mode and save power if the slot is not intended for them
Bitmap should be provided per sender/receiver pair
Bits: 2 | 1 | 5 | Octets: Variable | Octets: 2 or 8 | 2 or 8
Bitmap Size | Receiver Address Present = 1 | Reserved | Bitmap | Sender Address | Receiver Address
Bits: 2 | 1 | 5 | Octets: Variable | Octets: 2 or 8
Bitmap Size | Receiver Address Present = 0 | Reserved | Bitmap | Sender Address
Scheduling IE when Receiver Address field is present
Scheduling IE when Receiver Address field is not present

## Slide 10: Summary
Proposed new Scheduling IE can reduce the size of Control Message by utilizing bitmap
New Scheduling IE may have Receiver Address field to indicate intended receiver of scheduled slots to enable more often sleep mode
Note: Legacy RDM IE can still be used for the application which schedules only small number of slots per device

## Slide 11: Thank You