## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: UWB Sensing Discussion for 802.15.4ab
Date Submitted: September 14, 2022
Source: Pooria Pakrooh, Bin Tian, and Koorosh Akhavan (Qualcomm)
E-Mail:{ppakrooh, btian, kakhavan}@qti.qualcomm.com
Abstract: In this contribution, we share our thoughts on some aspects of UWB sensing that need further discussion and agreement among the group.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the authoring individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The authors(s) reserve(s) the right to add, amend or withdraw material contained herein.

## Slide 2
PAR Objective | Proposed Solution (how addressed)
Safeguards so that the high throughput data use cases will not cause significant disruption to low duty-cycle ranging use cases | 
Interference mitigation techniques to support higher density and higher traffic use cases | 
Other coexistence improvement | 
Backward compatibility with enhanced ranging capable devices (ERDEVs) | 
Improved link budget and/or reduced air-time | 
Additional channels and operating frequencies | 
Improvements to accuracy / precision / reliability and interoperability for high-integrity ranging | 
Reduced complexity and power consumption | 
Hybrid operation with narrowband signaling to assist UWB | 
Enhanced native discovery and connection setup mechanisms | 
Sensing capabilities to support presence detection and environment mapping | We share our thoughts on some aspects of UWB sensing that need further discussion and agreement among the group.
Low-power low-latency streaming | 
Higher data-rate streaming allowing at least 50 Mbit/s of throughput | 
Support for peer-to-peer, peer-to-multi-peer, and station-to-infrastructure protocols | 
Infrastructure synchronization mechanisms | 

## Slide 3: Introduction
Several contributions on UWB sensing have been discussed in 15.4ab [1]-[10].
There are several open aspects that we need to agree on to continue with the development of technical framework.
In this contribution, we plan to share our thoughts on the following aspects of UWB sensing, and motivate further discussion
  Sensing pulse shape
  Sensing packet formats
  Sensing sequence
  CIR report format
We suggest separating the discussion based on sensing modes
  Mono-static and bi/multi-static modes can have different requirements
  This justifies different considerations for sensing PPDU format, sequence and report format

## Slide 4: Sensing Pulse Shape
Two step definition for sensing pulse shape
  An ideal reference pulse shape to be defined
  Then, cross-correlation (with reference pulse), and/or time-domain mask need to be defined in 4ab.
    For ranging, the time domain (TD) mask is defined for “recommended min precursor pulse” in 4z
Gaussian pulse shape proposed in [1], whereas Kaiser window is proposed in [2]
  Both have minimal pre/post-curser. Need to proceed to defining sensing TD mask
Need to look at metrics such as range resolution, PSLR (peak to sidelobe ratio), the zero-Doppler ambiguity function, and spectrum efficiency (RMS BW) [3]
  For low RMS BW of sensing pulse, the ranging estimation accuracy is affected in joint sensing/ranging scenarios
Use the “sensing pulse” across the 4ab packet: preamble, payload, sensing and ranging frames
  Pulse shape does not change in the middle of packet. Sensing pulse shape is used for entire packet in sensing applications.

## Slide 5: Sensing Packet Format
Sensing PPDU format needs to be determined
  Need to define separate formats for monostatic and bi/multi-static mandatory modes
  Requirements for monostatic and bi/multi-static sensing are different, e.g., maximum unambiguous range is critical to monostatic sensing, synchronization is needed for bi-static sensing.
  One packet structure specific for monostatic sensing
    A sensing-only packet, including a field for sensing can be sufficient, as SYNC is not required for monostatic sensing.
    So far, one proposal on a pulse pattern for monostatic sensing [4].

## Slide 6: Sensing Packet Format for Bi-static Sensing
  For bi/multi-static sensing, it is convenient to build PPDUs on top of the existing 4z ranging PPDUs.
    Suggesting to define the packets for sensing to match the current 4z ranging packet formats
    Adding the sensing field to the end of the current 4z packets, to make things backward compatible
    Defining combined packets for sensing/ranging/data comm as optional modes
4z Ranging
4ab Sensing
PHY Payload
SEN
PHR
SYNC
SFD
SEN
SYNC
SFD
PHY Payload
STS
PHR
SYNC
SFD
SEN
STS
SYNC
SFD
SEN
Sensing only
SP0+Sensing
SP1/2+Sensing
SP3+Sensing
Mandatory
Optional
Optional
Optional

## Slide 7: Sensing Sequence
Proposal on sensing sequence for monostatic sensing [4].
For bi/multi-static sensing: prioritize the properties for sensing sequence: Low autocorrelation, low cross-correlation, security, as also mentioned in [10].
  Encrypted: STS can be re-used
    Encryption may not be needed for sensing as in ranging, as the concept of security for sensing is not well defined
  Non-encrypted: The sequence can be tied to preamble sequence discussion
    Similar requirements as in preamble sequence, since it is used for channel estimation
    The preamble sequence discussion, when converged, can be used for any non-secure ranging/sensing applications, including bi-static/multi-static sensing

## Slide 8: CIR Report
Different types of report for monostatic and bi/multi-static modes
  For monostatic sensing with inherent synchronization, further CIR processing can be done before creating the report
    Parameters such as Angle of Arrival (AoA), velocity, can be included in the report
  For bi/multi-static, convergence on the parameters of sensing CIR report is needed
    CIR reference path: Proposed earliest detected tap as the reference for the CIR report
        Earliest detected tap is already used for ranging
        For NLOS channels, specifying of CIR window offset is more efficient, relative to earliest detected tap
        Strongest tap can be spoofed and jammed using a strong interference, which can move the report window
Noise Threshold
Sensing window parameters defined relative to the earliest detected tap
Reference Point: Earliest detected tap
+

## Slide 9: Bi-static Sensing: CIR Report Parameters
On-going discussion on some of the parameters of CIR report
  Sampling rate: 2x chip rate (499.2MHz) to balance reasonable accuracy, complexity and report overhead
    Due to time drift, extra post-processing may be needed to align CIR reports for different packets. 2x chip rate gives better accuracy for interpolation
    Overhead of 2x chip rate CIR sampling is not significant: For example, HPRF payload duration of 37.5us to include the report for 10m of sensing range spread [5]
    Chip rate can be defined based on the effective BW, if sensing at multiple frequency is adopted
  The number of CIR windows: one window or multiple windows
    Suggesting to have one window of configurable duration and position, to cover a large sensing area.
      Multiple windows increase complexity and potentially payload CIR feedback size. Its need requires to be discussed.

## Slide 10: Summary
We reviewed the existing discussions on the following aspects of UWB sensing
  Sensing pulse shape
  Sensing packet formats
  Sensing sequence
  CIR report parameters for bi/multi-static sensing
Sensing packet formats, and sequence need to be defined separately for monostatic and multi-static sensing scenarios.
Parameters of the bi-static sensing report were further discussed, including the sampling rate, reference point, and window-based report.

## Slide 11: References
[1] 15-22-0418-00-04ab Sensing pulse shape consideration in 802.15.4ab
[2] 15-22-0175-00-04ab sensing device
[3] 15-22-0479-04ab More consideration on sensing pulse shape in 802.15.4ab
[4] 15-22-0308-04ab Air-time efficiency improvements
[5] 15-22-0066-02-04ab link budget analysis and CIR reporting for UWB RF sensing
[6] 15-22-0061-00-04ab sensing continued
[7] 15-22-0170-00-04ab discussion on UWB sensing report
[8] 15-22-0291-00-04ab proposal of sensing framework
[9] 15-22-0422-00-04ab UWB sensing scheduling
[10] 15-22-0489-00-04ab UWB sensing sequence selection