## Slide 1
Project: IEEE P802.15 Working Group for Wireless Specialty Networks (WSN)
Submission Title: Expanded HRP channel plan
Submitted: September 14, 2022
Source: Benjamin Rolfe (Blind Creek Associates)
Contact:
E-Mail: ben.rolfe@ieee.org
Voice: NA
Re: Enhanced channel access for UWB
Abstract: This contribution combines the ideas from multiple contributors (see references) to expand the HRP channel plan to include overlapping channel definitions and extension above 10.6 GHz. This contribution includes material from prior submissions by multiple authors.
Purpose: Consideration for inclusion in the draft amendment
Notice: This document has been prepared to assist the IEEE 802. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by 802.15.
Notes: Jul 12, 2010
Page 1

## Slide 2: Expanding and Extending HRP channel plan
Merging of multiple ideas to support sensing, communication, ranging and everything

## Slide 3: Technical Guidance
PAR Objective | Proposed Solution (how addressed)
Safeguards so that the HDR use cases will not cause disruption to low duty-cycle ranging use cases. | 
Interference mitigation techniques to support higher density and higher traffic use cases | 
Other coexistence improvement | 
Backward compatibility with enhanced ranging capable devices (ERDEVs). | 
Improved link budget and/or reduced air-time | 
Additional channels and operating frequencies | Merges the idea of overlapping channels for sensing, and data communications, with the extension of HRP above 10.6 GHz
Improvements to accuracy / precision / reliability and interoperability for high-integrity ranging; | 
Reduce complexity and power consumption; | 
Hybrid operation with narrowband signaling to assist UWB; | 
Enhanced native discovery and connection setup mechanisms; | 
Sensing capabilities to support presence detection and environment mapping; | 
Low-power low-latency streaming | 
higher data-rate streaming allowing at least 50 Mbit/s of throughput. | 
Support for peer-to-peer, peer-to-multi-peer, and station-to-infrastructure protocols; | 
Infrastructure synchronization mechanisms. | 

## Slide 4: Background (1)
Contribution 15-22-0175 explores the use of overlapping channels for sensing
Contribution 15-22-0409 presents the idea of overlapping channels for communications
Contributions 15-22-330 and 15-22-0444 presents the idea of extending the HRP channel plan above 10.6 GHz to provide access new spectrum under consideration or approved in some regions
This contributions combines these into a set of new channels that provides both overlapping channels and extension up to 12 GHz (~)
The TG expressed interest in further developing these ideas

## Slide 5: Background (2)
Overlapping channels are useful for both sensing and communications
Extending the UWB high band above 10.6 is being considered in multiple regulatory:
  For example, ETSI is currently working on an SRDoc (TR 103 750) that considers “(t)echnical characteristics for UWB operation in the frequency band between 8.5 GHz to 10.6 GHz and 10.7 GHz to 12.4 GHz” for various use cases.
802.15.4 is an international standard targeting world-wide adoption
  Where spectrum is available we why not be able to use it
  We need to be forward looking when able

## Slide 6: Background (3)
Considering the standard 499.2 MHz channel widths only
  This seems the most popular in practical use
The actual last channel shown here (extend HRP up to 12.7 GHz) is a guess based on current knowledge and may need to be adjusted
As more develops in regional regulations we may want to adjust and expand
We’ve focused on the high band for now but could also look at low band if there is interest

## Slide 7: The current HRP plan
Slide 7

## Slide 8: Band Allocation – Option 1 No overlap
Slide 8
Channel number | Centre frequency (MHz) | Channel start frequency (MHz) | Channel end frequency (MHz) | Notes
… |  |  |  | Channels currently defined in the IEEE 802.15 standard
13 | 9,484.8 | 9,235.2 | 9,734.4 | 
14 | 9,984.0 | 9,734.4 | 10,233.6 | 
N1 | 10,483.2 | 10,233.6 | 10,732.8 | Option 1: 499.2 MHz channels. Advantage: Ease of implementation. Problem: Transmission in the passive sensing band (10.6-10.7 GHz) will be prohibited in most, if not all, regulatory domains. Solution: Channel N1 would have to be skipped. Even if this is the case, the start frequency of N2 would be too close to 10,700 GHz, resulting in stringent implementation requirements.
N2 | 10,982.4 | 10,732.8 | 11,232.0 | 
N3 | 11,481.6 | 11,232.0 | 11,731.2 | 
N4 | 11,980.8 | 11,731.2 | 12,230.4 | 
N5 | 12,480.0 | 12,230.4 | 12,729.6 | 

## Slide 9: Band Allocation – Option 2 Avoiding Passive Sensing
Slide 9
Channel number | Centre frequency (MHz) | Channel start frequency (MHz) | Channel end frequency (MHz) | Notes
… |  |  |  | Channels currently defined in the IEEE 802.15 standard
14 | 9,984.0 | 9,734.4 | 10,233.6 | 
N1 | 11,107.2 | 10,857.6 | 11,356.8 | Option 2: 1.25x499.2 MHz gap is introduced to protect passive band Problem: Breaking from “multiple of 499.2 MHz” center frequencies increases implementation complexity Advantages: Protection passive band 3 499.2 MHz channels below 12.4/12.7 GHz
N2 | 11,606.4 | 11,356.8 | 11,856.0 | 
N3 | 12,105.6 | 11,856.0 | 12,355.2 | 
N4 | 12,604.8 | 12,355.2 | 12,854.4 | 
Breaking from “multiple of 499.2 MHz” center frequency allocation may lead to better spectrum utilization.
Infinite number of solutions exist. Below is an example of what could be achieved if a gap of 1.25x499.2 MHz is introduced to protect passive band.

## Slide 10: Overlapping Channels
We include overlapping channels at 3 overlaps: 75%, 50% and 25% of the channel width (499.2 MHz)
Presents this overlap over the entire high and extended high band
  This represents what is possible
  Certain regions may need to exclude some channels for various reasons
We propose all new channels are optional

## Slide 11: Other Considerates
We may not want overlapping channels everywhere across the high band for various reasons
  Consideration of coexistence is critical
  Ongoing studies should provide further insights (expecting contributions soon)
For example…
  There is a reason there is a gap between 4 and 6 GHz

## Slide 12: When we put it all together…
It looks something like…

## Slide 13: Overlapping channel plan – 6-10 GHz: adding overlapping channels to HRP channel plan
Channel Number | Center Freq, MHz | Nominal Width, MHz | Start | End
5 | 6489.6 | 499.2 | 6240.0 | 6739.2
15 | 6614.4 | 499.2 | 6364.8 | 6864.0
16 | 6739.2 | 499.2 | 6489.6 | 6988.8
17 | 6864.0 | 499.2 | 6614.4 | 7113.6
6 | 6988.8 | 499.2 | 6739.2 | 7238.4
18 | 7113.6 | 499.2 | 6864.0 | 7363.2
19 | 7238.4 | 499.2 | 6988.8 | 7488.0
20 | 7363.2 | 499.2 | 7113.6 | 7612.8
8 | 7488.0 | 499.2 | 7238.4 | 7737.6
21 | 7612.8 | 499.2 | 7363.2 | 7862.4
22 | 7737.6 | 499.2 | 7488.0 | 7987.2
23 | 7862.4 | 499.2 | 7612.8 | 8112.0
9 | 7987.2 | 499.2 | 7737.6 | 8236.8
24 | 8112.0 | 499.2 | 7862.4 | 8361.6
 | Current Channels
 | 75% overlap new
 | 50% overlap new
 | 25% overlap new
25 | 8236.8 | 499.2 | 7987.2 | 8486.4
26 | 8361.6 | 499.2 | 8112.0 | 8611.2
10 | 8486.4 | 499.2 | 8236.8 | 8736.0
27 | 8611.2 | 499.2 | 8361.6 | 8860.8
28 | 8736.0 | 499.2 | 8486.4 | 8985.6
29 | 8860.8 | 499.2 | 8611.2 | 9110.4
12 | 8985.6 | 499.2 | 8736.0 | 9235.2
30 | 9110.4 | 499.2 | 8860.8 | 9360.0
31 | 9235.2 | 499.2 | 8985.6 | 9484.8
32 | 9360.0 | 499.2 | 9110.4 | 9609.6
13 | 9484.8 | 499.2 | 9235.2 | 9734.4
33 | 9609.6 | 499.2 | 9360.0 | 9859.2
34 | 9734.4 | 499.2 | 9484.8 | 9984.0
35 | 9859.2 | 499.2 | 9609.6 | 10108.8
14 | 9984.0 | 499.2 | 9734.4 | 10233.6
36 | 10108.8 | 499.2 | 9859.2 | 10358.4
37 | 10233.6 | 499.2 | 9984.0 | 10483.2

## Slide 14: Overlapping channel plan – 6-12.7 GHz: linear extension of existing HRP channel plan
Channel Number | Center Freq, MHz | Nominal Width, MHz | Start | End
5 | 6489.6 | 499.2 | 6240.0 | 6739.2
15 | 6614.4 | 499.2 | 6364.8 | 6864.0
16 | 6739.2 | 499.2 | 6489.6 | 6988.8
17 | 6864.0 | 499.2 | 6614.4 | 7113.6
6 | 6988.8 | 499.2 | 6739.2 | 7238.4
18 | 7113.6 | 499.2 | 6864.0 | 7363.2
19 | 7238.4 | 499.2 | 6988.8 | 7488.0
20 | 7363.2 | 499.2 | 7113.6 | 7612.8
8 | 7488.0 | 499.2 | 7238.4 | 7737.6
21 | 7612.8 | 499.2 | 7363.2 | 7862.4
22 | 7737.6 | 499.2 | 7488.0 | 7987.2
23 | 7862.4 | 499.2 | 7612.8 | 8112.0
9 | 7987.2 | 499.2 | 7737.6 | 8236.8
24 | 8112.0 | 499.2 | 7862.4 | 8361.6
38 | 10358.4 | 499.2 | 10108.8 | 10608.0 | 
39 | 10483.2 | 499.2 | 10233.6 | 10732.8 | 
40 | 10608.0 | 499.2 | 10358.4 | 10857.6 | 
41 | 10732.8 | 499.2 | 10483.2 | 10982.4 | 
42 | 10857.6 | 499.2 | 10608.0 | 11107.2 | 
43 | 10982.4 | 499.2 | 10732.8 | 11232.0 | 
44 | 11107.2 | 499.2 | 10857.6 | 11356.8 | 
45 | 11232.0 | 499.2 | 10982.4 | 11481.6 | 
46 | 11356.8 | 499.2 | 11107.2 | 11606.4 | 
47 | 11481.6 | 499.2 | 11232.0 | 11731.2 | 
48 | 11606.4 | 499.2 | 11356.8 | 11856.0 | 
49 | 11731.2 | 499.2 | 11481.6 | 11980.8 | 
50 | 11856.0 | 499.2 | 11606.4 | 12105.6 | 
51 | 11980.8 | 499.2 | 11731.2 | 12230.4 | 
52 | 12105.6 | 499.2 | 11856.0 | 12355.2 | 
53 | 12230.4 | 499.2 | 11980.8 | 12480.0 | 
54 | 12355.2 | 499.2 | 12105.6 | 12604.8 | 
25 | 8236.8 | 499.2 | 7987.2 | 8486.4
26 | 8361.6 | 499.2 | 8112.0 | 8611.2
10 | 8486.4 | 499.2 | 8236.8 | 8736.0
27 | 8611.2 | 499.2 | 8361.6 | 8860.8
28 | 8736.0 | 499.2 | 8486.4 | 8985.6
29 | 8860.8 | 499.2 | 8611.2 | 9110.4
12 | 8985.6 | 499.2 | 8736.0 | 9235.2
30 | 9110.4 | 499.2 | 8860.8 | 9360.0
31 | 9235.2 | 499.2 | 8985.6 | 9484.8
32 | 9360.0 | 499.2 | 9110.4 | 9609.6
13 | 9484.8 | 499.2 | 9235.2 | 9734.4
33 | 9609.6 | 499.2 | 9360.0 | 9859.2
34 | 9734.4 | 499.2 | 9484.8 | 9984.0
35 | 9859.2 | 499.2 | 9609.6 | 10108.8
14 | 9984.0 | 499.2 | 9734.4 | 10233.6
36 | 10108.8 | 499.2 | 9859.2 | 10358.4
37 | 10233.6 | 499.2 | 9984.0 | 10483.2
 | Current
 | 75% overlap new
 | 50% overlap new
 | 25% overlap new
 | New, no overlap

## Slide 15: Overlapping channel plan – 6-12.7 GHz: linear extension of existing HRP channel plan
Channel Number | Center Freq, MHz | Nominal Width, MHz | Start | End
5 | 6489.6 | 499.2 | 6240.0 | 6739.2
15 | 6614.4 | 499.2 | 6364.8 | 6864.0
16 | 6739.2 | 499.2 | 6489.6 | 6988.8
17 | 6864.0 | 499.2 | 6614.4 | 7113.6
6 | 6988.8 | 499.2 | 6739.2 | 7238.4
18 | 7113.6 | 499.2 | 6864.0 | 7363.2
19 | 7238.4 | 499.2 | 6988.8 | 7488.0
20 | 7363.2 | 499.2 | 7113.6 | 7612.8
8 | 7488.0 | 499.2 | 7238.4 | 7737.6
21 | 7612.8 | 499.2 | 7363.2 | 7862.4
22 | 7737.6 | 499.2 | 7488.0 | 7987.2
23 | 7862.4 | 499.2 | 7612.8 | 8112.0
9 | 7987.2 | 499.2 | 7737.6 | 8236.8
24 | 8112.0 | 499.2 | 7862.4 | 8361.6
38 | 10358.4 | 499.2 | 10108.8 | 10608.0 | 
39 | 10483.2 | 499.2 | 10233.6 | 10732.8 | 
40 | 10608.0 | 499.2 | 10358.4 | 10857.6 | 
41 | 10732.8 | 499.2 | 10483.2 | 10982.4 | 
42 | 10857.6 | 499.2 | 10608.0 | 11107.2 | 
43 | 10982.4 | 499.2 | 10732.8 | 11232.0 | 
44 | 11107.2 | 499.2 | 10857.6 | 11356.8 | 
45 | 11232.0 | 499.2 | 10982.4 | 11481.6 | 
46 | 11356.8 | 499.2 | 11107.2 | 11606.4 | 
47 | 11481.6 | 499.2 | 11232.0 | 11731.2 | 
48 | 11606.4 | 499.2 | 11356.8 | 11856.0 | 
49 | 11731.2 | 499.2 | 11481.6 | 11980.8 | 
50 | 11856.0 | 499.2 | 11606.4 | 12105.6 | 
51 | 11980.8 | 499.2 | 11731.2 | 12230.4 | 
52 | 12105.6 | 499.2 | 11856.0 | 12355.2 | 
53 | 12230.4 | 499.2 | 11980.8 | 12480.0 | 
54 | 12355.2 | 499.2 | 12105.6 | 12604.8 | 
25 | 8236.8 | 499.2 | 7987.2 | 8486.4
26 | 8361.6 | 499.2 | 8112.0 | 8611.2
10 | 8486.4 | 499.2 | 8236.8 | 8736.0
27 | 8611.2 | 499.2 | 8361.6 | 8860.8
28 | 8736.0 | 499.2 | 8486.4 | 8985.6
29 | 8860.8 | 499.2 | 8611.2 | 9110.4
12 | 8985.6 | 499.2 | 8736.0 | 9235.2
30 | 9110.4 | 499.2 | 8860.8 | 9360.0
31 | 9235.2 | 499.2 | 8985.6 | 9484.8
32 | 9360.0 | 499.2 | 9110.4 | 9609.6
13 | 9484.8 | 499.2 | 9235.2 | 9734.4
33 | 9609.6 | 499.2 | 9360.0 | 9859.2
34 | 9734.4 | 499.2 | 9484.8 | 9984.0
35 | 9859.2 | 499.2 | 9609.6 | 10108.8
14 | 9984.0 | 499.2 | 9734.4 | 10233.6
36 | 10108.8 | 499.2 | 9859.2 | 10358.4
37 | 10233.6 | 499.2 | 9984.0 | 10483.2
 | Current
 | 75% overlap new
 | 50% overlap new
 | 25% overlap new
 | New, no overlap
Define channels 38 through 40 for use in regions where there may not be conflict wit passive sensing or where other mitigations may be used

## Slide 16: Overlapping channel plan – 6-12.7 GHz: Extension of HRP skipping 10.6-10.7 GHz
Channel Number | Center Freq, MHz | Nominal Width, MHz | Start | End
5 | 6489.6 | 499.2 | 6240.0 | 6739.2
15 | 6614.4 | 499.2 | 6364.8 | 6864.0
16 | 6739.2 | 499.2 | 6489.6 | 6988.8
17 | 6864.0 | 499.2 | 6614.4 | 7113.6
6 | 6988.8 | 499.2 | 6739.2 | 7238.4
18 | 7113.6 | 499.2 | 6864.0 | 7363.2
19 | 7238.4 | 499.2 | 6988.8 | 7488.0
20 | 7363.2 | 499.2 | 7113.6 | 7612.8
8 | 7488.0 | 499.2 | 7238.4 | 7737.6
21 | 7612.8 | 499.2 | 7363.2 | 7862.4
22 | 7737.6 | 499.2 | 7488.0 | 7987.2
23 | 7862.4 | 499.2 | 7612.8 | 8112.0
9 | 7987.2 | 499.2 | 7737.6 | 8236.8
24 | 8112.0 | 499.2 | 7862.4 | 8361.6
25 | 8236.8 | 499.2 | 7987.2 | 8486.4
26 | 8361.6 | 499.2 | 8112.0 | 8611.2
10 | 8486.4 | 499.2 | 8236.8 | 8736.0
27 | 8611.2 | 499.2 | 8361.6 | 8860.8
28 | 8736.0 | 499.2 | 8486.4 | 8985.6
29 | 8860.8 | 499.2 | 8611.2 | 9110.4
12 | 8985.6 | 499.2 | 8736.0 | 9235.2
30 | 9110.4 | 499.2 | 8860.8 | 9360.0
31 | 9235.2 | 499.2 | 8985.6 | 9484.8
32 | 9360.0 | 499.2 | 9110.4 | 9609.6
13 | 9484.8 | 499.2 | 9235.2 | 9734.4
33 | 9609.6 | 499.2 | 9360.0 | 9859.2
34 | 9734.4 | 499.2 | 9484.8 | 9984.0
35 | 9859.2 | 499.2 | 9609.6 | 10108.8
14 | 9984.0 | 499.2 | 9734.4 | 10233.6
36 | 10108.8 | 499.2 | 9859.2 | 10358.4
37 | 10233.6 | 499.2 | 9984.0 | 10483.2
 | Current
 | 75% overlap new
 | 50% overlap new
 | 25% overlap new
 | New, no overlap
38 | 11107.2 | 499.2 | 10857.6 | 11356.8
39 | 11232 | 499.2 | 10982.4 | 11481.6
40 | 11356.8 | 499.2 | 11107.2 | 11606.4
41 | 11481.6 | 499.2 | 11232.0 | 11731.2
42 | 11606.4 | 499.2 | 11356.8 | 11856.0
43 | 11731.2 | 499.2 | 11481.6 | 11980.8
44 | 11856.0 | 499.2 | 11606.4 | 12105.6
45 | 11980.8 | 499.2 | 11731.2 | 12230.4
46 | 12105.6 | 499.2 | 11856.0 | 12355.2
47 | 12230.4 | 499.2 | 11980.8 | 12480.0
48 | 12355.2 | 499.2 | 12105.6 | 12604.8
49 | 12480.0 | 499.2 | 12230.4 | 12729.6
50 | 12604.8 | 499.2 | 12355.2 | 12854.4

## Slide 17: Changes to the Standard
Additional rows to table 10-9 (see next slide)
Possible addition of new mask (to be considered) as discussed in prior contributions

## Slide 18: Add Rows to Table 10-9
Channel number | Center frequency (MHz) | HRP UWB band
16 | 6739.2 | High Band
17 | 6864.0 | 
18 | 7113.6 | 
19 | 7238.4 | 
20 | 7363.2 | 
21 | 7612.8 | 
22 | 7737.6 | 
23 | 7862.4 | 
24 | 8112.0 | 
25 | 8236.8 | 
26 | 8361.6 | 
27 | 8611.2 | 
28 | 8736.0 | 
29 | 8860.8 | 
30 | 9110.4 | 
31 | 9235.2 | 
32 | 9360.0 | 
33 | 9609.6 | 
34 | 9734.4 | 
35 | 9859.2 | 
36 | 10108.8 | 
37 | 10233.6 | 
Channel number | Center frequency (MHz) | HRP UWB band
38 | 11107.2 | Extended High Band
39 | 11232 | 
40 | 11356.8 | 
41 | 11481.6 | 
42 | 11606.4 | 
43 | 11731.2 | 
44 | 11856.0 | 
45 | 11980.8 | 
46 | 12105.6 | 
47 | 12230.4 | 
48 | 12355.2 | 
49 | 12480.0 | 
50 | 12604.8 |