## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Legacy 4z PHR for Several New Data Rates
Date Submitted: October, 2022
Source: Xiliang Luo, Vinod Kristem, Moche Cohen (Apple Inc), Frank Leong, Wolfgang Kuchler, Riku Pirhonen (NXP)
Address: One Apple Park Way, Cupertino, CA 95104, USA
E-Mail: luoxiliang@ieee.org
Abstract: Discuss the legacy PHRs to support several new data rates introduced in 4ab.
Purpose: To provide legacy PHR support for several new data rates in 4ab.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
        doc.: 15-22-0546-01-04ab

## Slide 2
PAR Objective | Proposed Solution (how addressed)
Safeguards so that the high throughput data use cases will not cause significant disruption to low duty-cycle ranging use cases | 
Interference mitigation techniques to support higher density and higher traffic use cases | 
Other coexistence improvement | 
Backward compatibility with enhanced ranging capable devices (ERDEVs) | 
Improved link budget and/or reduced air-time | Support of new lower data rates.
Additional channels and operating frequencies | 
Improvements to accuracy / precision / reliability and interoperability for high-integrity ranging | 
Reduced complexity and power consumption | 
Hybrid operation with narrowband signaling to assist UWB | 
Enhanced native discovery and connection setup mechanisms | 
Sensing capabilities to support presence detection and environment mapping | 
Low-power low-latency streaming | 
Higher data-rate streaming allowing at least 50 Mbit/s of throughput | Support of new higher data rates.
Support for peer-to-peer, peer-to-multi-peer, and station-to-infrastructure protocols | 
Infrastructure synchronization mechanisms | 
        doc.: 15-22-0546-01-04ab

## Slide 3: New Low Rate: 1.95 Mbps, K=7
Symbol structure at 124.8 MHz PRF for both PHR and PSDU
  default: K=7 CC for both PHR and PSDU
Tburst= 64xTchip
Tchip
Guard Interval
Tdsym = 256xTchip
Tburst= 64xTchip
Guard Interval
        doc.: 15-22-0546-01-04ab

## Slide 4: New High Rate: 62.4 Mbps, K=7
Symbol structure at 249.6 MHz PRF for both PHR and PSDU
  default: K=7 CC for both PHR and PSDU
Tburst= 2xTchip
Tchip
Guard Interval
Tdsym = 8xTchip
Tburst= 2xTchip
Guard Interval
        doc.: 15-22-0546-01-04ab

## Slide 5: New High Rate: 124.8 Mbps, K=7
Symbol structure at 249.6 MHz PRF for both PHR and PSDU
  default: K=7 CC for both PHR and PSDU
Tchip
Tburst= Tchip
Guard Interval
Tdsym = 4xTchip
Tburst= Tchip
Guard Interval
        doc.: 15-22-0546-01-04ab

## Slide 6: 4z PHR Field Bits
        doc.: 15-22-0546-01-04ab

## Slide 7: Proposal
  Legacy 4z PHR supports the following new data rates
    1.95, 62.4, and 124.8 Mbps
  When legacy 4z PHR is used with these new data rates
    default: K=7 CC applies to both PHR and PSDU
  For each new data rate, both PHR and PSDU employ the same symbol structure as defined in previous slides
        doc.: 15-22-0546-01-04ab