## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Evaluation of IEEE 802.15.6ma Ultra-wideband Physical Layer Utilizing Super Orthogonal Convolutional Code]
Date Submitted: [14 May 2024]
Source: [Kento Takabayashi1, Ryuji Kohno2,3 ] [1;Toyo University, 2;Yokohama National University, 3;YRP International Alliance Institute(YRP-IAI)]
Address [1: 2100 Kujirai, Kawagoe, Saitama, Japan 351-8585, Japan 719-1197,
2; 79-5 Tokiwadai, Hodogaya-ku, Yokohama, Japan 240-8501,
3; YRP1 Blg., 3-4 HikarinoOka, Yokosuka-City, Kanagawa, 239-0847 Japan]
Voice:[1; +81-866-94-2104, 2: +81-90-5408-0611],
Email:[1: takabayashi.kento.xp@gmail.com, 2:kohno@ynu.ac.jp]
Re: []
Abstract: [The performance of an IEEE 802.15.6ma ultra-wideband physical layer utilizing super orthogonal convolutional codes is evaluated. These slides may offer opportunity to discuss on revision for a dependable physical layer technology of a new standard IEEE802.15.6ma.] Purpose: [The discussion will lead definition and requirement of current ongoing research and development on dependable wireless networks.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein. Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
Notes: doc.: IEEE 802.15-09-0117-00-0007
<month year>

## Slide 2
Evaluation of IEEE 802.15.6ma Ultra-wideband Physical Layer Utilizing Super Orthogonal Convolutional Code
May 2024,
Hybrid Session ,
Marriott Warsaw - Warsaw, Poland
Kento Takabayashi1, Ryuji Kohno2,3
1. Toyo University, Japan
2. Yokohama National University, Japan
3. YRP International Alliance Institute, Japan

## Slide 3: Motivation and Aim of study
UWB is a promising technology that may satisfy the requirements of IoMT
IEEE 802.15.6 UWB PHY has limited transmission output and requires to ensure dependability
New consideration is given to the application of Super Orthogonal Convolutional Codes (SOCC) as a technique for improving dependability for higher priority case
We perform evaluation when SOCC is applied at the IEEE 802.15.6 UWB PHY, and confirm the effectiveness of these combinations
Notes: SOCCs have attracted attention as error correction codes for code division multiple access (CDMA) using the spread spectrum
Therefore, SOCCs are considered to be compatible with the UWB, as they use a very wide bandwidth

## Slide 4: SOCC
Fig. SOCC encoder
SOCC is a kind of orthogonal convolutional code of very low coding rate
The encoder is composed of K length shift registers (constraint length) and a block orthogonal (Hadamard) encoder
The coding rate is given by
The decoder uses the Viterbi algorithm
Notes: The inner (K- 2) bit memories are mapped into one Walsh sequence of length (two to the power of K-2)
The two outer bits are added to each binary number of the selected Walsh sequence by exclusive OR
One divided by two to the power of K-2
The inner (K- 2) bit memories are mapped into one Walsh sequence of length 2^(𝐾−2) (two to the power of K-2)
The two outer bits are added to each binary number of the selected Walsh sequence by exclusive OR
One divided by two to the power of K-2

## Slide 5: Bit erasure channel
0 1 1 0 0 1 0 0 1・・・0 1 1 1 ✕ ✕ ✕ ✕ ✕ ✕ ・・・0 1 1 0 0 0 1 1
Consecutive bit erasures
Bit erasure channel is assumed, which simulate asynchronous interference from another system
It is assumed that consecutive bit erasures of up to % of the length of PSDU occur
is uniformly distributed in the interval [0 ]

## Slide 6: Evaluation
Channel model | AWGN, Bit erasure
Bandwidth () | 499.2 MHz
Center Frequency | 3993.6 MHz
Modulation | BPSK
Transmission power () | 0 dBm
Thermal noise density () | -174 dBm/Hz
Implementation losses () | 3 dB
Receiver noise figure () | 5 dB
FEC | IEEE802.15.4ab BCC, LDPC (R=1/2) SOCC (K=3~6)
Decoding algorism | SOVA (BCC, SOCC), Belief propagation (LDPC)
Communication distance () | 0.5 m
Pulse waveform duration () | 2.003 ns
PSDU length () | 1296 bits
Maximum erasure ratio () | 0.001, 0.01, 0.05, 0.1
Pulse option | Single pulse option, burst pulse option
Channel model | AWGN, Bit erasure
 | 499.2 MHz
Center Frequency | 3993.6 MHz
Modulation | BPSK
 | -174 dBm/Hz
 | 3 dB
 | 5 dB
FEC | IEEE802.15.4ab BCC, LDPC (R=1/2) SOCC (K=3~6)
Decoding algorism | SOVA (BCC, SOCC), Belief propagation (LDPC)
 | 0.5 m
 | 2.003 ns
 | 1296 bits
 | 0.001, 0.01, 0.05, 0.1
Pulse option | Single pulse option, burst pulse option
4. Evaluation
Table. Simulation Parameters

## Slide 7: Results
Packet error ratio in the case of 15.4ab BCC, LDPC, and SOCC

## Slide 8: Results
Packet error ratio in the case of 15.4ab BCC, LDPC, and SOCC with and without random interleaver,

## Slide 9: Conclusion
Numerical results showed that SOCC achieved very strong performance under conditions with few consecutive bit erasures
However, an error floor occurred as consecutive bit erasures increased in the case of BCC and SOCC
On the other hand, there was no significant change in performance as consecutive bit erasures increased in the case of LDPC
It is considered that applying concatenation with burst error correction codes, interleaver and so on in the case of BCC and SOCC

## Slide 10: Reference
Kento Takabayashi, Hirokazu Tanaka, Katsumi Sakakibara, "Evaluation of Wireless Body Area Network Utilizing Super Orthogonal Convolutional Code," in Proceedings of 2019 International Symposium on Intelligent Signal Processing and Communication Systems (ISPACS 2019), Beitou, Taipei, Taiwan, pp.1-2, Dec. 2019.
Kento Takabayashi, Hirokazu Tanaka, Katsumi Sakakibara, "Toward Dependable Internet of Medical Things: IEEE 802.15.6 Ultra-Wideband Physical Layer Utilizing Superorthogonal Convolutional Code," Sensors, 2022, vol. 22, no. 6, 2172, Mar. 2022.

## Slide 11
11
Thank you for your attention ! ! !
* This research was funded by JSPS Grant-in-Aid for Early-Career Scientists Grant Number JP20K14737

## Slide 12: 2. IEEE 802.15.6 UWB PHY
Pulse option
Single pulse option: A single pulse transmitted per symbol
Burst pulse option: A concatenation of pulses transmitted per symbol
  This option improves the received power by correlating multiple pulses while decreasing the uncoded bit rate as increases
Transmitting signal
Fig. Signal transmission example where the burst pulse option is used

## Slide 13: 2. IEEE 802.15.6 UWB PHY
frequency
bandwidth 499.2 MHz
3993.6 MHz
7987.2 MHz
・・・
Frequency spectrum
The UWB band is divided into two band groups: low band (channel 0-2) and high band (channel 3-10) which are divided into operating frequency channels with 499.2 MHz bandwidth
Orange colors are mandatory channels (Low Band: channel 1，High Band: channel 6)
The power spectral density emission limit is -41.3 dBm/MHz which is very low
0
1
2
Low Band
・・・
・・・
3
6
10
High Band

## Slide 14: 2. IEEE 802.15.6 UWB PHY
Frame format
SHR is divided into two parts: The first part is the preamble, intended for timing synchronization, packet detection, and carrier frequency offset recovery, and The second part is the start-of-frame delimiter (SFD) for frame synchronization
The PHR contains information about the data rate of the PSDU, length of the medium access control (MAC) frame body, pulse shape, burst mode, and so on
The PSDU contains the MAC protocol data unit (MPDU)

## Slide 15: 2. IEEE 802.15.6 UWB PHY
is the power of two
As increases, a uncoded bit rate decreases
Uncoded bit rate and received signal to noise ratio (SNR) are in a trade-off relationship

## Slide 16: Cross-layer Evaluation
PSDU length and Time slot length is fixed
  The smaller coding rate is, the shorter information bits including PSDU is
The ratio of each link type is as follows: LD:MD:HD = 3:2:1
The ratio of the lengths of MAP and RAP is as follows: MAP:RAP = 4:1
The same number of time slots are assigned to each sensor in MAP
PHY packet errors at each link type refer to previous results

## Slide 17: Cross-layer Evaluation
The number of sensors | 6
The number of hub | 1
Data rate of each sensor () | 100, 200 Kbps
User priority of each sensor data | 5
Uncoded symbol rate | 7.8 Msps
SHR length | 315 bits
PHR length | 40 bits
PSDU length () | 155 bytes
ACK length () | 155 bits
Coding rate | 1, 0.8 (RS), 1/2, 1/4, 1/8 (SOCC)
Beason period | 250 ms
Time slot length | 170 μs
The maximum number of retransmissions | 4
The number of sensors | 6
The number of hub | 1
 | 100, 200 Kbps
User priority of each sensor data | 5
Uncoded symbol rate | 7.8 Msps
SHR length | 315 bits
PHR length | 40 bits
 | 155 bytes
 | 155 bits
Coding rate | 1, 0.8 (RS), 1/2, 1/4, 1/8 (SOCC)
Beason period | 250 ms
Time slot length | 170 μs
The maximum number of retransmissions | 4

## Slide 18: Cross-layer Evaluation
(a)
Average successful transmission ratio
(a) is 100 Kbps
(b) is 200 Kbps
1~5: The Same coding rate for all links
1: No encoding case (R=1)
2: RS encoding (R=0.8)
3: SOCC encoding (R=1/2)
4: SOCC encoding (R=1/4)
5: SOCC encoding (R=1/8)
6: Change coding rate according to link
100Kbps: LD: 0.8, 0.8, 0.8, MD: 1/2, 1/2, HD: 1/4
200Kbps: LD: 1, 1, 0.8, MD: 0.8, 0.8, HD: 1/2
(b)

## Slide 19: Cross-layer Evaluation
(a)
Average Latency [ms]
(a) is 100 Kbps
(b) is 200 Kbps
1~5: The Same coding rate for all links
1: No encoding case (R=1)
2: RS encoding (R=0.8)
3: SOCC encoding (R=1/2)
4: SOCC encoding (R=1/4)
5: SOCC encoding (R=1/8)
6: Change coding rate according to link
100Kbps: LD: 0.8, 0.8, 0.8, MD: 1/2, 1/2, HD: 1/4
200Kbps: LD: 1, 1, 0.8, MD: 0.8, 0.8, HD: 1/2
(b)

## Slide 20: Cross-layer Evaluation
(a)
Network throughput [Kbps]
(a) is 100 Kbps
(b) is 200 Kbps
1~5: The Same coding rate for all links
1: No encoding case (R=1)
2: RS encoding (R=0.8)
3: SOCC encoding (R=1/2)
4: SOCC encoding (R=1/4)
5: SOCC encoding (R=1/8)
6: Change coding rate according to link
100Kbps: LD: 0.8, 0.8, 0.8, MD: 1/2, 1/2, HD: 1/4
200Kbps: LD: 1, 1, 0.8, MD: 0.8, 0.8, HD: 1/2
(b)

## Slide 21: Cross-layer Evaluation - Discussion
In the same coding rate cases for all links, each performance deteriorates when the coding rate is too low
  In case that is 100 Kbps, that is more than SOCC coding rate 1/8
  In case that is 200 Kbps, that is more than SOCC coding rate 1/4
  The reason is that it increases the number of packets transmitted out to the network to transmit the same amount of data due to fixed PSDU and time slot length
  Therefore, it increases the number of packet collisions in RAP and waiting packets in queue from the above reason
Each performance can be balanced by adjusting the coding rate according to the link type
  Because of the same number of time slots assigned to each sensor in MAP, the best performance are not achieved
  It is necessary to adjust the number of allocated slots in the MAP according to the coding rate