## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Study on polarized THz-wave scattering from slightly rough surfaces
Date Submitted: 12 November 2022
Source: Tetsuya Kawanishi, Riku Yoshino, Toshiya Yoshida, Waseda University
3-4-1, Okubo, Shinjuku-ku, Tokyo 169-8555, Japan
Voice: +81 3 5286 3386, E-Mail: kawanishi@waseda.jp
Keizo Inagaki, Iwao Hosako, National Institute of Information and Communications Technology (NICT)
4-2-1, Nukui-Kitamachi, Koganei, Tokyo 184-8795, Japan, E-Mail: hosako@nict.go.jp
Re: n/a
Abstract: This document overviews of polarized THz-wave scattering from slightly rough surfaces and its impact on interference. Slightly rough surfaces such as wooden tables and walls would scatter THz waves with particular polarization distribution. The scattered wave would induce interference between short distance THz links.
Purpose: Information document for IEEE 802.15 SC THz
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Study on polarized THz-wave scattering from slightly rough surfaces
Tetsuya Kawanishi, Riku Yoshino, Toshiya Yoshida,
Keizo Inagaki and Iwao Hosako
Waseda University, Japan
National Institute of Information and Communications Technology (NICT), Japan
November 2022

## Slide 3: Outline of this contribution
Basics on a model of THz-wave scattering from slightly rough surfaces
Examples of experimental and numerical results
Potential interference induced by scattering

## Slide 4: THz-wave scattering from slightly rough surfaces
Microwave
THz-wave
Typical roughness of polished wooden surface is 80 um.
E. Csanády et al., Surface Roughness of Wood. In: Quality of Machined Wood Surfaces, Springer 2015.
Tetsuya Kawanishi, Waseda Univ., et al

## Slide 5: Model of electromagnetic wave scattering
A stochastic functional approach provides mathematical models for EM wave scattering by 2D slightly random surfaces.
Scattering distributions largely depend on polarization.
Wiener kernels offer concise mathematical expressions.
Surfaces are described by Gaussian distribution stochastic functions whose spectra are Gaussian.
Parameters of rough surface
Refractive index
T. Kawanishi, et al.: “Scattering of electromagnetic wave from a slightly dielectric surface--Yoneda peak and Brewster angle incoherent scattering--,” Waves in Random Media 7 (1997) 351

## Slide 6: Scattering distribution of TE polarization incidence
TE-polarized scattering
TM-polarized scattering
Wavenumber in the air
R. Yoshino, et al.: “Modeling and evaluation of millimeter wave scattering from minimally rough surfaces on stones,” IEICE ELEX 19 (2022) 20220257.

## Slide 7: Scattering distribution of TE polarization incidence
Wavenumber in the air
TE-polarized scattering
TM-polarized scattering

## Slide 8: Millimeter-wave scattering measurement (75-100GHz)
Mable stone (9cm x 9cm)
Tetsuya Kawanishi, Waseda Univ., et al

## Slide 9: Comparison between numerical and experimental results
Theory
Scattered wave
-36.5dB ~ -56.5dB
-40dB ~ -60dB
Experiment
Tetsuya Kawanishi, Waseda Univ., et al

## Slide 10: Wooden rough surface sample
Surface parameter | 
Refractive index | 1.47 (300GHz)
 | 135.57[μm]
 | 66.99[μm]
Surface parameter | 
 | 1.47 (300GHz)
 | 135.57[μm]
 | 66.99[μm]
Tetsuya Kawanishi, Waseda Univ., et al

## Slide 11: Roughness and correlation length
Tetsuya Kawanishi, Waseda Univ., et al

## Slide 12: Scattered wave distribution TE polarized incidence
Tetsuya Kawanishi, Waseda Univ., et al

## Slide 13: Scattered wave distribution TM polarized incidence
Tetsuya Kawanishi, Waseda Univ., et al

## Slide 14: Total scattered wave power 60-degree incidence
Reflectivity 0.4075
Transmittance 0.5925
TE-polarized incidence 3.63% (-14.4dB)
In Medium 1 TE=>TE 0.57% TE=>TM 0.47%
In Medium 2 TE=>TE 1.82% TE=>TM 0.77%
TM-polarized incidence 4.13% (-13.8dB)
In Medium 1 TM=>TE 0.40% TM=>TM 0.43%
In Medium 2 TM=>TE 1.12% TM=>TM 2.18%
Medium 1 (Air)
Medium 2 (Wood)
Tetsuya Kawanishi, Waseda Univ., et al

## Slide 15: Issues on interference induced by scattering
Short distance THz links close to surfaces would have interference issues caused by scattered waves.
Tetsuya Kawanishi, Waseda Univ., et al
Notes: The logical step would be to
Design a MPC estimation algorithm and compare how it performs with existing algorithm and our manual approach.
Model the stochastic processes in signal propagation at the band of interest (300 GHz). Also find out the intra-cluster parameters.
Develop channel model suited to THz band propagation

## Slide 16: Future works
Study on interference mitigation based on scattering distribution and polarization dependence
  45-deg linear polarization shows asymmetric scattering
Explore materials or surfaces which suppress undesired scattering
Tetsuya Kawanishi, Waseda Univ., et al
T. Kawanishi, et al.: “Polarization characteristics of an electromagnetic wave scattered from a slightly random surface: +45° polarized incidence,” Waves in Random Media 7 (1997) 593
Notes: The logical step would be to
Design a MPC estimation algorithm and compare how it performs with existing algorithm and our manual approach.
Model the stochastic processes in signal propagation at the band of interest (300 GHz). Also find out the intra-cluster parameters.
Develop channel model suited to THz band propagation

## Slide 17: Summary
Stochastic functional approach would be applicable to THz-wave scattering from wood and stone surfaces.
Scattered wave distribution shows large polarization dependence.
Total scattered wave from a wood sample was -14dB.
Tetsuya Kawanishi, Waseda Univ., et al
Notes: With the current dataset and its subsequent analysis the following inferences can be drawn
High K-factor indicates LoS dominant path but as observed from ray-tracing triple bounce path with significant power exists in most of the positions
The impulse like nature of the PDP indicates less number of MPCs per cluster
Further extensive campaign is required to make conclusive statements about the cross-correlation between different large scale parameters