## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: RSF and MMRS in Multi-Millisecond UWB
Date Submitted: November 10, 2022
Source: Xiliang Luo, Vinod Kristem, Moche Cohen (Apple), Michael McLaughlin, Billy Verso, Igor Dotlic, Carl Murray, Jarek Niewczas (Qorvo), Frank Leong, Wolfgang Kuchler, Riku Pirhonen (NXP), Chenchen Liu, Bin Qian, Lei Huang, and David Xun Yang (Huawei)
Address: One Apple Park Way, Cupertino, CA 95104, USA
E-Mails: xiliang_luo@apple.com, Michael.McLaughlin@qorvo.com, frank.leong@nxp.com, qianbin14@huawei.com
Abstract: A way forward on the ranging sequences for MMS UWB.
Purpose: Converge on the ranging sequences for MMS UWB.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
        doc.: 15-22-0570-00-04ab

## Slide 2
PAR Objective | Proposed Solution (how addressed)
Safeguards so that the high throughput data use cases will not cause significant disruption to low duty-cycle ranging use cases | 
Interference mitigation techniques to support higher density and higher traffic use cases | Periodicity-Division Multiple Access
Other coexistence improvement | 
Backward compatibility with enhanced ranging capable devices (ERDEVs) | 
Improved link budget and/or reduced air-time | MMS
Additional channels and operating frequencies | 
Improvements to accuracy / precision / reliability and interoperability for high-integrity ranging | MMS for high-integrity ranging
Reduced complexity and power consumption | 
Hybrid operation with narrowband signaling to assist UWB | NBA-MMS
Enhanced native discovery and connection setup mechanisms | 
Sensing capabilities to support presence detection and environment mapping | 
Low-power low-latency streaming | 
Higher data-rate streaming allowing at least 50 Mbit/s of throughput | 
Support for peer-to-peer, peer-to-multi-peer, and station-to-infrastructure protocols | 
Infrastructure synchronization mechanisms | 
        doc.: 15-22-0570-00-04ab

## Slide 3: Definitions
A multi-millisecond (MMS) UWB packet consists of a number of fragments of one of the following types
  Ranging sequence fragment (RSF)
    carries multi-millisecond ranging sequence (MMRS)
      good cross-correlation over long accumulation
      a large set of available sequences
  Ranging integrity fragment (RIF)
    carries 4z waveform for ranging integrity
      e.g. STS waveform
        doc.: 15-22-0570-00-04ab

## Slide 4: Illustration of MMS Packets
NB
OR
RSF
1
RSF
2
RSF
X
RIF
1
RIF
2
RIF
Y
1~2 ms
1ms
(1+Z) ms
1ms
(X-2) ms
(Y-2) ms
UWB
Z = {0, 1}
MMRS
MMRS
STS
MMRS
MMRS
STS
Same sequences
Different STS sequences for integrity
S
Y
N
C
S
FD
        doc.: 15-22-0570-00-04ab

## Slide 5: Way Forward on MMRS
  16 length-128 multi-millisecond ranging sequences (MMRS) based on complementary sets are introduced for MMS UWB
    more than 30dB cross-correlation suppression could be realized with zero relative CFO
    further cross-correlation suppression as relative CFO gets larger
    periodicity division multiple access through flexible & natural insertion of gaps
      MMRS without gap before spreading: [A, B], where A and B are of length 64
      MMRS with gap before spreading: [A, G, B, G], where the gap G contains 0~64 zeros
    spreading factor L=4  mean PRF from 62.4 to 124.8 MHz
    a proposed set of 16 MMRSs are listed in the following slide
  MMRS based on 4z Ipatov sequences of length 91 or 127
    spreading factor L=4
    8 length-91 Ipatov sequences for mean PRF of 111.09 MHz
    16 length-127 Ipatov sequences for mean PRF of 62.89 MHz
        doc.: 15-22-0570-00-04ab

## Slide 6: 16 MMRSs based on Complementary Sets
+-++-++++-+++---+-++-+++-+---++++-++-++++-+++----+--+---+-+++--- +-++-++++-+++---+-++-+++-+---+++-+--+----+---++++-++-+++-+---+++
+--++--+++----+++-+--+-++++++++++-+-+-+-++++----+--+-++-++--++-- +--++--+++----+++-+--+-+++++++++-+-+-+-+----++++-++-+--+--++--++
+--++--+-+-++-+-++++++++--++++--+--+-++--+-+-+-+++++------++--++ +--++--+-+-++-+-++++++++--++++---++-+--++-+-+-+-----++++++--++--
+---+----+---+--+----++++-++-+--+----+++-+--+-+++---+---+-+++-++ +---+----+---+--+----++++-++-+---++++---+-++-+---+++-+++-+---+--
+----++++-+++-+++---+---+-++-+--+----++++-+++-++-+++-+++-+--+-++ +----++++-+++-+++---+---+-++-+---++++----+---+--+---+---+-++-+--
++--+-+------++---++-+-+-----++---++-+-++++++--+--++-+-+-----++- ++--+-+------++---++-+-+-----++-++--+-+------++-++--+-+-+++++--+
------+++-+--++-++--++++-++-+-+-------+++-+--++---++----+--+-+-+ ++++++---+-++--+--++----+--+-+-+------+++-+--++---++----+--+-+-+
-----++------++---++-+-+++--+-+------++-+++++--+--++-+-+--++-+-+ +++++--++++++--+++--+-+---++-+-+-----++-+++++--+--++-+-+--++-+-+
--++-++------+-+++---++-----+-+------+-+--++-++-++++-+-+--+++--+ ++--+--++++++-+---+++--+++++-+-+-----+-+--++-++-++++-+-+--+++--+
-+---+---+++-++++-++-+---++++----+--+-++-++++---+-+++-++-+++-+++ +-+++-+++---+----+--+-+++----+++-+--+-++-++++---+-+++-++-+++-+++
-+---+--+-++-+---++++---+---+----+---+---+--+-++-++++----+++-+++ +-+++-++-+--+-+++----+++-+++-+++-+---+---+--+-++-++++----+++-+++
-+-++-+----------++--++---++++---++-+--+--++--++-+-+-+-+----++++ +-+--+-++++++++++--++--+++----++-++-+--+--++--++-+-+-+-+----++++
-++--++-++----++-+-++-+-+++++++++-+-+-+-----+++++--+-++---++--++ +--++--+--++++--+-+--+-+--------+-+-+-+-----+++++--+-++---++--++
+--++--+-+-++-+-++++++++--++++--+--+-++--+-+-+-+++++------++--++ -++--++-+-+--+-+--------++----+++--+-++--+-+-+-+++++------++--++
+--+----+--+-----+-+++--+-+---++-++-+++++--+----+-+---+++-+---++ -++-++++-++-+++++-+---++-+-+++---++-+++++--+----+-+---+++-+---++
++---+-+----+--+--+++-+-----+--+--+++-+-++++-++---+++-+-----+--+ --+++-+-++++-++-++---+-+++++-++---+++-+-++++-++---+++-+-----+--+
        doc.: 15-22-0570-00-04ab

## Slide 7: Appendix
        doc.: 15-22-0570-00-04ab

## Slide 8
+
+
X
-
+
+
+
X
-
+
+
+
X
-
+
length
#Stages:
Delay Vector: , ,
Seed:
Time Reversal Vector: ,
  when . When , is time-reversed in the final Golay pair, i.e.,
  when . When , is time-reversed in the final Golay pair, i.e.,
Final Golay pair as MMRS: ,
Note-1: the above structure could be exploited for efficient construction.
Note-2: we propose to specify the exact bit patterns in the 16 MMRSs explicitly
MMRS Generation from Seeds
        doc.: 15-22-0570-00-04ab

## Slide 9: Seeds for the 16 MMRSs
Sequence # | Seed | Delay Vector: D | Time Reversal Vector:[Ra, Rb]
1 | 58 | [1 2 4 8 16 32] | [0, 0]
2 | 46 | [1 8 4 16 2 32] | [0, 0]
3 | 50 | [1 16 2 8 4 32] | [0, 0]
4 | 56 | [1 2 8 16 4 32] | [0, 0]
5 | 52 | [1 2 8 4 16 32] | [0, 0]
6 | 3 | [1 4 2 8 16 32] | [0, 0]
7 | 12 | [32 16 2 4 8 1] | [1, 0]
8 | 30 | [32 8 16 2 4 1] | [1, 0]
9 | 20 | [32 2 8 16 4 1] | [1, 0]
10 | 58 | [32 4 16 8 2 1] | [1, 0]
11 | 60 | [32 8 4 16 2 1] | [1, 0]
12 | 54 | [32 2 16 4 8 1] | [1, 0]
13 | 45 | [32 2 16 4 8 1] | [1, 0]
14 | 19 | [32 4 8 2 16 1] | [0, 1]
15 | 2 | [32 8 16 2 4 1] | [0, 1]
16 | 32 | [32 16 8 2 4 1] | [0, 1]
        doc.: 15-22-0570-00-04ab

## Slide 10
Worst-case cross correlation
is below -12dB (without gaps)
Cross-Correlation Peaks among 16 MMRS Sequences
        doc.: 15-22-0570-00-04ab

## Slide 11
Multiple Interpretations: 2x64 Golay  64x2 CZC
        doc.: 15-22-0570-00-04ab

## Slide 12
16 good candidates for the number of zeros in the gap G (before spreading)
  0 3 5 7 9 15 19 21 25 33 37 39 43 45 49 57
  The period of one MMRS including the gap (before spreading) is one of the following
    128 134 138 142 146 158 166 170 178 194 202 206 214 218 226 242
    the GCD between each two periods is 2
    the GCD between each of these periods and 4z Ipatov period is 1
Network operation example 1: 16 Tx-Rx pairs nearby
  each pair utilizes one different gap size from the above set
    interference suppression is maximized between any two Tx-Rx pairs
Network operation example 2: 2 Tx-Rx pairs nearby
  gap sizes: 0<=g1,g2<=64 are good as long as GCD(128+2g1,128+2g2)=2
    mutual interference suppression is maximized
Considerations on the Gap Size for MMRS
        doc.: 15-22-0570-00-04ab