## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Channels for Frequency Stitching
Date Submitted: November 8, 2022
Source: Steve Shellhammer, Pooria Pakrooh, Bin Tian, and Koorosh Akhavan (Qualcomm)
E-Mail:{sshellha, ppakrooh, btian, kakhavan}@qti.qualcomm.com
Abstract: We propose channels for Frequency Stitching in RF Sensing.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the authoring individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The authors(s) reserve(s) the right to add, amend or withdraw material contained herein.

## Slide 2
PAR Objective | Proposed Solution (how addressed)
Safeguards so that the high throughput data use cases will not cause significant disruption to low duty-cycle ranging use cases | 
Interference mitigation techniques to support higher density and higher traffic use cases | 
Other coexistence improvement | 
Backward compatibility with enhanced ranging capable devices (ERDEVs) | 
Improved link budget and/or reduced air-time | 
Additional channels and operating frequencies | 
Improvements to accuracy / precision / reliability and interoperability for high-integrity ranging | 
Reduced complexity and power consumption | 
Hybrid operation with narrowband signaling to assist UWB | 
Enhanced native discovery and connection setup mechanisms | 
Sensing capabilities to support presence detection and environment mapping | We propose a channel for Frequency Stitching for RF Sensing.
Low-power low-latency streaming | 
Higher data-rate streaming allowing at least 50 Mbit/s of throughput | 
Support for peer-to-peer, peer-to-multi-peer, and station-to-infrastructure protocols | 
Infrastructure synchronization mechanisms | 

## Slide 3: Background
To increase the bandwidth for RF Sensing a proposal for Frequency Stitching was made in [1, 2]
This allows for increased bandwidth by stitching together frequency overlapping frequency segments
Here is a figure from [2]
Frequency
CM
Time
SF
SF
SF
Control on Main UWB Channel
CM = Control Message SF = Sensing Fragment
The sensing fragments (SFs) overlap sufficiently so that it is possible to stitch them together and increase the effective bandwidth
The required total bandwidth is larger than the 499.2 MHz channel bandwidth

## Slide 4: Background (cont.)
To address the wider bandwidth, it was proposed in [3] to support overlapping channels
Channel Number | Center Freq, MHz | Nominal Width, MHz | Start | End
5 | 6489.6 | 499.2 | 6240.0 | 6739.2
15 | 6614.4 | 499.2 | 6364.8 | 6864.0
16 | 6739.2 | 499.2 | 6489.6 | 6988.8
17 | 6864.0 | 499.2 | 6614.4 | 7113.6
6 | 6988.8 | 499.2 | 6739.2 | 7238.4
18 | 7113.6 | 499.2 | 6864.0 | 7363.2
19 | 7238.4 | 499.2 | 6988.8 | 7488.0
20 | 7363.2 | 499.2 | 7113.6 | 7612.8
8 | 7488.0 | 499.2 | 7238.4 | 7737.6
21 | 7612.8 | 499.2 | 7363.2 | 7862.4
22 | 7737.6 | 499.2 | 7488.0 | 7987.2
23 | 7862.4 | 499.2 | 7612.8 | 8112.0
9 | 7987.2 | 499.2 | 7737.6 | 8236.8
24 | 8112.0 | 499.2 | 7862.4 | 8361.6
 | Current Channels
 | 75% overlap new
 | 50% overlap new
 | 25% overlap new
25 | 8236.8 | 499.2 | 7987.2 | 8486.4
26 | 8361.6 | 499.2 | 8112.0 | 8611.2
10 | 8486.4 | 499.2 | 8236.8 | 8736.0
27 | 8611.2 | 499.2 | 8361.6 | 8860.8
28 | 8736.0 | 499.2 | 8486.4 | 8985.6
29 | 8860.8 | 499.2 | 8611.2 | 9110.4
12 | 8985.6 | 499.2 | 8736.0 | 9235.2
30 | 9110.4 | 499.2 | 8860.8 | 9360.0
31 | 9235.2 | 499.2 | 8985.6 | 9484.8
32 | 9360.0 | 499.2 | 9110.4 | 9609.6
13 | 9484.8 | 499.2 | 9235.2 | 9734.4
33 | 9609.6 | 499.2 | 9360.0 | 9859.2
34 | 9734.4 | 499.2 | 9484.8 | 9984.0
35 | 9859.2 | 499.2 | 9609.6 | 10108.8
14 | 9984.0 | 499.2 | 9734.4 | 10233.6
36 | 10108.8 | 499.2 | 9859.2 | 10358.4
37 | 10233.6 | 499.2 | 9984.0 | 10483.2

## Slide 5: Alternative Proposal
Overlapping channels for communications can make sharing the spectrum difficult
The probability of packet collision increases with overlapping channels
In 802.11 within the 2.4 GHz the industry ultimately focused on the non-overlapping channels (e.g., Channels 1, 6 and 11)
However, we do need wider channels for Frequency Stitching of Sensing Fragments
There currently exists several wider channels which can support Frequency Stitching

## Slide 6: Current Channel Plan (From [3])
Channel width more than double 499.2 MHz
Can support Frequency Stitching for RF Sensing

## Slide 7: Low Band Channels

## Slide 8: High Band Channels

## Slide 9: Discussion on Channels
Additional Info
We expect Channels 5, 6, 8, and 9 to be widely supported
Observations
The wideband channels overlap all the 499.2 MHz channels
We propose supporting Frequency Stitching in Channel 4 (Low Band) and Channel 15 (High Band)

## Slide 10: Summary
As an alternative to overlapping frequency channels, we proposed supporting Frequency Stitching in the wider channels already defined
  Channel 4 (Low Band) and Channel 15 (High Band)
This avoids the overlapping channels for communications which can make sharing of the spectrum difficult

## Slide 11: References
Frank Leong, Wolfgang Küchler, Riku Pirhonen, “Sensing Continued,” IEEE 802.15/22-061r0, January 2022
Frank Leong, Wolfgang Küchler, Riku Pirhonen, “UWB Sensing - Scheduling,” IEEE 802.15/22-422r0, July 2022
Ben Rolfe, “Expanded HRP channel plan,” IEEE 802.15-22/520r1, September 2022