## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: One-to-Many Ranging using NBA-MMS
Date Submitted: Nov 14, 2022
Source: Jinjing Jiang, Robert Golshan, Alexander Krebs, Yong Liu, Xiliang Luo, Santhosh Kumar Mani, SK Yong (Apple Inc.)
Address: One Apple Park Way, Cupertino, CA 95104, USA
E-Mail: jinjing@apple.com
Abstract: Basic frame exchange sequences for one-to-many ranging using NBA-MMS.
Purpose: Extend NBA-MMS usage to one-to-many use cases.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
PAR Objective | Proposed Solution (how addressed)
Safeguards so that the high throughput data use cases will not cause significant disruption to low duty-cycle ranging use cases | 
Interference mitigation techniques to support higher density and higher traffic use cases | 
Other coexistence improvement | 
Backward compatibility with enhanced ranging capable devices (ERDEVs) | 
Improved link budget and/or reduced air-time | 
Additional channels and operating frequencies | 
Improvements to accuracy / precision / reliability and interoperability for high-integrity ranging | 
Reduced complexity and power consumption | 
Hybrid operation with narrowband signaling to assist UWB | 
Enhanced native discovery and connection setup mechanisms | 
Sensing capabilities to support presence detection and environment mapping | 
Low-power low-latency streaming | 
Higher data-rate streaming allowing at least 50 Mbit/s of throughput | 
Support for peer-to-peer, peer-to-multi-peer, and station-to-infrastructure protocols | One-to-many ranging utilizing NBA-MMS mode
Infrastructure synchronization mechanisms | 

## Slide 3: Recap of One-to-One Ranging

## Slide 4: Concatenate “Many” Responders
Access Slot is a chunk of continuous ranging slots that are used between the Initiator and a Responder
Responder 1
Responder 2

## Slide 5: Control/Initialization/Poll Message
Define the one-to-many session
  Time scheduled or contention-based
  Access slot structure
  Initial NB synchronization
If a 1ms slot is used, high data rate for NB payload is needed assuming this message carries at least 2-byte Short Address for each Responder

## Slide 6: Optimizations
Improve the performance by considering power consumption and collision avoidance
  Deferred Measurement Report
  Adaptively change the Access Slot duration for schedule mode
  …

## Slide 7: One Optimization Example: Switching the Order of Poll and Response Frame
Response frame is expected first in an Access Slot
  If there is no valid Response frame from a Responder, the Initiator can skip the Access Slot without sending Poll frame
Beneficial in terms of power consumption and in-device CoEx requirement at the Initiator and the spectrum efficiency for the network

## Slide 8: Modifications
Support many-to-one ranging: Initiator reports the time stamp, and the Responder computes the range

## Slide 9: Summary
The concatenated one-to-many mode on Slide 3 is the recommended baseline/mandatory method
Optimizations and modifications can be further developed and should be optional