## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Challenges in Shor-Range and Middle-Range Wireless Communications using the 300GHz-Band
Date Submitted: November 16, 2022
Source: Tetsuya Kawanishi, Kazuhiko Tamesue, Takuro Sato,
Waseda University
3-4-1, Okubo, Shinjuku-ku, Tokyo 169-8555, Japan
Voice: +81 3 5286 3386, E-Mail: kawanishi@waseda.jp
Iwao Hosako, National Institute of Information
and Communications Technology (NICT)
4-2-1, Nukui-Kitamachi, Koganei, Tokyo 184-8795, Japan
E-Mail: hosako@nict.go.jp
Re: n/a
Abstract: Overviews of applications and challenges in shared use of short-range and middle-range 300GHz transmission.
Purpose: Informing SC THz on key technologies for 300GHz transmission by addressing various applications and interference for discussion in future THz standardization
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
Takuichi Hirano, Tokyo City University
1-28-1, Tamazutsumi, Setagaya-ku, Tokyo,
158-8557, JAPAN
E-mail: thirano@tcu.ac.jp

## Slide 2: Challenges in Short-Range and Middle-Range Wireless Communications using the 300GHz-Band
Tetsuya Kawanishi, Kazuhiko Tamesue, Takuro Sato,
Takuichi Hirano, and Iwao Hosako
Waseda University, Japan
Tokyo City University, Japan
National Institute of Information and Communications Technology (NICT), Japan

## Slide 3: Outline of this contribution
Use-cases of short-range and middle-range WPAN
System configuration and features of 300 GHz wireless communication
Interference between short-range and middle-range wireless communication

## Slide 4: Applications for short-rage and middle-range WPAN
Tetsuya Kawanishi, Waseda Univ., et al
High speed wireless communication for personalized 8K videos
Short-range communication to cover indoor space
Medium-range communication to cover stadium or aircraft cabin
70m
300GHz
20Gbps 100 users
Use case 3:
-Aircraft cabin
-In-flight video services
-8K video stream (middle range)
70m
300GHz
20Gbps 100 users ( 1 channel )
Use case 2:
-Stadium
-Personalized video services
-8K video stream
(middle-range)
Use case 1:
-Indoor
-Virtual experiences
-8K video stream
(short range)
300GHz
100Gbps
3m

## Slide 5: A short-range wireless communication system
Tetsuya Kawanishi, Waseda Univ., et al
Target
  - Throughput 100 Gbps
  - Bandwidth 25 GHz
  - Distance 3 m
  - Beam scan 30deg
Key Features
  - 16-QAM
  - Beamforming
  - A small size TX module for a compact access point
Access Point
WT
300 GHz beam forming

## Slide 6: Link budget for short-range WPAN
Tetsuya Kawanishi, Waseda Univ., et al
25dBm
(Tx Pow.)
15dBi
(Ant. Gain)
40dBm
(EIRP)
-91.5dB (3m)
(Free Space Loss)
-51.5dBm
-46.5dBm
(Rx Pow.)
3m: -91.5dB
5m: -96.dB
10m: -102dB
20m: -108dB
50m: -115dB
Noise Floor (-73.8dBm)
5dBi
(Ant. Gain)

## Slide 7: System Design for middle-range WPAN
Target
  - Throughput 20 Gbps per channel
  - Spectral efficiency 10 bps/Hz
  - Bandwidth 2.16 GHz per channel
  - Distance 70 m
Key Specification
  - 3x3 MIMO
  - CP-OFDM 64-QAM subcarriers and LDPC (1440, 1344)
  256-QAM subcarriers and LDPC (1440, 1056)
Transmitter
Receiver
RHCP Right-handed circular polarization
LHCP Left-handed circular polarization
IP data
IP data
PHY
PHY
QSFP+ I/F
QSFP+
I/F
3x3MIMO
RHCP
ANT
LHCP
ANT
RHCP
ANT
RHCP
ANT
LHCP
ANT
RHCP ANT
Interference
Interference
feedback precoding weights
precoder
equalizer
Changing the third stream from LP to RHCP or LHCP reduces the number of interfering stream from (1,1,2) to (1,0,1) in stream1/2/3.

## Slide 8: System Design for middle-range WPAN
MIMO operation
  Crosstalk between RHCP and LHCP If the XPD between antennas is enough, the D/U ratio is ensured.
  Crosstalk between RHCP and RHCP D/U ratio is ensured by the null point due to the array antennas.
XPD：Cross Polarization Discrimination
HPBW : Half Power Beam Width
FNBW : First Null Beam Width
16x16 array antenna
Peak Gain: 28.9dBi
HPBW: 6.0°
FNBW: 16.0°
8x8 array antenna
Peak Gain: 22.9dBi
HPBW: 12.0°
FNBW: 32.0°

## Slide 9
Assumption
Tx antennas are in same position
antenna main lobes opposite each other
height of TX and RX antenna is same
1path LoS communication
D/U ratio vs. Antenna distance
D/U ratio [dB]
10m
d
RHCP array antenna
Top view
10m
RHCP array antenna
RHCP array antenna
θ
D
U
Tx
Rx
Antenna distance d[m]
64-QAM
256-QAM
desired D/U ratio is 3dB higher than desired SINR for demodulation.
16x16 array antenna
8x8 array antenna
2.86° @d=1m
16-QAM

## Slide 10: Interference between short-range and middle-range wireless communication
  From the link budget, Receiver level -68dBm is necessary for 64-QAM demodulation. In this case, desired interference level from short range system to middle-range system receiver should be lower than -90dBm.
  As an example, if the transmit EIRP of a short-range system is 40 dBm, distance attenuation alone is insufficient. To further reduce interference, it is necessary to ensure isolation by the coordinated directivity antenna control between the short-range and the middle-range systems.
20m
Short-range assumption
Tx Power 25dBm
Antenna Gain 15dBi
RHCP array antenna
70m
RHCP array antenna
Tx
Rx
desired interference level for 64-QAM

## Slide 11: Summary and Discussion
Use-cases of short-range and middle-range WPAN
System configuration and features of 300 GHz wireless communication
  The short-range WPAN will covers a narrow (3m) range with high throughput
  The middle-range WPAN will covers a longer 70 m range for multiple users
Interference reduction between short-range and middle-range wireless communications
  Coordinated antenna directivity control to reduce each interference.