## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [NBA-MMS-UWB Compressed PSDU]
Date Submitted: [November 15, 2022]
Source: [Alexander Krebs, Moche Cohen, Santhosh Kumar Mani, Xiliang Luo, Yong Liu, Lochan Verma, Jinjing Jiang, SK Yong (Apple)]
Email: krebs@apple.com
Re: [Input to the Working Group]
Abstract: [Proposal of an efficient MAC control signal format suitable for a baseline feature set supported by low-rate O-QPSK narrowband PHYs.]
Purpose: []
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
PAR Objective | Proposed Solution (how addressed)
Safeguards so that the high throughput data use cases will not cause significant disruption to low duty-cycle ranging use cases | 
Interference mitigation techniques to support higher density and higher traffic use cases | 
Other coexistence improvement | 
Backward compatibility with enhanced ranging capable devices (ERDEVs) | 
Improved link budget and/or reduced air-time | 
Additional channels and operating frequencies | 
Improvements to accuracy / precision / reliability and interoperability for high-integrity ranging | 
Reduced complexity and power consumption | 
Hybrid operation with narrowband signaling to assist UWB | Signaling, control, and information elements (IEs) for hybrid operation and multi-millisecond ranging mode
Enhanced native discovery and connection setup mechanisms | 
Sensing capabilities to support presence detection and environment mapping | 
Low-power low-latency streaming | 
Higher data-rate streaming allowing at least 50 Mbit/s of throughput | 
Support for peer-to-peer, peer-to-multi-peer, and station-to-infrastructure protocols | 
Infrastructure synchronization mechanisms | 

## Slide 3: Compressed PSDU: Application
NBA-MMS-UWB [1, 2]
  Poll, Response
    CFO sync for MMS-UWB
    Optional payload for MAC synchronization and control
  Report
    Payload with measurement report data: timestamps, …

## Slide 4: Compressed PSDU: Why?
NBA-MMS-UWB
  UWB requires avg. eirp limit => sweet spot @ 1ms MAC grid
  NB O-QPSK 250k has limited PSDU capacity (~25 bytes/ms)
    Control channel must support baseline feature set (Poll, Resp, Report, …)
    Extended feature set may require higher rate modulation (500k/1M)
      E.g., Secure Ranging Report, Angle of Arrival, …
  Keeping NB packets shorter than 1ms
    reduces energy consumption
    improves internal radio co-existence
    gives better CFO estimate for UWB fragments
    More features can be supported in baseline 250k O-QPSK PHY

## Slide 5: Example: 802.15.4z PSDU+RMI IE
Payload (Encrypted Measurement Report IE, TOF present)
  2-octet MLME header
  2-octet IE header (type=RMI IE, length=4)
  2-octet field bitmask + field length
  4-octet timestamp
Total: 25 octets
MAC Header/Footer
  2-octet Frame Control
  2-octet Dst Short Addr
  1-octet AuxSecHeader
  8-octet ENC-MIC-64
  2-octet CRC16

## Slide 6: Compressed PSDU: Format Proposal
Generic compressed PSDU format
  1-octet PSDU ID
  PSDU content is ID specific

## Slide 7: Compressed PSDU: Format Proposal
Compressed PSDU specific to NBA-MMS-UWB control frames
  1-octet message ID (0x00=Poll, 0x01=Response, 0x02=Report, …)
  2-octet session identifier/address
  ID specific data (variable length)
  2-octet CRC16

## Slide 8: Example: EncTimestamp64
PSDU for ID=0xtbd (EncTimeStamp64)
  1-octet message ID (0xtbd)
  2-octet session identifier/address
  4-octet timestamp(s) (encrypted)
  8-octet cryptographic protection (MAC)
Total octets:
  w/o CRC: 15, 19, 23, …
  w CRC: 17, 21, 25, …
Remarks
  PHR length field => number of timestamps + presence of CRC
  Redundancy between ENC-MIC-64 and CRC16 can be exploited to reduce PSDU size

## Slide 9: Comparison: Compressed vs 4z IE
Example: Secured Timestamp Report (1 timestamp)
  PSDUs as defined in previous slides
  TX-RX switch not feasible with 802.15.4z RMI IE @ 250kbit/s O-QPSK PHY

## Slide 10: Comparison: Compressed vs 4z IE
Example: Poll, Response, Report (format as in previous slides)
  802.15.4z PSDU with RMI IE (TOF) and minimal (2-octet) nested IE for Poll/Resp
  Compressed PSDU Poll/Response (w/o block index), Report (1 timestamp)
  32-38% frame duration reduction @ 250kbit/s O-QPSK PHY
    Less than 50% TX occupancy per slot
    Reduced energy consumption, scheduling conflicts, and collision rate (PER)

## Slide 11: Summary
Compressed PSDU Proposal
  Cross-session interoperability NOT required for MMS-UWB control packets
  Existing RMI IE scheme does not support 1-timestamp report w encryption in 1ms grid
  Proposed PSDU format gains an >30% advantage of packet duration every MMS cycle

## Slide 12: References
[1] X. Luo (Apple Inc), F. Leong (NXP), M. Lee (Samsung Electronics), et al., “NBA-UWB Technical Framework Proposal”, 15-22-0571-01-04ab.
[2] A. Krebs et al., “Updates on Narrowband Channel Allocation and Access”, 15-22-0493-02-04ab.
[3] E. Ekrem et al., “Link budget analysis for narrowband assisted multi-millisecond UWB”, 15-22-0074-00-04ab.
[4] L. Verma (Apple), M. Lee (Samsung), W. Kuchler (NXP), et al., “UWB Channel Usage Coordination for better UWB Coexistence”, 15-22-0456-00-04ab.
[5] E. Ekrem (Apple) et al., “More on narrowband assisted multi-millisecond UWB”, 15-21-0593-01-04ab.
[6] L. Verma (Apple) et al., ”Follow-up on UWB Channel Usage Coordination”, 15-22-0573-00-04ab.