## Slide 1
Project: P802.15 Working Group for Wireless Specialty Networks
Submission Title: Overview of FEC proposals for 15.6ma
Date Submitted: November 15th, 2022
Source: Marco Hernandez1,3, Ryuji Kohno1,2, Takumi Kobayashi1,2, Minsoo Kim1
Company: 1Yokosuka Research Park International Alliance Institute (YRP-IAI), Japan; 2Yokohama National University (YNU), Japan. 3CWC, Oulu Univ. Finland.
Address: 3-4 Hikarino-oka, Yokosuka, 239-0847, Japan.
E-Mail: Marco.Hernandez@ieee.org; kohno@ynu.ac.jp; Kobayashi-Takumi-ch@ynu.ac.jp; Minsoo@minsookim.com;
Abstract: Technical contributions.
Purpose: In response to the call for technical contributions.
Notice: This document has been prepared to assist P802.15.6ma. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.6ma.

## Slide 2: FEC harmonization
The proposal for FEC depends on the coexistence operation of 6ma BANs according to 15-23-0101-02.
Coexistence environment class | Environment
0 | 6ma BAN only
1 [1a] | Multiple 6ma BANs 1a
2 [1b] | Multiple 15.6 & 6ma BANs
3 | Multiple 6ma BANs & non-UWB systems (Wi-Fi & Unlicensed 3GPP)
4 [2a] | Multiple 6ma BANs & 802.15 UWB systems
5 [2b] | Multiple 6ma BANs, non-802.15 UWB systems (ETSI UWB systems)
6 [2c] | Multiple 6ma BANs & 802.15 UWB & non-802.15 UWB systems (ETSI UWB)
7 | Multiple 6ma BANs & non-UWB systems (Wi-Fi & Unlicensed 3GPP) & 802.15 UWB & non-802.15 UWB systems (ETSI UWB)

## Slide 3: FEC Harmonization
Proposal to use of BCC and LDPC for coexistence environment class 0.
For other coexistence environment classes, the PHY may add a concatenated external FEC:
  BCC; LDPC + External FEC (details are TBD)
For coexistence environment classes with the highest levels of interference, the PHY may use a HARQ
  decomposable CC (details are TBD)

## Slide 4
Coexistence environment class | Technologies
0 | BCC; LDPC
1 [1a] | BCC; LDPC + Extrinsic
2 [1b] | 
3 | 
4 [2a] | 
5 [2b] | 
6 [2c] | 
7 | HARQ
How the specification of FEC may look like
Open for discussion: if specification of FEC depends on QoS or traffic type as well.

## Slide 5
QoS/Cox | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0 | BCC | BCC+E | BCC+E | BCC+E |  |  | HARQ | HARQ
1 | BCC | BCC+E | BCC+E | BCC+E |  |  | HARQ | HARQ
2 | BCC | BCC+E | BCC+E | BCC+E |  |  | HARQ | HARQ
3 | BCC | BCC+E | BCC+E | BCC+E |  |  | HARQ | HARQ
4 | BCC | BCC+E | BCC+E | BCC+E |  |  | HARQ | HARQ
5 | BCC | BCC+E | BCC+E | BCC+E |  |  | HARQ/IM | HARQ/IM
6 | CFP/HARQ | CFP/HARQ | CFP/HARQ | CFP/HARQ | CFP/HARQ | CFP/HARQ | HARQ/IM | HARQ/IM
7 | CFP/HARQ | CFP/HARQ | CFP/HARQ | CFP/HARQ | CFP/HARQ | CFP/HARQ | HARQ/IM | HARQ/IM
Open for discussion: if specification of FEC depends on QoS or traffic type as well.

## Slide 6: HARQ and others
The description of HARQ based on decomposable CC and use of super orthogonal CC will be done in revisions of 15-22-0561 and 15-22-0562, respectively.
The design of the extrinsic FEC is under evaluation.