## Slide 1
Project: P802.15 Working Group for Wireless Specialty Networks
Submission Title: Overview of FEC proposals for 15.6ma
Date Submitted: November 15th, 2022
Source: Marco Hernandez1,3, Ryuji Kohno1,2, Takumi Kobayashi1,2, Minsoo Kim1
Company: 1Yokosuka Research Park International Alliance Institute (YRP-IAI), Japan; 2Yokohama National University (YNU), Japan. 3CWC, Oulu Univ. Finland.
Address: 3-4 Hikarino-oka, Yokosuka, 239-0847, Japan.
E-Mail: Marco.Hernandez@ieee.org; kohno@ynu.ac.jp; Kobayashi-Takumi-ch@ynu.ac.jp; Minsoo@minsookim.com;
Abstract: Technical contributions.
Purpose: In response to the call for technical contributions.
Notice: This document has been prepared to assist P802.15.6ma. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.6ma.

## Slide 2: FEC harmonization
The proposal for FEC depends on the coexistence operation of 6ma BANs (coexistence environment class)
Coexistence environment class | 15.6ma | 15.6-2012 | Non-UWB (Wi-Fi, unlicensed 5G) | 802.15 UWB (15.4, 15.8) | Non-802.15 UWB (ETSI, SmartBAN) | Note
0 |  |  |  |  |  | A single BAN
1 |  |  |  |  |  | Multiple BANs
2 |  |  |  |  |  | 
3 |  |  |  |  |  | Non-UWB systems
4 |  |  |  |  |  | Multiple UWB systems
5 |  |  |  |  |  | 
6 |  |  |  |  |  | 
7 |  |  |  |  |  | Multiple: BANs, non-UWB and UWB systems

## Slide 3
QoS type | FEC configuration
0 | Inner encoder: BCC or LDPC
1 | Inner encoder: BCC or LDPC
2 | Inner encoder: BCC or LDPC
3 | Inner encoder: BCC or LDPC
4 | Outer Encoder: shortened RS (200,168) and Inner encoder: BCC or LDPC
5 | Outer Encoder: shortened RS (200,168) and Inner encoder: BCC or LDPC
6 | Outer Encoder: shortened RS (200,168) and Inner encoder: BCC or LDPC
7 | Outer Encoder: shortened RS (200,168) and Inner encoder: BCC or LDPC
QoS type | FEC configuration
0 | Inner encoder: BCC or LDPC
1 | Inner encoder: BCC or LDPC
2 | Inner encoder: BCC or LDPC
3 | Inner encoder: BCC or LDPC
4 | HARQ
5 | HARQ
6 | HARQ
7 | HARQ
Coexistence class 0
Coexistence class 1

## Slide 4
QoS type | FEC configuration
0 | Inner encoder: BCC or LDPC
1 | Inner encoder: BCC or LDPC
2 | Inner encoder: BCC or LDPC
3 | Inner encoder: BCC or LDPC
4 | HARQ
5 | HARQ
6 | HARQ
7 | HARQ
QoS type | FEC configuration
0 | Outer Encoder: shortened RS (200,168) and Inner encoder: BCC or LDPC
1 | Outer Encoder: shortened RS (200,168) and Inner encoder: BCC or LDPC
2 | Outer Encoder: shortened RS (200,168) and Inner encoder: BCC or LDPC
3 | Outer Encoder: shortened RS (200,168) and Inner encoder: BCC or LDPC
4 | Outer Encoder: shortened RS (200,168) and Inner encoder: BCC or LDPC
5 | HARQ
6 | HARQ
7 | HARQ
Coexistence class 2
Coexistence class 3

## Slide 5
QoS type | FEC configuration
0 | Outer Encoder: shortened RS (200,168) and Inner encoder: BCC or LDPC
1 | Outer Encoder: shortened RS (200,168) and Inner encoder: BCC or LDPC
2 | Outer Encoder: shortened RS (200,168) and Inner encoder: BCC or LDPC
3 | Outer Encoder: shortened RS (200,168) and Inner encoder: BCC or LDPC
4 | Outer Encoder: shortened RS (200,168) and Inner encoder: BCC or LDPC
5 | HARQ
6 | HARQ
7 | HARQ
QoS type | FEC configuration
0 | Inner encoder: BCC or LDPC
1 | Inner encoder: BCC or LDPC
2 | Inner encoder: BCC or LDPC
3 | Inner encoder: BCC or LDPC
4 | Inner encoder: BCC or LDPC
5 | Outer Encoder: shortened RS (200,168) and Inner encoder: BCC or LDPC
6 | Outer Encoder: shortened RS (200,168) and Inner encoder: BCC or LDPC
7 | Outer Encoder: shortened RS (200,168) and Inner encoder: BCC or LDPC
Coexistence class 4
Coexistence class 5

## Slide 6
QoS type | FEC configuration
0 | Outer Encoder: shortened RS (200,168) and Inner encoder: BCC or LDPC
1 | Outer Encoder: shortened RS (200,168) and Inner encoder: BCC or LDPC
2 | Outer Encoder: shortened RS (200,168) and Inner encoder: BCC or LDPC
3 | Outer Encoder: shortened RS (200,168) and Inner encoder: BCC or LDPC
4 | Outer Encoder: shortened RS (200,168) and Inner encoder: BCC or LDPC
5 | HARQ
6 | HARQ
7 | HARQ
QoS type | FEC configuration
0 | Outer Encoder: shortened RS (200,168) and Inner encoder: BCC or LDPC
1 | Outer Encoder: shortened RS (200,168) and Inner encoder: BCC or LDPC
2 | Outer Encoder: shortened RS (200,168) and Inner encoder: BCC or LDPC
3 | Outer Encoder: shortened RS (200,168) and Inner encoder: BCC or LDPC
4 | Outer Encoder: shortened RS (200,168) and Inner encoder: BCC or LDPC
5 | HARQ
6 | HARQ
7 | HARQ
Coexistence class 6
Coexistence class 7