## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Found Issues in 802.15.4w]
Date Submitted: [15 November 2022]
Source: [Joerg ROBERT, Daniel HERGERT] Company: [TU Ilmenau / Fraunhofer IIS]
Address [Helmholtzplatz 2, 98693 Ilmenau, Germany]
Voice:[+49 3677 69-4260], FAX: [], E-Mail:[joerg.robert@tu-ilmeau.de]
Abstract: [This presentation contains issues found in the current version of IEEE 802.15.4w]
Purpose: [Presentation in TG4me]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Found Issues in IEEE 802.15.4w
Joerg ROBERT (TU Ilmenau, Fraunhofer IIS), Daniel HERGERT (TU Ilmenau)

## Slide 3: Motivation
During the implementation of IEEE 802.15.4w several smaller issues and unclear definitions have been found
The goal is to correct these as part of TG4me

## Slide 4: 23.3.5.3.4 – LPDC Coding
The description of the indices m and i is wrong. Most likely this is a copy paste error when defining the shorter 4w LDPC code out of a longer LDPC code used somewhere else.

## Slide 5: 23.3.5.3.4 – LPDC Coding

## Slide 6: 23.3.6a.2 – Convolutional Interleaving
The different radio bursts may have different length. However, this is not stated anywhere and may potentially lead to confusion. Some clarification would be helpful.

## Slide 7: 23.3.6a.3 – LPDC Interleaving
The last section specifies the behavior in case of multiple codewords. The index i=0 is used for addressing the first bit in the payload of the next codeword. This text is formally correct, but leaves room for wrong interpretation.
Example:
  0. codeword, n=0  i=0 refers to Bit #1
  1. codeword, n=1  i=0 refers to Bit #33
  2. codeword, n=2  i=0 refers to Bit #65

## Slide 8: 23.3.6a.3 – LPDC Interleaving
Proposed text:
In both cases i=0 refers to the first bit of the radio-burst payload. If multiple codewords {cw0, cw1, …, cwN-1} are transmitted, i=0 for the next codeword refers to the first bit after the already placed bits in the radio-burst payload, namely bit number n*32+1, where n denotes the number of the next codeword, since every LDPC-codeword appends 32 bit to each radio-burst payload.

## Slide 9: 23.3.6b.2 – Time - Assignment:
The text states that the delay between the first and the next radio burst is given by T(p, l0). However, the first radio burst has index l0. Therefore, the correct term is T(p, l0+1).

## Slide 10: 23.3.6b.2 – Time - Assignment:

## Slide 11: 23.3.6b.2 – ChanNumber
The parameter ChanNumber(p,l) is identical to the parameter phyCurrentChannel. However, this is not stated anywhere. A clarification could be done in 7.4.4.17a or directly below the ChanNumber definition in 23.3.6b.2. Alternatively, ChanNumber could be replaced by phyCurrentChannel.

## Slide 12: 23.3.6b.2 –Assignment-Pattern
The calculation of the transmit pattern p is given by p=R mod 8, resulting in values between 0 and 7. However, the values given in the tables are 1, …, 8. The values in the Tables 23-3c and 23-3d should be corrected to 0, …, 7.

## Slide 13: 10.1.3.11.3 Channel numbering for LECIM FSK PHY
It is not 100% clear which channel spacing has to be used in Table 10-18, even though the experience reader knows what to do. We may have to add some text that 12.5 kHz spacing is for non-split, the others are for split modulation.

## Slide 14: 7.4.4.17 LECIM FSK Operating Mode IE
The 12.5 kHz channel bandwidth cannot be signaled in the LECIM FSK Operation Mode IE

## Slide 15: 11.3 – Parameter phyLecimSymbolrate
In 23.3.1 to additional rates are added (2,4 kb/s and 4,8 kb/s) in Table 23-a. for 262 MHz. However, these values are not added in chapter 7.4.4.17. Furthermore, we also do not have any bits left to add them in Table 7-35.

## Slide 16: Thanks!