## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Inter Frame Spacing Follow Up]
Date Submitted: [16 November, 2022]
Source: [Kangjin Yoon, Chunyu Hu, Carlos Aldana, Claudio Da Silva] Company [Meta Platforms, Inc.]
[Bin Tian, Pooria Pakrooh, Steve Shellhammer, Koorosh Akhavan] Company [Qualcomm]
E-Mail:[{kyoon, chunyuhu, caldana, claudiodasilva}@fb.com,
{btian, ppakrooh, sshellha, kakhavan} @qti.qualcomm.com]
Re: [Input to TG4ab]
Abstract: [AIFS values are proposed for Imm-Ack]
Purpose: [To make a consensus on AIFS value]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
PAR Objective | Proposed Solution (how addressed)
Safeguards so that the high throughput data use cases will not cause significant disruption to low duty-cycle ranging use cases | 
Interference mitigation techniques to support higher density and higher traffic use cases | 
Other coexistence improvement | 
Backward compatibility with enhanced ranging capable devices (ERDEVs) | 
Improved link budget and/or reduced air-time | 
Additional channels and operating frequencies | 
Improvements to accuracy / precision / reliability and interoperability for high-integrity ranging | 
Reduced complexity and power consumption | 
Hybrid operation with narrowband signaling to assist UWB | 
Enhanced native discovery and connection setup mechanisms | 
Sensing capabilities to support presence detection and environment mapping | 
Low-power low-latency streaming | Short AIFS values help to keep low-latency
Higher data-rate streaming allowing at least 50 Mbit/s of throughput | AIFS should be defined for reliable data communication
Support for peer-to-peer, peer-to-multi-peer, and station-to-infrastructure protocols | 
Infrastructure synchronization mechanisms | 

## Slide 3: Previous Contributions Related To Ack Inter Frame Spacing (AIFS)
DCN 173r0 (Mar 2022) “Ack for data communication”
DCN 296r1 (May 2022) “A Higher Data Rate Proposal For UWB”
DCN 369r0 (July 2022) “Inter frame spacing for HRP UWB PHY”

## Slide 4: Background
Ack Interframe spacing (AIFS) value defines the minimum separation between data frame and ack frame
AIFS value impacts on Spectral efficiency and Power consumption
However, shorter AIFS requires higher implementation cost
We need to find a value with good balance between performance and cost
Plus, we need to consider all different type of UWB devices (from simple tag to high performance smart device)

## Slide 5: Recap: Straw Poll Result
Which option do you prefer for the choice of AIFS:
  Option 1: Use legacy IFS values: 0
  Option 2: Find new fixed IFS values: 17
  Option 3: Have different IFS values for different PHY usage: 1
  Option 4: Make IFS values negotiable: 8

## Slide 6: AIFS and Enh-Ack
Enh-Ack can have IEs and MAC payload
Time for Enh-Ack frame preparation is unpredictable
  Enh-Ack may require upper layer processing to be prepared
  Hard to define fixed AIFS
We propose to use AIFS only for Imm-Ack which will be sent in the same slot
  AIFS should be long enough to do CRC check

## Slide 7: AIFS for Imm-Ack
We propose:
  One mandatory AIFS value for compatibility
  Multiple optional AIFS value for high-performance device
Mandatory AIFS value
  64 us
Optional AIFS values
  32 us
  16 us
  Etc.

## Slide 8: AIFS Values Negotiation
AIFS values negotiation should happen during association/setup phase (just like other optional features)
  Controlee should inform its capability to Controller
  Controller will select which AIFS value will be used
  Those negotiation may happen in out-of-band or in-band
  Mandatory AIFS value shall be used when there is no negotiation

## Slide 9: Summary
We propose to define and use AIFS only for Imm-Ack
We propose 64 us AIFS as a mandatory and smaller AIFS (e.g., 32 and 16) as optional
AIFS values negotiation may happen in out-of-band or in-band

## Slide 10: Thank You

## Slide 11: Backup slides

## Slide 12: Recap: IFS in 15.4 & 15.4z
AIFS: Minimum separation between data frame and ack frame
SIFS: Minimum separation which shall come after short data frame (up to 18 Byte MPDU)
LIFS: Minimum separation which shall come after long data frame (over 18 B MPDU)
AIFS = SIFS = 12 preamble symbols (Ref: 15.4-2020, pp. 61, 454)
LIFS = 40 preamble symbols (Ref: 15.4-2020, p. 454)
 | Preamble symbol duration (ns) | AIFS = SIFS (us) | LIFS (us)
HPRF | 729.17 | 8.75 | 29.17
BPRF | 993.6 | 11.92 | 39.74
 | 1017.6 | 12.21 | 40.70
 | 3974.4 | 47.70 | 158.98