## Slide 1
Project: IEEE P802.15 Working Group for Wireless Specialty Networks
Submission Title: Overview of MAC proposals for 15.6ma
Date Submitted: November 17th, 2022
Source: Minsoo Kim, Takumi Kobayashi, Marco Hernandez, Ryuji Kohno
Company: (1)Yokohama National University (2) YRP International Alliance Institute
Address: (1)79-5 Tokiwadai, Hodogaya-ku, Yokohama, 240-8501 Japan,
(2) YRP1 Blg., 3-4 HikarinoOka, Yokosuka-City, Kanagawa, 239-0847 Japan
Voice:[+81-90-5408-0611] E-Mail:[minsoo@minsookim.com, kobayashi-takumi-ch@ynu.ac.jp, marco.hernandez@ieee.org, kohno@ynu.ac.jp]
Re: In response to call for proposal
Abstract: Overview of MAC proposals for 15.6ma
Purpose: Material for discussion in P802.15.6a TG
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: MAC Protocol Proposal for Multiple BAN Environmnet (Lv1) # 15-22-0639
Utilizes Control Channel.
  Limits transmission privilege on Control Channel only to coordinators.
  Allows more efficient and accurate clear channel assessment by separating control frames and data frames.
  Two mandatory channels for control and data frames are required.
Introduces 3 Periods in Data Channel
  Network Management Period (NMP) for Data Beacons,
  Contention Free Period (CFP) for scheduled data frames,
  And Contention Access Period (CAP) for unscheduled data frames and node connection/disconnection.
Each BAN has its own contention free period while sharing superframes.
  To avoid frame collision between coexisting BANs.
Operating procedures of some MAC functions such as BAN creation are shown with a flowchart.
The newly required fields for performing this procedure have been explained.

## Slide 3: MAC proposal for coexisting dependable BANs # 15-22-0594
Dependable BAN Service Classes
  Specifies three classes. Coexisting BANs will coordinates based on the BAN class.
Beacon Period Extension
  Allows flexible configuration of the beacon period.
  Supports large number of nodes while guaranteeing short cycle time.
  Guarantees that nodes can access the channel every cycle time.
Coordinator Hub and Beacon Access Phase
  Defines Beacon Access Phase (BAP) in the beacon period.
  Defines a coordinator hub and a leaf hub and let coordinator hub assigns beacon slots for leaf hubs.
Scheduled Access Extension
  Allows nodes have periodic access multiple ties in a beacon period
Adaptative Superframe Interleaving with Adjustment and Regulation
  Negotiates the structure of beacon period among coexisting dependable BANs and regulates transmissions.