## Slide 1
Project: IEEE P802.15 Working Group for Wireless Specialty Networks (WSN)
Submission Title: How strong a PHR do we need for LDPC?
Date Submitted: 21st December 2022
Source: Carl Murray(Qorvo), Jarek Niewczas (Qorvo), Billy Verso (Qorvo)
Abstract: Presents an argument for support of PHRx2 instead of PHRx4 on the basis that it better utilizes the maximum packet energy by minimizing energy wasted on unusable headroom.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
Notes: Jul 12, 2010
Page 1

## Slide 2
PAR Objective | 
Safeguards so that the high throughput data use cases will not cause significant disruption to low duty-cycle ranging use cases | 
Interference mitigation techniques to support higher density and higher traffic use cases | 
Other coexistence improvement | 
Backward compatibility with enhanced ranging capable devices (ERDEV | 
Improved link budget and/or reduced air-time | 
Additional channels and operating frequencies | 
Improvements to accuracy / precision / reliability and interoperability for high-integrity ranging | 
Reduced complexity and power consumption | 
Hybrid operation with narrowband signaling to assist UWB | 
Enhanced native discovery and connection setup mechanisms | 
Sensing capabilities to support presence detection and environment mapping | 
Low-power low-latency streaming | 
Higher data-rate streaming allowing at least 50 Mbit/s of throughput | 
Support for peer-to-peer, peer-to-multi-peer, and station-to-infrastructure protocols | 
Infrastructure synchronization mechanisms | 

## Slide 3: How we should make progress
Firstly, to decide on relative strength of PHR wrt LDPC
  Options are for PHR symbols to be at the same nominal rate as the LDPC data but to repeat PHR symbols x2 or x4 times, denoted PHRx2 and PHRx4 respectively
  The real issue is not the PHR strength, but the implications on the preamble detector
Only then decide how to implement the PHR
  2-stage PHR
    Composed of PHR1 and PHR2
    PHR1 is at a fixed low data rate and encodes the data rate of PHR2 and the payload
    PHR1 transmission and coding designed to match the PHR2 strength
This submission addresses step A only

## Slide 4: Terminology
2 types of packets are referenced in this submission based on their duration
  Sub-millisecond packets (< 1ms) – can use gating-gain
  Supra-millisecond (≥ 1ms) – cannot use gating-gain
In this submission a distinction is made between the ‘nominal data rate’ and the ‘effective data rate’.
  The nominal data rate is the data rate assuming a code rate of 0.5.
  The effective data rate is the true instantaneous data rate and is equal to the payload bits divided by payload duration
  This distinction is required because with full-parity LDPC with payloads less than half the LDPC code block size, the effective code rate is always less than 0.5. The effective data rate incorporates the effective code rate.

## Slide 5: Recap of PHRx2 vs PHRx4 (see also Decoder SNR Appendix-A)
PHRx4 is necessary if we want to support LDPC-1944 down to 17 bytes
However, this means that the PHR has significant excess margin for all bigger payloads
This also means that the SHR will need to have the same excess margin
PHRx2 requires 3dB less margin
Decoder SNR does not map directly to link margin as it does not incorporate gating gain

## Slide 6: Analysis Methodology
Coherent data demodulation
  This is realistic as there should only be a small residual CFO at the data demodulation stage
Coherent preamble detection
  This is unrealistic in practice, but it permits investigation of an upper bound on performance
  This analysis sets the preamble length based on the nominal data rate
    For every 3dB reduction in SNR at the nominal rate the preamble length is increased x2
  This matches data and SHR strengths for supra-millisecond packets
See Appendix-B for additional parameters

## Slide 7: Steps in Analysis I
Plot data link-margin with idealized coherent preamble detector
Check preamble link-margin with this idealized coherent preamble detector
Increase preamble strength (length) so that preamble is not packet bottleneck.
Add 1st constraint to the preamble detector
  Set a minimum SHR length
Add 2nd constraint to the preamble detector
  No longer fully coherent, i.e. 3dB reduction in signal strength will require the preamble length increase to be > x2
Compare packet link-margin for PHRx2 and PHRx4 and restrict to the nominal data rates being recommended in 4ab

## Slide 8: Steps in Analysis II
Sanity Check. Compare packet link-margin for PHRx2 and PHRx4 with constrains in steps (4) and (5) removed
Compare LDPC-1944 PHRx4 to PHRx2 performance for payloads where PHRx4 is carrying excess margin in PHR and preamble

## Slide 9: Step 1- Data Link-Margin Ideal Preamble Detector
SHR and data strengths are matched for supra-millisecond packets
SHR and data strengths will also match for sub-millisecond packets which do not benefit from “full-parity” (see next slide)

## Slide 10: Step 2 – Check Preamble Link Margin Ideal Preamble Detector
A → B : Both data and preamble benefit equally from gating-gain => stay matched
B → C : Again, both data and preamble benefit equally from gating-gain but data also benefits from code-rate reduction due to full-parity => data becomes stronger than preamble
dashed lines represent packets with the same nominal data rate

## Slide 11: Step 3 - Packet Link Margin Ideal Preamble Detector – Increased Preamble length
Increasing the preamble length to offset the data code rate reduction due to full-parity
As packet energy is fixed, proportionally more energy is allocated to the SHR
Therefore, the data, and hence the packet link-margin will reduce

## Slide 12: Step 4 - Packet Link Margin Preamble length increased and Minimum SHR length
Need to ensure that the SHR is above some minimum length
Minimum SHR length will depend on the particular implementation
Introducing this constraint causes shoulders to form at higher rates for a given payload

## Slide 13: Step 5 - Packet Link Margin Increased Preamble, Minimum SHR length, Not fully coherent PD
Preamble detection not fully coherent : 3dB reduction in signal strength implies preamble length increase will need to be more than x2
Non fully coherent performance will be implementation dependent, so this is just illustrative

## Slide 14: Step 6 - Packet Link Margin LDPC PHRx2 vs PHRx4 – Increased Preamble, Not fully coherent preamble detector
For 20 bytes LDPC-648 PHRx2 performance matches LDPC-1944 PHRx4 performance

## Slide 15: Step 7 - Packet Link Margin LDPC PHRx2 vs PHRx4 – Increased Preamble, Ideal coherent preamble detector
For 20 bytes LDPC-648 PHRx2 performance matches LDPC-1944 PHRx4 performance

## Slide 16: Step 8 - Packet Link Margin LDPC PHRx2 vs PHRx4 – Increased Preamble, Ideal coherent preamble detector
For 40 bytes LDPC-1296 PHRx2 performance is better than LDPC-1944 PHRx4 performance

## Slide 17: Observations 1/2
The max packet energy for sub-millisecond packets is fixed
  For optimum performance need to minimize the imbalance between the sensitivities of data, PHR and preamble as any imbalance translates to wasted packet energy
Full-parity 802.11n is a non-optimum choice as the decoder performance depends on payload length
  This means that the PHR and preamble must have excess headroom to accommodate this (since they are not payload dependent)
  This is mitigated somewhat by switching between code block sizes at reasonable switch over points
PHRx2 can match PHRx4 link-margin by using a lower nominal data rate for the same payload

## Slide 18: Observations 2/2
For a given packet link-margin, a higher gating gain permits a poorer preamble sensitivity level
  Therefore, it is best to operate at the highest nominal data rate that does not sacrifice link margin
  So, for example, with a 20-byte sub-millisecond payload, PHRx4 at 62.4 Mbps is better than at 1.95 Mbps (will be implementation dependent)
For a given nominal data rate PHRx4 has to have more preamble margin than PHRx2 to accommodate full-parity
  As per point (3) PHRx2 can match PHRx4 link-margin
  But by switching to the appropriate code block size PHRx2 will have better link-margin than PHRx4 as less packet energy is wasted on excess headroom

## Slide 19: Recommendation
To make best use of the maximum allowed packet energy and gating gain the link-margin of the different segments of the packet should be properly balanced
Therefore, with full-parity 802.11n LDPC we should use PHRx2 rather than PHRx4

## Slide 20
Appendix-A
Decoder SNR

## Slide 21: Decoder SNR

## Slide 22: Decoder SNR
The decoder SNR at 1% PER has been used in many submissions to quantify the performance of different decoders
The decoder SNR is a convenient metric as it facilitates the comparison of the relative strength of the different fields of the packet
  This is useful as the receiver architecture can be specific to the packet field
  It assumes constant packet pulse amplitude and constant mean PRF
The values were provided by Carlos Aldana on a related but separate context. They are reused here with his permission
The absolute value of these numbers depends on the particular definition used, but in this submission only the relative values are of interest
The decoder component with the highest SNR requirement will be the bottleneck

## Slide 23: Breaking out the components of SNR
It is instructive to break out the 2 components of the decoder SNR to appreciate how coding gain and code rate gain separately contribute to the overall performance
  The relative coding gain is indicated by the decoder Eb/No
  The relative code rate gain is measured by how much it lowers the required SNR
  In both cases lower is better
In the following figures the SNR is the sum of the respective components, the Eb/No and code rate component respectively
  The range of the y-axis is the same in each figure to highlight the relative contribution of each component
For short payloads the SNR for LDPC is dominated by the impact of the full-parity induced code rate
  The coding gain benefit of LDPC over CC k = 7 is ~2.4 dB

## Slide 24: Components of Decoder SNR

## Slide 25: Comments on decoder SNR
The code rate gain is not intrinsic to the LDPC decoder
  An equivalent way to achieve this would be to lower the data rate and fix the LDPC code rate at 0.5
  This would also lead to a better and easier match in sensitivity between the PHR and data payload as LDPC code rate dependency would be removed
    The preamble would also be easier to match
  This has the significant advantage of decoupling the LDPC “gain” from the payload size and mapping it back to the data rate
  It is also simpler to integrate as an add-on component as it is decoupled from the payload size
  LDPC can now be viewed as giving a gain of 2.4 dB and would only need to be deployed in PHYs where this additional gain is advantageous
  Would only be relying on LDPC for the gains that only LDPC can deliver
    The other benefits can be achieved with CC k = 7

## Slide 26
Appendix-B
Additional Analysis Parameters

## Slide 27: Analysis Parameters I
The preamble PRF is always 124.8 MHz
The minimum preamble configuration is 32 SYNC + 8 SFD symbols
For every 3dB reduction in SNR at the nominal rate, the preamble length is increased x2.4 rather than x2 for not fully coherent preamble detection
Only interested in optimizing for payloads of 20 bytes and above
The data PRF is 124.8 MHz for nominal data rates ≤ 15.6 Mbps.
The data PRF is 249.6 MHz for nominal data rates ≥ 31.2 Mbps.

## Slide 28: Analysis Parameters II
To have a common reference for the gating gain with mixed PRF, the gating gain is always with respect to the pulse amplitude of a 1 millisecond packet at 124.8 MHz PRF. This means that for homogeneous PRF the gating gain will always be positive. For mixed PRF the gating gain can be negative.
The pulse amplitude is assumed to be constant throughout the packet
The PHR is encoded using CC k=7
The exact configuration and length of the PHR are unimportant for the analysis in this submission
The payload data is encoded using either CC k=7 or full-parity LDPC

## Slide 29
Appendix-C
CC k=7
vs
LDPC-1944 PHRx4

## Slide 30: Packet Link Margin CC k=7 PHRx1 vs LDPC PHRx4 – Preamble lengthened, Not fully coherent preamble detector
For 20 bytes CC K=7 PHRx1 is only 1.6 dB worse than LDPC-1944 PHRx4 performance

## Slide 31: Packet Link Margin CC k=7 PHRx1 vs LDPC PHRx4 – Preamble lengthened, Not fully coherent preamble detector
For 20 bytes CC K=7 PHRx2 with 2.4 dB extra performance is better than LDPC-1944 PHRx4 performance