## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Improvements on UWB In-band Discovery]
Date Submitted: [16 January, 2023]
Source: [Lei Huang, Kuan Wu, Rojan Chitrakar, Stephen McCann, David Xun Yang (Huawei); Kangjin Yoon (Meta)]
E-Mail:[lei.huang1@huawei.com]
Abstract: [Improvements on UWB in-band discovery protocol has been discussed.]
Purpose: [To improve the UWB in-band discovery protocol.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
PAR Objective | Proposed Solution (how addressed)
Safeguards so that the high throughput data use cases will not cause significant disruption to low duty-cycle ranging use cases | 
Interference mitigation techniques to support higher density and higher traffic use cases | 
Other coexistence improvement | 
Backward compatibility with enhanced ranging capable devices (ERDEVs) | 
Improved link budget and/or reduced air-time | 
Additional channels and operating frequencies | 
Improvements to accuracy / precision / reliability and interoperability for high-integrity ranging | 
Reduced complexity and power consumption | 
Hybrid operation with narrowband signaling to assist UWB | 
Enhanced native discovery and connection setup mechanisms | Improved UWB in-band discovery and association
Sensing capabilities to support presence detection and environment mapping | 
Low-power low-latency streaming | 
Higher data-rate streaming allowing at least 50 Mbit/s of throughput | 
Support for peer-to-peer, peer-to-multi-peer, and station-to-infrastructure protocols | 
Infrastructure synchronization mechanisms | 

## Slide 3: Previous Contributions Related To Discovery
[1] DCN 646r0 (November 2022) “UWB In-Band Discovery”
[2] DCN 456r0 (September 2022) “UWB Channel Usage Coordination for better UWB Coexistence”

## Slide 4: Recap: UWB in-band discovery (1)
A UWB in-band discovery mechanism was proposed in [1].
  Controller sends Control Message containing Application Control (AC) IE with Association Availability field.
    0: No further association is available
    1: Further association is available
  Controlee shall choose random timing within empty slots to send Association Request frame.
  After receiving an Association Request frame, the controller can schedule a slot in the next block for the transmission of an Association Response frame.
Association Response
Association Request
Data
Data
Data
Data
Control
Data
Data
Data
Data
Control
Block N
Block N+1
Scheduling via Control Message
5 empty slots
4 empty slots

## Slide 5
Observation 1
How does an unassociated controlee know the locations of empty slots in the block is not disclosed in [1].
A reasonable guess is that the unassociated controlee has to parse the Scheduling IE in the same Control message with AC IE to determine the locations of empty slots.
  This may adversely impact power efficiency of unassociated controlee.
    Controller has no reason to schedule any slots to the unassociated controlee.
    If the unassociated controlee can determine the locations of empty slots by other means, it can skip parsing the scheduling IE for power saving purposes.

## Slide 6
Proposal 1
Octets: 2 | 0/4 | 0/1 | 0/1 | 0/2 | 0/variable | 0/TBD | 0/TBD | 0/TBD | 0/TBD | 0/TBD
Content Control | Session ID | Block Duration | Round Duration | Slot Duration | Contention Phase Structure | Ranging Control | Data Comm Control | Sensing Control | TDoA Control | Empty Slot Info
AC IE includes the information on empty slots.
  Unassociated controlee is able to determine locations of empty slots by parsing the AC IE and thus it can skip parsing the scheduling IE in the same Control Message as the AC IE.
In AC IE, the Association Availability subfield of Content Control field indicates the presence of the Empty Slot Info field
  Empty slots are typically located at the end of each block. The 3-bit Empty Slot Info field should be enough to indicate the number of empty slots located at the end of each block.

## Slide 7: Recap: UWB in-band discovery (2)
Association Request frame format proposed in [1]
  Only Capability Information field is updated
Octets: Variable | 1 | 2 | 2/4
MAC Header | Command ID = 0x01 | Capability Information | FCS
Bits: 0 | 1 | 2-3 | 4 | 5 | 6 | 7 | 8-15
Allocate Address | LDPC | Data rates | MMS ranging | Sensing | DL TDoA | UL TDoA | Reserved
Association Response frame format proposed in [1]
  Only Association Status field is updated
Octets: Variable | 1 | 2 | 1 | 2/4
MAC Header | Command ID = 0x02 | Short Address | Association Status | FCS
Association status | Description
0x00 | Association successful
0x01 | UWB session at capacity
0x02 | Association denied
0x03-0xff | Reserved

## Slide 8
Observation 2
The Association Request and Association Response frame format proposed in [1] are not backward compatible to 802.15.4-2020 and its amendments.
    The valid values of the Capability Information field in the Association Request frame are reused to indicate the 4ab related capability information.
    The valid values of the Association Status field in the Association Response frame are reused to indicate the status especially for UWB in-band discovery.
    4ab related capability information proposed in [1] needs to be updated according to latest consensus on UWB sensing and MMS based ranging.

## Slide 9
Proposal 2
Define a new Header IE or new Nested IE included in the existing Association Request frame or a New Association Request frame to carry 4ab related capability information
  We slightly prefer new Association Request frame.
Enhanced Association Request frame format
Octets: Variable | 1 | 2 | 2/4
MHR | Command ID = 0x0c | Extended Capability Information | FCS
Bits: 0 | 1 | 2 | 3 | 4 | 5 | 6
LDPC | 124.8 Mbps | RSF-only MMS Packet | Mixed MMS Packet | Sensing | SENS1 | SENS2
Bits: 7 | 8 | 9 | 10 | 11-15
Processed CIR report | Strongest detected tap as reference | DL TDoA | UL TDoA | Reserved

## Slide 10
Proposal 2 (cont.)
Octets: Variable | 1 | 2 | 1 | 2/4
MHR | Command ID = 0x02 | Short Address | Association Status | FCS
Association status | Description
0x00 | Association successful
0x01 | PAN at capacity
0x02 | PAN access denied
0x03 | Hopping sequence offset duplication
0x04 | UWB session at capacity
0x05 | Association denied
0x06-0x7f | Reserved
0x80 | Fast association successful
0x81-0xff | Reserved
Association Response frame format
The previously reserved values (e.g. 0x04, 0x05) of the Association Status field in the Association Response frame are used to indicate status especially for UWB in-band discovery.
  The Association Response frame becomes backward compatible.

## Slide 11: Summary
This contribution proposes improvements for UWB in-band discovery as follows:
    Include empty slot information in the Application Control IE to achieve better power efficiency of the unassociated controlee.
    Define a new Association Request frame carrying 4ab related capability information.
    Use previously reserved values of the Association Status field in the Association Response frame to indicate status especially for UWB in-band association to make it backward compatible.
    4ab related capability information is updated according to latest consensus on UWB sensing and MMS based ranging.

## Slide 12: Appendix

## Slide 13: Association Request frame format in 802.15.4
January 2023

## Slide 14: Association Response frame format in 802.15.4
January 2023