## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Compressed Header IE for Control Message]
Date Submitted: [15 January, 2023]
Source: [Kangjin Yoon, Chunyu Hu, Carlos Aldana, Claudio Da Silva] Company [Meta Platforms, Inc.]
E-Mail: [{kyoon, chunyuhu, caldana, claudiodasilva}@fb.com]
Re: [Input to TG4ab]
Abstract: [We propose a new header IE which can be used for Control Message.]
Purpose: [To improve link margin of Control Message]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
PAR Objective | Proposed Solution (how addressed)
Safeguards so that the high throughput data use cases will not cause significant disruption to low duty-cycle ranging use cases | 
Interference mitigation techniques to support higher density and higher traffic use cases | 
Other coexistence improvement | 
Backward compatibility with enhanced ranging capable devices (ERDEVs) | 
Improved link budget and/or reduced air-time | Compressed header IE can reduce the size of Control Message and improve link margin.
Additional channels and operating frequencies | 
Improvements to accuracy / precision / reliability and interoperability for high-integrity ranging | 
Reduced complexity and power consumption | 
Hybrid operation with narrowband signaling to assist UWB | 
Enhanced native discovery and connection setup mechanisms | 
Sensing capabilities to support presence detection and environment mapping | 
Low-power low-latency streaming | 
Higher data-rate streaming allowing at least 50 Mbit/s of throughput | 
Support for peer-to-peer, peer-to-multi-peer, and station-to-infrastructure protocols | 
Infrastructure synchronization mechanisms | 

## Slide 3: Previous Contributions
DCN 604r0 (November 2022) “NBA-MMS-UWB compressed PSDU”
DCN 608r1 (November 2022) “Header IE extension”
DCN 568r1 (November 2022) “Improvements on scheduling IE design in 802.15.4ab”
DCN 500r0 (September 2022) “New Control IE for 4ab applications”
DCN 501r0 (September 2022) “New Scheduling IE for 4ab applications”

## Slide 4: Background
Control Message should have:
  Control information (e.g., ARC IE or Application Control IE)
  Scheduling information (e.g., RDM IE or Scheduling IE)
The PSDU size of Control Message
  [ARC IE + RDM IE]: 31+3*N bytes, where N is the number of list elements
  [AC IE + Scheduling IE]: 27+4*N bytes, where N is the number of list elements
4ab applications may have short frames
  Small sensor data may be transferred (e.g., 30 bytes IMU data)
  MMS ranging utilizes fragmented preamble

## Slide 5: Background
DCN 604r0 and DCN 608r1 proposed to have a compressed Header IE for Control Message
  PSDU of Control Message could be up to 25 bytes or 54 bytes for 250k or 500k O-QPSK PHY
  Proposed to utilize Header IE format to make PSDU short (at least 3 bytes shorter than existing 4z nested payload IE format)
Short PSDU is also preferred for Control Message in UWB channel
  Long Control Message may have lower link margin than other frames (e.g., small sensor data frame or fragmented preamble)

## Slide 6: How to Reduce Control Message Size
Header IE format
  6 bytes overhead  2 bytes overhead
2 B MLME header
2 B Payload IE header
ARC IE
RDM IE
2 B Payload IE header
MSDU

## Slide 7: How to Reduce Control Message Size
Redefining Block Duration field
  Currently, we specify the block duration in the unit of RSTU (~833.33 ns)
  Propose to specify the block duration in units of ranging rounds
  One byte should be enough (255 rounds in a block)
Skipping Block/Round/Slot Duration fields if possible
  ARC IE has fields indicating the presence of each duration fields, but no defined rule on that
  Propose to define and use default values, when the duration field is not present
    Default value of Block Duration field: 1 Round
    Default value of Round Duration field: 1 Slot
    Default value of Slot Duration field: 1200 RSTU (1 ms)

## Slide 8: How to Reduce Control Message Size
Consecutive Slot Scheduling:
  To reduce the number of Scheduling List Elements, we proposed Bitmap-based Scheduling and Periodic Scheduling in [568r1]
  However, when the number of controlees is big and only one slot is scheduled per controlee, bitmap-based scheduling and periodic scheduling are not effective
  Propose to introduce a new scheduling method, Consecutive Slot Scheduling
    See the next slide for more details

## Slide 9: How to Reduce Control Message Size
Consecutive Slot Scheduling (continued):
  Each Scheduling List Element has the Sender Address field only (2 B or 8 B)
  Control Message shall be sent in the Slot 0 (as described in 4z spec)
  The Nth element schedules the slot N to the specified device
  For example, if there are two Scheduling List Elements;
    The 1st element assigns Slot 1 to the device specified in the first element
    The 2nd element assigns Slot 2 to the device specified in the second element
  Caveat: There will be no empty slot between scheduled slots

## Slide 10: Final Control Message Format
One and only header IE for control and scheduling information
Block/Round/Slot Duration Fields can be skipped when default values are used
In most cases, one of application-specific Control fields will be present
Octets: 2 | 0/4 | 0/1 | 0/1 | 0/2 | 0/TBD | 0/TBD | 0/TBD | 0/TBD | Variable
Control | Session ID | Block Duration | Round Duration | Slot Duration | Ranging Control | Data Comm Control | Sensing Control | TDoA Control | Scheduling List
Proposed Header IE Content field

## Slide 11: Final Control Message Format
Control field
  Merge Control fields of AC IE and Scheduling IE [see 500r0 and 568r1]
  Only difference is Scheduling List Type field
    0: (Traditional 4z style) Per-slot scheduling
    1: Consecutive Slot Scheduling
    2: Bitmap-based Scheduling [see 568r1]
    3: Periodic Scheduling [see 568r1]
Bits: 0-3 | 4-5 | 6 | 7 | 8 | 9 | 11 | 12 | 13 | 14 | 15 | 16-23
Scheduling List Length | Scheduling List Type | SIP | RBDP | RRDP | RSDP | Scheduling Mode | RCP | DCP | SCP | TCP | Reserved
Control field

## Slide 12: Example 1: Control Message for Data Communication
Scenario
  8 controlees in a session
  One uplink data from every controlee within 10 ms (100 Hz update rate)
Block Structure
Slot 0 for Control Message
Slot 1 for Controlee 1
10 ms Block (containing 1 Round)
Slot 2 for Controlee 2
Slot 3 for Controlee 3
Slot 4 for Controlee 4
Slot 5 for Controlee 5
Slot 6 for Controlee 6
Slot 7 for Controlee 7
Slot 8 for Controlee 8
Slot 9 is empty
1 ms Slot

## Slide 13: Example 1: Control Message for Data Communication
Control Message with 26 B header IE
  No Block Duration and Slot Duration fields (used default values)
  Only Data Comm Control (expectedly 1 B)
  Consecutive Slot Scheduling
Octets: 2 | 4 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 2*8
Control | Session ID | Block Duration | Round Duration | Slot Duration | Ranging Control | Data Comm Control | Sensing Control | TDoA Control | Scheduling List
Proposed Header IE Content field
Bits: 0-3 | 4-5 | … | 16-23
Scheduling List Length = 8 | Scheduling List Type = 1 | … | Reserved
Octets: 2 | 2 | … | 2
Addr of Cntrlee 1 | Addr of Cntrlee 2 | … | Addr of Cntrlee 8

## Slide 14: Example 2: Control Message for MMS Ranging
Scenario
  One controlee in a session
  One MMS ranging with 32 RIFs within 100 ms (10 Hz update rate)
Block Structure
Slot 0 for Control Message
Slot 1 for RIF 1
100 ms Block (containing 2 Rounds)
…
Slot 32 for RIF 32
Empty slots 33~49
Empty Round
1 ms Slot
50 ms Round
NB frame for Control Message
Choose one

## Slide 15: Example 2: Control Message for MMS Ranging
Control Message with 16+𝛼 B header IE
  No Slot Duration fields (used default values 1 ms)
  Only Ranging Control (the size 𝛼 is TBD)
  Bitmap-based Scheduling
Octets: 2 | 4 | 0 | 1 | 0 | 𝛼 (TBD) | 1 | 0 | 0 | 7
Control | Session ID | Block Duration | Round Duration | Slot Duration | Ranging Control | Data Comm Control | Sensing Control | TDoA Control | Scheduling List
Proposed Header IE Content field
Bits: 0-3 | 4-5 | … | 16-23
Scheduling List Length = 1 | Scheduling List Type = 2 | … | Reserved
Octets: 1 | 4 | 2
Bitmap Length = 2, No offset, … | Bitmap | Address of Controlee

## Slide 16: Thoughts on AC IE and Scheduling IE
Can we replace AC IE and Scheduling IE with the proposed IE?
  Unified header IE: Lower overhead
  AC IE and Scheduling IE: More flexible (can be sent with other IEs)
Options we have:
  [1] Unified header IE only
  [2] AC IE and Scheduling IE with below updates
    Redefining Block Duration field
    Skipping Block/Round/Slot Duration fields if possible
    Consecutive Slot Scheduling
  [3] Unified header IE AND AC IE and Scheduling IE

## Slide 17: Summary
Need to reduce the size of the Control Message for following reasons
  The maximum payload size, which O-QPSK PHY can transmit within 1 ms, is very limited
  Control Message sent in UWB should have similar level of link margin with data frames
Followings are proposed to reduce the size of Control Message
  Unified header IE for control and scheduling
  Redefining Block Duration field
  Skipping Block/Round/Slot Duration fields if possible
  Consecutive Slot Scheduling
The size of the Control Message is significantly reduced in toy examples

## Slide 18: Thank You

## Slide 19: Backup slides

## Slide 20: Control Message Size Comparison
Control Message PSDU size comparison: Control Message with AC IE and Scheduling IE
  15 B for AC IE + 27 B for Scheduling IE + 2 B MLME header = 34 B
 | With Proposed header IE | With AC IE & Scheduling IE
Example 1 (data comm) | 26 B | 34 B
Example 2 (MMS ranging) | 16+𝛼 B | 22+𝛼 B

## Slide 21: Further Possible Optimizations
Automatic slot scheduling for retransmissions
Introducing shorter ID which can be used for scheduling purpose instead of 2 B MAC address