## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Further Discussion on UWB Sensing for 802.15.4ab
Date Submitted: January 17, 2023
Source: Pooria Pakrooh, Bin Tian, Steve Shellhammer, and Koorosh Akhavan (Qualcomm)
E-Mail:{ppakrooh, btian, sshellhammer, kakhavan}@qti.qualcomm.com
Abstract: We share our thoughts on some aspects of UWB sensing that need further discussion and agreement among the group. Specifically, we present more details on CIR report format for UWB sensing as well as considerations for sensing mask.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the authoring individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The authors(s) reserve(s) the right to add, amend or withdraw material contained herein.

## Slide 2
PAR Objective | Proposed Solution (how addressed)
Safeguards so that the high throughput data use cases will not cause significant disruption to low duty-cycle ranging use cases | 
Interference mitigation techniques to support higher density and higher traffic use cases | 
Other coexistence improvement | 
Backward compatibility with enhanced ranging capable devices (ERDEVs) | 
Improved link budget and/or reduced air-time | 
Additional channels and operating frequencies | 
Improvements to accuracy / precision / reliability and interoperability for high-integrity ranging | 
Reduced complexity and power consumption | 
Hybrid operation with narrowband signaling to assist UWB | 
Enhanced native discovery and connection setup mechanisms | 
Sensing capabilities to support presence detection and environment mapping | We share our thoughts on some aspects of UWB sensing that need further discussion and agreement among the group. Specifically, we present more details on CIR report format for UWB sensing as well as considerations for sensing mask.
Low-power low-latency streaming | 
Higher data-rate streaming allowing at least 50 Mbit/s of throughput | 
Support for peer-to-peer, peer-to-multi-peer, and station-to-infrastructure protocols | 
Infrastructure synchronization mechanisms | 

## Slide 3: Introduction
Several contributions on UWB sensing have been discussed in 802.15.4ab [1]-[13].
Some of the main open items were listed in [1], including PHY and MAC aspects of UWB sensing.
Progress was made during last November meeting, summarized as an agreement in [2].
In this presentation, we share more details on the following open topics related to UWB sensing.
  CIR report format for bi/multi-static sensing
  Mask design for sensing pulse shape
  Sensing sequence

## Slide 4: Bi-static Sensing: CIR Report
As noted in the sensing framework document [3], in the window-based CIR report, the CIR measurement report consists of two parts
  Sensing control parameters: Number of Rx antennas, CIR report bitmap length and CIR report bitmap
    CIR window duration (), CIR window offset () can be inferred from the bitmap.
    Control fields are included in the report only when requested by the initiator, to avoid constant overhead.
  Content fields for the CIR measurement report: Including CIR in-phase and quadrature values for each Rx chain, normalization factor for each chain, etc.
The table in the next slide presents our updated baseline CIR report.

## Slide 5: Bi-Static Sensing: CIR Report
Field | Field length (bits) | Comments
Control Fields |  | 
Number of Rx antennas | 2 bits | Up to 4 Rx antennas
Bitmap duration (See slide 9 for details) | 4 bits | 32, 64, 128, 256
Bitmap | Variable, up to 256 bits | Max length=256
Content Fields for Each Rx Chain |  | 
Timing Offset () (See slide 5 for details) | 6 bits | First arrival tap offset from the CIR report grid (chip ratex2 resolution) Could be in units of of chipping period.
Normalization factor for I/Q | TBD | Common normalization value for In-phase and Quadrature CIR values
RSSI | TBD | Indication of per packet power level
CIR In-Phase report | 16 bits | Per tap; normalized
CIR Quadrature report | 16 bits | Per tap; normalized
Field | Field length (bits) | Comments
Control Fields |  | 
Number of Rx antennas | 2 bits | Up to 4 Rx antennas
Bitmap duration (See slide 9 for details) | 4 bits | 32, 64, 128, 256
Bitmap | Variable, up to 256 bits | Max length=256
Content Fields for Each Rx Chain |  | 
 | 6 bits | 
Normalization factor for I/Q | TBD | Common normalization value for In-phase and Quadrature CIR values
RSSI | TBD | Indication of per packet power level
CIR In-Phase report | 16 bits | Per tap; normalized
CIR Quadrature report | 16 bits | Per tap; normalized

## Slide 6: Interpolation of CIR values
      The responder generally estimates channel at a certain time grid, for example at the resolution of twice chip rate.
        Responder further interpolates CIR and estimates the Earliest Arrival Path (EAP) more accurately.
        The estimated EAP generally is used for ranging, and it is not necessarily on the CIR grid.
        For the sensing report, the CIR window is referenced to the EAP.
      But to relieve the burden of interpolation, it is desirable that the responder avoids interpolation across CIR before sending the report (Fig. 1).
        We recommend to report the CIR on the grid (at points ), in addition to first arrival tap offset from the CIR report grid () (Fig. 2).
+2T
…
Earliest detected tap before interpolation
+2T
Earliest detected tap after interpolation
Second tap after interpolation
…
Second tap before interpolation
Fig. 1: (Not preferred) All CIR taps are interpolated before reporting (Green points are reported)
Fig. 2: (Preferred approach) CIR is reported at the grid points. Offset of earliest arrival path and grid point is contained in the report (Blue instances are reported), along with
Notes: 〖Δ𝑡〗_0 is related to the reply time in two way ranging. Le said the reply time is not related to earliest arrival path.
Window offset could be negative to include previous taps as well for interpolation.

## Slide 7: CIR Report Bitmap
  Sensing report bitmap is proposed to signal taps present in the CIR report
    Suggested by Xiliang et. al. during November meetings as an alternative for having one/multiple windows of fixed length for sensing report.
    Details of bitmap determination need to be addressed
      How is the bitmap determined?
      What bitmap parameters need to be specified in the standard?
      Should the bitmap be included in the CIR report?
  Next slide includes some of our high-level thoughts on each of these questions.

## Slide 8: More Details on CIR Report Bitmap
    1. How is the CIR report bitmap determined?
      Initiator proposes the bitmap, based on its sensing area of interest. Responder can further negotiate the bitmap with the initiator based on its capabilities.
      The bitmap is fixed and agreed upon before the sensing session starts.
      Giving responder the freedom to select the taps to report could be concerning.
        Responder may omit different taps in CIR reports for different sensing packets.
          The initiator’s upper layers may want to do extra interpolation across estimated CIRs (often needed for sensing). Missing taps from different packets makes interpolation in the initiator upper layers more challenging.
        Responder does not have enough knowledge of range or reflection level of different objects of interest and may potentially drop CIR taps conveying useful information.
        The saving on report time could not be much as the whole CIR report does not occupy significant airtime.

## Slide 9: More Details on CIR Report Bitmap
    2. What CIR report bitmap parameters need to be specified in the standard?
      If initiator determines the bitmap, responder must prepare to handle arbitrary bit patterns, which could be complicated. To avoid this implementation and testing burden, standard should specify commonly used bitmap patterns
        Options for max length of bitmap (CIR Window length options)
        Subset of bitmap patterns for mandatory support (limiting test burden)
        Choices of offset to reference
    3. Should the CIR report bitmap be included in the CIR report?
      Bitmap does not need to be included in the CIR report. The initiator already knows the CIR bitmap in negotiation step.
      However, to make the report self contained, it could be included it in the report.

## Slide 10: CIR Report Bitmap Options
  Assuming the initiator proposes the CIR report bitmap, below are suggestions on the bitmap parameters
    Maximum bitmap duration
      Depends on maximum CIR duration to be covered, which must be smaller than sensing symbol length.
      At 2x chip rate, 64 taps cover around 20m of sensing range spread.
      However, at larger sampling rates, the coverage scales down with effective sensing BW. We propose four options for bitmap length: M= 32, 64, 128, 256
      At mandatory 2x chip rate CIR sampling, these lengths cover up to 10-80m of sensing range spread.
      Options for offset need to be defined depending on CIR reference
    Mandatory bitmaps to support
      A window is defined as a string of ones
      Two windows of CIR samples within the bitmap duration

## Slide 11: Pulse Shape and Mask
  Agreement among the group to have Kaiser-window as reference pulse for sensing.
  A symmetric time-domain mask has been proposed in [5] to limit pre/post-cursor of sensing pulse.
  However, to limit Tx/Rx cross-correlation shape at the receiver, a correlation mask/metric need to be defined.
    Tx sensing signal , where represents the sensing sequence and is the Tx pulse shape.
    Rx pulse matched filter output = , where is the cross-correlation between Tx and Rx pulse shapes.
    The cross-correlation shape can affect the performance.
  If the time-domain mask proposed in [5] is adopted, a tighter correlation metric than 15.4a is needed. This forces main lobe of the sensing pulse more like the reference pulse, and sidelobes more controlled.
    15.4a correlation metrics (>0.8 for main lobe, <0.3 for sidelobe) are not good enough for sensing.
    Another alternative is to define a tighter time-domain mask.

## Slide 12: Mask for Sensing Pulse Shape
  Example1: Objects at 0 and 4ns . Tx and Rx pulses perfectly match. Both objects are detectable.
  Example 2: Tx and Rx pulses mismatch (Tx= Proposed TD Mask). Weaker object is not detectable.

## Slide 13: Sensing Sequence
For bi/multi-static sensing, we suggest to use the Ipatov sequence
  Sensing performances is based on a channel estimation quality. Thus, the perfect auto-correlation properties of Ipatov sequences helps with sensing weak reflections in the presence of stronger reflectors.
Sensing sequence symbol duration, and the number of symbols need to be decided
  The length of sequence is TBD.
  15.4z Ipatov sequences of length 91 and 127 give around 215 and 300 meters of unambiguous sensing range, with spreading factor of L=4.

## Slide 14: Summary
We shared our thoughts on the following aspects of UWB sensing
  CIR report format for bi/multi-static sensing
  Mas design for sensing pulse shape
  Sensing sequence
Details of the CIR report were updated based on further discussion with the group
  Control and content fields for CIR report
  Thoughts on details for CIR report bitmap
Requirement of a cross-correlation metric or a tighter time-domain mask for sensing pulse shape was discussed.

## Slide 15: References
[1] 15-22-0504-01-04ab UWB Sensing Discussion for 802.15.4ab
[2] 15-22-0650-02-04ab Consensus on UWB Sensing for 802.15.4ab
[3] 15-22-0291-02-04ab Proposal of sensing framework
[4] 15-22-0175-00-04ab Sensing device
[5] 15-23-01-00-04ab Pulse shape and time domain mask for 802.15.4ab
[6] 15-22-0308-04ab Air-time efficiency improvements
[7] 15-22-0066-02-04ab link budget analysis and CIR reporting for UWB RF sensing
[8] 15-22-0061-00-04ab sensing continued
[9] 15-22-0170-00-04ab discussion on UWB sensing report
[10] 15-22-0422-00-04ab UWB sensing scheduling
[11] 15-22-0418-00-04ab Sensing pulse shape consideration in 802.15.4ab
[12] 15-22-0479-04ab More consideration on sensing pulse shape in 802.15.4ab
[13] 15-22-0489-00-04ab UWB sensing sequence selection