## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [NBA-MMS-UWB Native Discovery Concept]
Date Submitted: [January XX, 2022]
Source: [Alexander Krebs, Robert Golshan, Lochan Verma, Jinjing Jiang, Yong Liu, SK Yong (Apple)]
Email: krebs @ apple.com
Re: [Input to the Working Group]
Abstract: [Discovery and association protocol for NBA-MMS-UWB sessions using in-band 802.15.4 radio only.]
Purpose: []
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
PAR Objective | Proposed Solution (how addressed)
Safeguards so that the high throughput data use cases will not cause significant disruption to low duty-cycle ranging use cases | 
Interference mitigation techniques to support higher density and higher traffic use cases | 
Other coexistence improvement | 
Backward compatibility with enhanced ranging capable devices (ERDEVs) | 
Improved link budget and/or reduced air-time | 
Additional channels and operating frequencies | 
Improvements to accuracy / precision / reliability and interoperability for high-integrity ranging | 
Reduced complexity and power consumption | 
Hybrid operation with narrowband signaling to assist UWB | 
Enhanced native discovery and connection setup mechanisms | Generic native discovery concept for MMS ranging, applicable to NBA and/or UWB only
Sensing capabilities to support presence detection and environment mapping | 
Low-power low-latency streaming | 
Higher data-rate streaming allowing at least 50 Mbit/s of throughput | 
Support for peer-to-peer, peer-to-multi-peer, and station-to-infrastructure protocols | 
Infrastructure synchronization mechanisms | 

## Slide 3: Related Contributions
[1, 2] NBA-MMS-UWB Technical Framework and MAC
[3, 4] UWB Channel Usage Coordination
  L. Verma (Apple), M. Lee (Samsung), W. Kuchler (NXP) et al., Nov. 2022
[5] “UWB In-band Discovery”, Kangjin Yoon (Meta), Nov. 2022, 15-22-0646-00-04ab.
[6] “Draft text for UWB wake-up radio”, Billy Verso, Michael McLaughlin (Qorvo), Nov. 2022, 15-22-0654-00-04ab.

## Slide 4: Scope of this contribution
Enable two, or more devices to start a first ranging exchange via 802.15.4 PHYs
  Devices are assumed to be able to identify each other
  Not in scope: pairing, identity resolution, key exchange, …
P2P ranging session (1 Initiator + 1 Responder)
  Not in scope here: one-to-many, many-to-many, …
Generic procedure, common to applicable 15.4 PHYs
  Not in scope: specific PSDU formats

## Slide 5: Discovery and Acquisition Packets
3 MAC packets types (not PHY specific)
  ADV-POLL: advertising identity and protocol version of the initiator, may be sent repetitively to the discretion of the initiator
  ADV-RESP: acquisition request, sent by the responding device upon receiving ADV-POLL
    channel selection parameters, MMS fragment configuration, MMS preamble parameters, NB data rate, etc.
  SOR: start of ranging indication packet, sent by the initiator upon receiving ADV-RESP
    final confirmation of ADV-RESP parameters (updated, if needed)
    time offset to next MMS POLL packet

## Slide 6: Discovery Channels for NB
Discovery is time critical for ranging to start
  Packet collisions may delay start of ranging
2 possible NB channels in UNII-3 non-overlapping with 802.11
  Good candidate as default channel for discovery
  Other channel may be configured via OOB
From: “Coexistence discussion on narrowband assisted UWB”, Bin Tian et al., 802.15-22-0261-00-04ab

## Slide 7: Discovery Walk-through Example
Discovery phase
  Initiator sends one, or more ADV-POLL packets
  Responder scans pre-defined discovery channel sporadically

## Slide 8: Discovery Walk-through Example
Association phase
  Initiator and Responders handshake ranging configuration via ADV-RESP and SOR
    Initiator sends POLL after announced time offset
    Responder awaits POLL at announced time offset

## Slide 9: Discovery Walk-through Example
Ranging phase
  Initiator may cease, or continue advertising depending on e.g.
    whether MMS exchanged has been performed successfully
    One, or more additional responders are awaiting discovery

## Slide 10: Summary
Discovery and acquisition via ADV-POLL, ADV-RESP, SOR packets
  Generic to NB-OQPSK and UWB 802.15.4 PHYs
OOB methods may additionally be used to
  roughly coordinate TX/RX timings of AP packets
  configure alternative discovery configuration (e.g. channel, PHY mode)

## Slide 11: References
[1] X. Luo (Apple Inc), F. Leong (NXP), M. Lee (Samsung Electronics), et al., “NBA-UWB Technical Framework Proposal”, 15-22-0571-01-04ab.
[2] A. Krebs et al., “Updates on Narrowband Channel Allocation and Access”, 15-22-0493-02-04ab.
[3] L. Verma (Apple), M. Lee (Samsung), W. Kuchler (NXP), et al., “UWB Channel Usage Coordination for better UWB Coexistence”, 15-22-0456-00-04ab.
[4] L. Verma (Apple) et al., ”Follow-up on UWB Channel Usage Coordination”, 15-22-0573-00-04ab.
[5] Kangjin Yoon (Meta), “UWB In-band Discovery”, 15-22-0646-00-04ab.
[6] Billy Verso et al. (Qorvo), “Draft text for UWB wake-up radio”, 15-22-0654-00-04ab.