## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Enhanced poll and report based on compressed PSDU for NBA-MMS UWB
Date Submitted: January 2023
Source: Kuan Wu, Lei Huang, Bin Qian, Rojan Chitrakar, David Xun Yang (Huawei Technologies)
Email: wukuan2@huawei.com
Abstract: Introducing enhanced designs of request and report messages in compressed PSDU format for NBA-MMS UWB applications
Purpose: Enhancing the design of messages in compressed PSDU format for NBA-MMS UWB
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
PAR Objective | Proposed Solution (how addressed)
Safeguards so that the high throughput data use cases will not cause significant disruption to low duty-cycle ranging use cases | 
Interference mitigation techniques to support higher density and higher traffic use cases | 
Other coexistence improvement | 
Backward compatibility with enhanced ranging capable devices (ERDEVs) | 
Improved link budget and/or reduced air-time | 
Additional channels and operating frequencies | 
Improvements to accuracy / precision / reliability and interoperability for high-integrity ranging | 
Reduced complexity and power consumption | 
Hybrid operation with narrowband signaling to assist UWB | To enhance the design of messages in compressed PSDU format for NBA-MMS UWB
Enhanced native discovery and connection setup mechanisms | 
Sensing capabilities to support presence detection and environment mapping | 
Low-power low-latency streaming | 
Higher data-rate streaming allowing at least 50 Mbit/s of throughput | 
Support for peer-to-peer, peer-to-multi-peer, and station-to-infrastructure protocols | 
Infrastructure synchronization mechanisms | 

## Slide 3
References
1. IEEE Standard for Low-Rate Wireless Networks–Amendment 1: Enhanced Ultra Wideband (UWB) Physical Layers (PHYs) and Associated Ranging Techniques, IEEE Standard 802.15.4z-2020 (Amendment to IEEE Standard 802.15.4-2020)
2. DCN 604r0 (November 2022) “NBA-MMS-UWB Compressed PSDU”
3. IEEE Standard for Low‐Rate Wireless Networks IEEE Std 802.15.4‐2020
4. DCN 378r0 (July 2022) “On the selection of number of fragments in MMS-UWB”
5. DCN 659r1 (November 2022) “Further thoughts on the MAC of the NBA-MMS UWB”

## Slide 4
Recap: Compressed PSDU format for NB message(s)
As compared with 802.15. 4z nested IE format [1], a compressed PSDU format [2] specific to NBA-MMS-UWB control frames is proposed for efficient transmission of ranging measurement information
  Baseline 250k O-QPSK NB PHY has limited PSDU capacity
  To keep NB packets duration shorter than 1ms  Good for energy consumption, radio co-existence, CFO estimate and etc.
Compressed PSDU format specific to NBA-MMS-UWB [2]
General format of Nested IE in legacy 4z (minimal configuration) [1]
Multiple nested IEs can be included in the same PSDU
Octets: 1 | 2 | Variable | 2
Message ID | Address | Content | CRC
SHR | PHR | Compressed PDSU
Bits: 0-6 | 7
Frame Length | TBD
SHR | PHR | PSDU (legacy 4z)
Octets: 4 | 2 | Variable | Variable | … | Variable | 2
MAC header | MLME header | Nested IE | Nested IE | … | Nested IE | CRC
Octets:2 | Variable | Variable
Nested IE header | Configuration Field for Bitmask + length | Content

## Slide 5
Recap: Compressed PSDU format for NB message(s) (cont.)
Example case [2]: reporting 1 ranging TOF result
TOF in legacy 4z RMI IE: 70.4% TX occupancy in 1ms @ baseline 250kbit/s O-QPSK PHY [3]
Octets: 1 | 2 | 4 | 2
Message ID | Address | TOF | CRC
SHR | PHR | Compressed PDSU
SHR | PHR | PSDU (legacy 4z)
Octets: 4 | 2 | Variable | Variable | … | Variable | 2
MAC header | MLME header | Nested IE | Nested IE | … | Nested IE | CRC
Octets:2 | 2 | 4
Nested IE header | Configuration Field for Bitmask + length | TOF
TOF in compressed PSDU: 48.0% TX occupancy in 1ms @ baseline 250kbit/s O-QPSK PHY

## Slide 6
Recap: Updating the number of fragments in NBA-MMS UWB
Dynamic # of fragments selection based on UWB channel conditions [4]-[5].
  Feedback of recommended number of fragments (RNF) from responder to the initiator
Observation:
  The feedback of RNF is not subject to the request from the initiator/controller side. Unneeded/uncontrolled feedback may consume unnecessary NB message overhead

## Slide 7
Recap: Agile Frequency Hopping
Adaptive Frequency Hopping (AFH) is applied in NBA-MMS UWB [5]
  To mitigate Wi-Fi interference
  To use Wi-Fi non-occupied spectrum in priority
  A new IE is designed to indicate AFH map in NBA-MMS UWB, which is efficient and flexible
Wi-Fi non-occupied channels | Wi-Fi channels (20MHz) | Scaling Factor (SF)
B0
UNII-3(5725-5850)
144
5725
5730
149
5735
5740
5745
5750
153
…
…
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
B3
B9
B11
SF = 3/4
111101111101
AFH Map IE
Wi-Fi ch
NB ch
Format of the AFH map proposed in [5]

## Slide 8
Motivation
To enable the aforementioned functionalities in the compressed PSDU form in NBA-MMS UWB ranging
  RNF request for updating the number of fragments
  AFH map indication

## Slide 9
Proposal 1: Poll piggybacking extended functionality
Joint exploiting Frame Length and Message ID to carry Poll with Extended Functionality
  Introducing 1-octet/2-octet for Extended Functionality field in the data content field
  Reusing message ID of Poll message  Not introducing new message IDs
  TX occupancy in 1ms is less than 50%  following the considerations for NB compression
Frame Length (octet) | Message ID | Data Content Description | TX occupancy in 1ms duration (@ baseline 250kbit/s O-QPSK PHY)
5 | 0x00 | Poll | 35.2%
6 |  | Poll with 1-octet piggybacking information | 38.4%
7 |  | Poll with 2-octet piggybacking information | 41.6%
Octets: 1 | 2 | 1/2 | 2
Message ID 0x00 | Address | Piggybacking information content | CRC
SHR | PHR | PHY payload

## Slide 10
Proposal 1: Poll piggybacking extended functionality (cont.)
Octets: 1 | 2 | 1 | 2
Message ID 0x00 | Address | Piggyback information content | CRC
SHR | PHR | PHY payload
Bits: 0 | 1-7
RNF Request | Reserved
Poll with 1-octet piggybacking information
  Poll message piggybacks RNF request for updating the number of fragments
Poll with 2-octet piggybacking information
  Besides RNF request, the poll message also piggybacks the Agile Frequency Hopping (AFH) map [5] information in the content
Octets: 1 | 2 | 2 | 2
Message ID 0x00 | Address | Piggyback information content | CRC
SHR | PHR | PHY payload
Bits: 0 | 1-12 | 13-15
RNF Request | AFH map | Reserved

## Slide 11
Proposal 2: Report piggybacking extended functionality
Joint exploiting Frame Length and Message ID to carry report with Extended Functionality
  Introducing 1 octet for Report with extended functionality field in the data content field
  Not introducing new message IDs to distinguish different ranging measurement reports  Saving the number of message IDs
Frame Length (octet) | Message ID | Data Content Description | TX occupancy in 1ms duration (@ baseline 250kbit/s O-QPSK PHY)
10 | TBD | Report with extended functionality | 51.2%
Octets: 1 | 2 | 1 | 4 | 2
Message ID 0x02 | Address | Report Control | Ranging Measurement Report | CRC
SHR | PHR | PHY payload
Bits: TBD | TBD | TBD
RNF Report presence control | RNF | Ranging Measurement Report Selection (RMRS)
The detailed formats of RNF and RNF Report presence control are TBD.

## Slide 12
Proposal 2: Report piggybacking extended functionality (cont.)
Octets: 1 | 2 | 1 | 4 | 2
Message ID 0x02 | Address | Report Control | Ranging Measurement Report | CRC
SHR | PHR | PHY payload
Bits: TBD | TBD | TBD
RNF Report presence control | RNF | Ranging Measurement Report Selection (RMRS)
RMRS values | Description
0 | Ranging Measurement Report field contains TOF result
1 | Ranging Measurement Report field contains RT result
2 | Ranging Measurement Report field contains RTT result
Other values | Reserved
The Ranging Measurement Report Selection (RMRS) field in the Report Control field determines the content of the ranging measurement report
  Including TOF, Reply Time (RT), Round Trip Time (RTT), and etc

## Slide 13
Summary
  In this contribution, we introduce the enhanced poll and report messages in the form of compressed PSDU for NBA-MMS UWB applications
    Allowing poll message piggybacking extended functionality with RNF request and/or AFH map information
    Allowing report message piggybacking extended functionality with RNF report and ranging measurement report