## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: ChannelNumber Issue
Date Submitted: 14h March, 2023
Source: Tero Kivinen Company -
E-Mail: kivinen@iki.fi
Re: Removal of ChannelPage from revision
Abstract:
Proposal for solving the issue with ChannelNumber and ChannelPage
Purpose: Propose a solution for ChannelNumber/ChannelPage issue
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
ChannelPage
In the last TG4me meeting the TG decided to remove ChannelPage.
This causes the issue that we have MLME calls that used to provide ChannelPage and ChannelNumber and now only provide ChannelNumber

## Slide 3
ChannelNumber
The problem with ChannelNumber is that it does not specify the actual channel to be used.
Actual frequence depends on:
    Phy to be used
    Operating band used
    Operating mode used
    Actual Channel number

## Slide 4
ChannelNumber
Not all PHYs have all those information so the Channel information is always going to be PHY specific.

## Slide 5
Proposal
Replace ChannelNumber with ChannelInfo
ChannelInfo is specified as PHY specific information that specifies all required information that is needed to specify channel.

## Slide 6
Example SUN FSK PHY
ChannelInfo contains:
    PHY: SUN FSK
    Band: 915-b
    Operation Mode: #5
    Channel Number: 11
    This matches: 902.2+0.4*11 = 906.6 MHz, with ChannelSpacing of 0.4 MHz

## Slide 7
Solves
All PIB and MLME issues are solved with this.
All MLME calls that take ChannelNumber will be taking ChannelInfo instead:
    MLME-ASSOCIATE.request
    MLME-BEACON-NOTIFY.indication
    MLME-START.request
    MLME-SYNC.request
    MLME-SYNC-LOSS.indication
    MLME-DPS.request, response, confirm
    MLME-SRM-REPORT.request, indication
    MLME-SRM-NFORMATION.request
    MLME-SRM-REQ.request, indication
    MLME-SRM-RES.request, indication

## Slide 8
Issues
IEs:
    O-QPSK PHY Mode IE: Channel Index (8-bit)
    LECIM DSSS Operating mode: Channel Number (9-bit)
    LECIM FSK Operating mode: Channel Number (9-bit)
    LECIM FSK Split Operating mode: Channel Number (16-bit)
    TVWS PHY Operating Mode Description IE: PHY Channel ID (8-bit)
    RCC PHY Operating Mode IE: Channel Number (14-bit)
    Ranging Channel and Preamble Code Selection IE: Channel Number (5-bit)
All of those are for one specific PHY so there should not be real issues, they can simply use the channel number as defined in 10.1.3.

## Slide 9
Issues
MAC Commands:
    Coordinator Realignment command: Channel Number, Channel Page (8-bit)
    DSME Association Response Command: Channel Index (16-bit)
    DSME GTS Response command: Channel Index (16-bit)
    DBS Response command: Allocate PHY Channel Number (8-bit)
    SRM Request command: Channel Number, Channel Page (16-bit)
Here the Coordinator realignement and SRM Request commands are real issues, as they had also the Channel Page

## Slide 10
Coordinator Realignment command
Is anybody using it in a way where they used to change from one channel page to another.
    If not then we can simply ignore the issue.
    If yes, we need information how they thought is was supposed to work.
Proposed solution: Ignore issue, and remove channel page.

## Slide 11
SRM Request command
Is there a need to do SRM over multiple channel pages?
    The channel pages have been so badly defined so I doubt there are any implementations of SRM that would care.
Proposed solution: Ignore issue, and remove channel page.