## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Updates on UWB Discovery and Association]
Date Submitted: [15 March, 2023]
Source: [Kangjin Yoon, Chunyu Hu, Carlos Aldana, Claudio Da Silva (Meta Platforms, Inc.);
Lei Huang, Kuan Wu, Bin Qian, David Xun Yang, and Rojan Chitrakar (Huawei)]
E-Mail:[kyoon@meta.com, lei.huang1@Huawei.com]
Re: [Input to TG4ab]
Abstract: [UWB in-band discovery protocol has been proposed.]
Purpose: [To have the UWB in-band discovery protocol.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
PAR Objective | Proposed Solution (how addressed)
Safeguards so that the high throughput data use cases will not cause significant disruption to low duty-cycle ranging use cases | 
Interference mitigation techniques to support higher density and higher traffic use cases | 
Other coexistence improvement | 
Backward compatibility with enhanced ranging capable devices (ERDEVs) | 
Improved link budget and/or reduced air-time | 
Additional channels and operating frequencies | 
Improvements to accuracy / precision / reliability and interoperability for high-integrity ranging | 
Reduced complexity and power consumption | 
Hybrid operation with narrowband signaling to assist UWB | 
Enhanced native discovery and connection setup mechanisms | UWB-based discovery and association
Sensing capabilities to support presence detection and environment mapping | 
Low-power low-latency streaming | 
Higher data-rate streaming allowing at least 50 Mbit/s of throughput | 
Support for peer-to-peer, peer-to-multi-peer, and station-to-infrastructure protocols | 
Infrastructure synchronization mechanisms | 

## Slide 3: Previous Contributions Related To Discovery
[1] DCN 646r0 (November 2022) “UWB In-band Discovery”
[2] DCN 002r1 (January 2023) “Improvements on UWB in-band discovery”
[3] DCN 033r2 (January 2023) “nba mms uwb native discovery concept”

## Slide 4: Background
Two approaches on device discovery and association
 | UWB-based | NB-based
Ref. | DCN 646r0, 002r1 | DCN 033r2
Pros | No NB hardware requirement Simple design (without NB-to-UWB handover) | Long range Power efficient for scanning
Suits when | MMS fragments are not used Discovery can be triggered when needed (e.g., wearable connection) | MMS fragments are used Controlees need to scan all the time (e.g., passive access sys.)
For devices without NB, we need UWB-based discovery and association protocol

## Slide 5: Background
Recap of DCN 646r0, 002r1:
Controller
Associated Controlee
Unassociated Controlee
AC IE (Association Availability = 1, Empty Slot Info), Scheduling IE
Association Request command (Capability Information) in one of empty slot
Scheduled traffic
AC IE (Association Availability = 1, Empty Slot Info), Scheduling IE
Association Response command (Association Status) in a scheduled slot
Scheduled traffic
Block N
Block N+1

## Slide 6: Background
Recap of DCN 646r0, 002r1:
Octets: 2 | 0/4 | 0/1 | 0/1 | 0/2 | 0/variable | 0/TBD | 0/TBD | 0/TBD | 0/TBD | 0/TBD
Content Control | Session ID | Block Duration | Round Duration | Slot Duration | Contention Phase Structure | Ranging Control | Data Comm Control | Sensing Control | TDoA Control | Empty Slot Info
Bits: 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10-15
SIP | RBDP | RRDP | RSDP | Scheduling Mode | Association Availability | RCP | DCP | SCP | TCP | Reserved
Content Control field of the Application Control IE
Application Control IE

## Slide 7: Update #1: Contention Slots Info
Empty Slot Info field was only for Association Request commands
Propose renaming the field to ‘Contention Slots Info’ and expanding its utilization for other objectives (e.g., intermittent data or other future usage)
Octets: 2 | 0/4 | 0/1 | 0/1 | 0/2 | 0/TBD | 0/TBD | 0/TBD | 0/TBD | 0/TBD
Content Control | Session ID | Block Duration | Round Duration | Slot Duration | Contention Slots Info | Ranging Control | Data Comm Control | Sensing Control | TDoA Control
Bits: 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11-15
SIP | RBDP | RRDP | RSDP | Scheduling Mode | Association Availability | Contention Slots Info Present (CSIP) | RCP | DCP | SCP | TCP | Reserved
Content Control field of the Application Control IE
Application Control IE

## Slide 8: Update #1: Contention Slots Info
Contention Slots Start: The index of the first slot which can be used without prior scheduling
Contention Slots Size: The number of slots, starting from the slot specified by the Contention Slots Start field, that can be utilized without prior scheduling
Bits: 0-3 | 4-7
Contention Slots Start | Contention Slots Size
Contention Slots Info field of the AC IE

## Slide 9: Update #2: Short Address Assignment
Short address assignment in 802.15.4
  Controlee uses 8B extended address for the Association Request command
  Controller generates and conveys 2B short address in Association Response command (still need to use 8B address in MHR)
  Controller and controlee use the assigned 2B address afterward
Controller
Controlee
…
Sender Address: Extended (8B)
Association Request command
New Short Address (2B)
Receiver Address: Extended (8B)
Association Response command
…

## Slide 10: Update #2: Short Address Assignment
Motivation
  Want to reduce the size of Association Request/Response commands
  Achieve higher Tx power & lower chance of collision
Proposal
  Controlee generates 2B short address
  Controller uses the 2B address unless duplicated
  In the most scenario, the chance of duplication is very low
Controller
Controlee
…
Sender Address: Short (2B)
Association Request command
Receiver Address: Short (2B)
Association Response command
…
Controller
Controlee
…
Sender Address: Extended (8B)
Association Request command
New Short Address (2B)
Receiver Address: Extended (8B)
Association Response command
…

## Slide 11: Update #3: New MAC commands for HRP UWB Association
Propose add new Association Request/Response command for HRP UWB
Command ID | Command name | RFD |  | Subclause
 |  | TX | RX | 
0x29-0xff2f | Reserved |  |  | 
0x30 | HRP UWB Association Request command | X |  | 7.5.31
0x31 | HRP UWB Association Response command |  | X | 7.5.32
0x32-0xff | Reserved |  |  | 
Table 7-53 – MAC commands

## Slide 12: Update #3: New MAC commands for HRP UWB Association
HRP UWB Association Request command
Octets: 4 | TBD
Session ID | UWB HRP Capability Information
HRP UWB Association Request command Content field format
Bits: 0 | 1 | 2–3 | TBD
LDPC | High Throughput (124.8 Mbps) | Supported AIFS | TBD
Supported AIFS field value | Supported AIFS (refer DCN 71r0)
0 | 64 us
1 | 64, 32 us
2 | 64, 32, 16 us
3 | Reserved

## Slide 13: Update #3: New MAC commands for HRP UWB Association
HRP UWB Association Response command
Octets: 1 | 0/TBD
Association Status | Session Configuration
HRP UWB Association Response command Content field format
Association Status | Description
0x00 | Association successful
0x01 | Session at capacity
0x02 | Short address duplication
0x03 | Association denied by other reason
0x04–0xff | Reserved
Session Configuration field format is TBD

## Slide 14: Summary
Contention Slots Info field is introduced instead of Empty Slot Info field to maximize potential utilization
New short address assignment protocol is proposed to minimize the size of MAC commands
Detailed formats of HRP UWB Association Request/Response commands are proposed

## Slide 15: Thank You