## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Some thoughts on 4ab device classes
Date Submitted: March, 2023
Source: Vinod Kristem, Xiliang Luo, Moche Cohen (Apple)
Address: One Apple Park Way, Cupertino, CA 95104, USA
E-Mails: vkristem@apple.com
Abstract: Initial thoughts on defining the 4ab device categories and device class
Purpose: To discuss the feasibility of defining the device categories and device classes in 4ab
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
        doc.: 15-23-0177-00-04ab

## Slide 2
PAR Objective | Proposed Solution (how addressed)
Safeguards so that the high throughput data use cases will not cause significant disruption to low duty-cycle ranging use cases | Defines device categories
Interference mitigation techniques to support higher density and higher traffic use cases | Defines device categories
Other coexistence improvement | Defines device categories
Backward compatibility with enhanced ranging capable devices (ERDEVs) | Defines device categories
Improved link budget and/or reduced air-time | Defines device categories
Additional channels and operating frequencies | Defines device categories
Improvements to accuracy / precision / reliability and interoperability for high-integrity ranging | Defines device categories
Reduced complexity and power consumption | Defines device categories
Hybrid operation with narrowband signaling to assist UWB | Defines device categories
Enhanced native discovery and connection setup mechanisms | Defines device categories
Sensing capabilities to support presence detection and environment mapping | Defines device categories
Low-power low-latency streaming | Defines device categories
Higher data-rate streaming allowing at least 50 Mbit/s of throughput | Defines device categories
Support for peer-to-peer, peer-to-multi-peer, and station-to-infrastructure protocols | Defines device categories
Infrastructure synchronization mechanisms | Defines device categories
        doc.: 15-23-0177-00-04ab

## Slide 3: Introduction
Many new interesting features have been proposed in 4ab
  Enhanced Data Communications
    Data rates up to 124.8 Mb/s
    LDPC coding
    Dynamic PHR
    ….
  Enhanced ranging with MMS
    NBA-MMS
    RSF, RIF, Mixed MMS
    MMRS
    ….
  Sensing
    Sensing with Ipatov 91 codes
    Sensing, Sensing+Data comm
    Frequency stitching
    ….
10’s of config. parameters per feature, huge parameter set!!!
Single 4ab device support all of them?
        doc.: 15-23-0177-00-04ab

## Slide 4: Device categories in 4ab
It might be good to categorize the 4ab device(s) based on the feature set
Further division into multiple classes
  Class A devices targeting low cost/complexity/simple extensions
  Class B devices targeting high performance
Simplify parameter set definition, inter-operability, testing burden
Vendor can target for the specific category of interest
        doc.: 15-23-0177-00-04ab
4z Data rates
4z PHR
1.95, 62.4, 124.8 Mb/s
Dynamic PHR
4z BCC
LDPC
4z Ipatov
4z STS
MMRS
NBA
RSF Only MMS
Mixed MMS
4ab Ranging device
CIR report
Sensing Seq
Freq. stitching
4ab Sensing device
4ab Data device

## Slide 5: 4ab Data device
Several data enhancements introduced in 4ab
  High data rate modes for improved throughput
    62.4 Mb/s
    124.8 Mb/s
  Low data rate mode for improved link budget
    1.95 Mb/s
  Advanced coding schemes for better link budget
    LDPC, in addition to K = 7 BCC
  New PHR targeting low latency streaming
    Dynamic PHR to support rapidly varying channel conditions
        doc.: 15-23-0177-00-04ab

## Slide 6: 4ab Data device classes
Enhanced Data device: lower complexity and simple extension
Advanced Data device: superior performance
Packet format could be defined for each device class
        doc.: 15-23-0177-00-04ab
4z Data rates
4z PHR
1.95, 62.4, 124.8 Mb/s
Dynamic PHR
4z BCC
LDPC
4ab Enhanced Data device
4ab Advanced Data device
4z Sync

## Slide 7: Summary
4ab group could look into defining device categories and the device class
  Simplifies parameter set definition, reduce testing burden, better UWB ecosystem
        doc.: 15-23-0177-00-04ab
4z Data rates
4z PHR
1.95, 62.4, 124.8 Mb/s
Dynamic PHR
4z BCC
LDPC
4ab Enhanced Data device
4ab Advanced Data device
4z Ipatov
4z STS
MMRS
NBA
RSF Only MMS
Mixed MMS
4ab Ranging device
CIR report
Sensing Seq
Freq. stitching
4ab Sensing device