## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Frequency Stitching Considerations]
Date Submitted: [16 March, 2023]
Source: [Frank Leong, Wolfgang Küchler, Riku Pirhonen, Bernhard Großwindhager, Andreas Gruber, Stefan Tertinek, David Veit] Company [NXP Semiconductors]
Re: [Input to the Working Group]
Abstract: [Presentation, UWB, sensing, scheduling, frequency stitching]
Purpose: []
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
PAR Objective | Proposed Solution (how addressed)
Safeguards so that the high throughput data use cases will not cause significant disruption to low duty-cycle ranging use cases | 
Interference mitigation techniques to support higher density and higher traffic use cases | 
Other coexistence improvement | 
Backward compatibility with enhanced ranging capable devices (ERDEVs) | 
Improved link budget and/or reduced air-time | Combining ranging and sensing
Additional channels and operating frequencies | 
Improvements to accuracy / precision / reliability and interoperability for high-integrity ranging | Frequency stitching
Reduced complexity and power consumption | 
Hybrid operation with narrowband signaling to assist UWB | 
Enhanced native discovery and connection setup mechanisms | 
Sensing capabilities to support presence detection and environment mapping | Monostatic and multistatic radar operation
Low-power low-latency streaming | 
Higher data-rate streaming allowing at least 50 Mbit/s of throughput | 
Support for peer-to-peer, peer-to-multi-peer, and station-to-infrastructure protocols | 
Infrastructure synchronization mechanisms | 

## Slide 3: Frequency Stitching Considerations

## Slide 4: Recap: Scheduling Options
Frequency
CM
CM = Control Message SF = Sensing Fragment
Time
SF
SF
SF
Frequency
CM
Time
SF
SF
SF
CM
CM
Frequency
CM
Time
SF
SF
SF
Dedicated Control Channel (e.g., Narrowband PHY)
Control on Main UWB Channel
Control on All UWB Channels

## Slide 5: Frequency Stitching – Considerations
Timescale
  SENS field / segments, SYNC (intra-packet)
  Multiple packets within one or more time-slots (inter-packet)
Achieve coherence across all employed channels for each measurement (i.e., for each update, for each CIR Estimate)
  Short total time span per update is good
  Long total time span per update may be problematic (depending on application)

## Slide 6: Frequency Stitching – Channel Order
Overlap between adjacent channels leads to Mean EIRP accumulation when minimizing total time span
  For sequential channel ordering, this may lead to power loss
  Mitigated by grouping non-overlapping channels into sets of millisecond-long windows
Grouping can be done in three ways
  Across segments in the SENS field (intra-packet)
  Across multiple packets (inter-packet – this will also work for the SYNC field in legacy 4z packet types)
  A combination of the above

## Slide 7: Out-Of-Sequence Channel Order (I)
Consider an integer numbered set of equidistantly spaced channels (CH(k))
  Typical spacing would be ({1,2,3}/4) * 499.2 MHz
Consider the aggregate sensing bandwidth to be defined according to number of occupied channels N: CH(0) ... CH(N-1)
Consider the Overlap Factor (OF), which is the number of channels overlapping with a channel at the edge of the selected set of channels (i.e., worst-case single-sided overlap for all of the selected channels)
  Of relevance: (CH spacing, OF) pairs (499.2 MHz, 0), (374.4 MHz, 1), (249.6 MHz, 1), (124.8 MHz, 3)

## Slide 8: Out-Of-Sequence Channel Order (II)
Step through according to: CH((p*(OF+1) MOD (N)) + (p*(OF+1) DIV (N))), where p = 0 ... (N-1) and DIV denotes integer division
Start transmitting at t = 0
  The first wrap occurs after t ≥ 1 millisecond
CH(0) ... CH(N-1) is padded such that N is divisible by (OF+1)
  Padding with “unused” channels → idle transmitter

## Slide 9: Out-Of-Sequence Channel Order (III)
Step through according to: CH((p*(OF+1) MOD (N)) + (p*(OF+1) DIV (N))), where p = 0 ... (N-1) and DIV denotes integer division
Frequency
Time
SF
SF
SF
≥1 millisecond
OF+1
SF
SF
SF
CH(0)
CH(2)
CH(4)
CH(1)
CH(3)
CH(5)
Example: OF = 1, N = 6 → p = 0 ... 5