## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Discussion on NBA-MMS-UWB MAC]
Date Submitted: [March 16, 2022]
Source: [Alexander Krebs (Apple)]
Email: krebs @ apple.com
Re: [Input to the Working Group]
Abstract: [Group discussion on protocol for NBA-MMS-UWB sessions.]
Purpose: []
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
PAR Objective | Proposed Solution (how addressed)
Safeguards so that the high throughput data use cases will not cause significant disruption to low duty-cycle ranging use cases | 
Interference mitigation techniques to support higher density and higher traffic use cases | 
Other coexistence improvement | 
Backward compatibility with enhanced ranging capable devices (ERDEVs) | 
Improved link budget and/or reduced air-time | Improved session startup and discussion
Additional channels and operating frequencies | 
Improvements to accuracy / precision / reliability and interoperability for high-integrity ranging | 
Reduced complexity and power consumption | 
Hybrid operation with narrowband signaling to assist UWB | 
Enhanced native discovery and connection setup mechanisms | 
Sensing capabilities to support presence detection and environment mapping | 
Low-power low-latency streaming | 
Higher data-rate streaming allowing at least 50 Mbit/s of throughput | 
Support for peer-to-peer, peer-to-multi-peer, and station-to-infrastructure protocols | 
Infrastructure synchronization mechanisms | 

## Slide 3: Agenda
Additional NB-MMS discovery modes (30min)
MMS MAC TFD open items (30min)

## Slide 4: Coordination vs Initialization/Discovery
Coordination (Mingyu et. al, DCN 67, Baltimore)
  Devices broadcast own scheduling information in AP packets
  Devices scan for AP packets to learn about unoccupied network resources
Discovery/Initialization (Alex et. al, DCN 33, Baltimore)
  Peer-to-peer handshake between Initiator and responder for MMS configuration
  Triggers start of MMS ranging upon success
Discussion
  Initialization carries privacy sensitive information that needs to be protected
  Coordination must not broadcast privacy sensitive information
Proposal/Conclusion:
  keep as separate methods, merge would simplify, but limit functionality
  Add coordination to MMS MAC TFD document with tbd scope

## Slide 5: Coordination after Handshake
Relevant for non-triggered use cases (e.g., background activity)
  Coordination AP information is only relevant in the moment of handshake
  Scanning for AP information ahead of handshake is energy draining
“Initiator shall RX for ADV-RESP after ADV-POLL” (DCN 381)
“Initiator may TX SOR after ADV-RESP” (DCN 381)
Means: Initiator may decide to not start ranging after ”discovery” of responder, scan for coordination APs for arbitrary duration, then TX ADV-POLL again to handshake

## Slide 6: Coordination after Handshake
Improvement (Mingyu et. al, DCN 150, Atlanta) + 4ab Brainstorming
  Initiator advertising (non-trigger based) can save power by deferring scanning for coordination AP by using ADV-CONF instead of SOR
  ADV-CONF defers SOR through time offset announcement
  Initiator scans for AP information, then commits to sending SOR
  Pro: Responder knows exact time offset to SOR
SOR

## Slide 7: Coordination after Handshake
Question/Discussion
  Original discovery scheme already allows scanning for coordination APs after “discovery”
  Improvement by deferred SOR is that Responder knows exactly for how long initiator will be scanning for APs
  Faster session start, no random scanning from Responder necessary
  Multiple packet types with varying functionality SOR/ADV-CONF add implementation complexity and standard variants
  Group preference?

## Slide 8: Summary
Discovery/Initialization
  Encouraging feedback from the discussion to further work on deferred start of ranging
  Intent to work on merging text proposals
MMS MAC TFD
  Expressed interest on extending the UWB only MMS by either OOB, or in-band UWB MAC data protocol
  Proposal to simplify NB channel switching frequency to “per-block” only, and drop “per-slot”, tabled for further discussion
  Discussion on ETSI specification changes regarding CCA bandwidth in ETSI EN 303 687
    Intention is to assure 4ab specification compliance independent of outcome of ongoing regulatory discussions