## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Negotiation of Short-Term Operating Parameters during the MMS Ranging Phase]
Date Submitted: [16 May, 2023]
Source: [Lei Huang, Rojan Chitrakar, Kuan Wu, Bin Qian, David Xun Yang] Company [Huawei Technologies]
E-Mail:[lei.huang1@huawei.com]
Abstract: [The protocol for negotiating short-term operating parameters during the MMS ranging phase is addressed.]
Purpose: [To enable negotiation of short-term operating parameters during the MMS ranging phase.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
PAR Objective | Proposed Solution (how addressed)
Safeguards so that the high throughput data use cases will not cause significant disruption to low duty-cycle ranging use cases | 
Interference mitigation techniques to support higher density and higher traffic use cases | 
Other coexistence improvement | 
Backward compatibility with enhanced ranging capable devices (ERDEVs) | 
Improved link budget and/or reduced air-time | Negotiation of short-term operating parameters during the MMS ranging phase
Additional channels and operating frequencies | 
Improvements to accuracy / precision / reliability and interoperability for high-integrity ranging | 
Reduced complexity and power consumption | 
Hybrid operation with narrowband signaling to assist UWB | Negotiation of short-term operating parameters during the MMS ranging phase
Enhanced native discovery and connection setup mechanisms | 
Sensing capabilities to support presence detection and environment mapping | 
Low-power low-latency streaming | 
Higher data-rate streaming allowing at least 50 Mbit/s of throughput | 
Support for peer-to-peer, peer-to-multi-peer, and station-to-infrastructure protocols | 
Infrastructure synchronization mechanisms | 

## Slide 3: Previous Contributions Related To MMS ranging
[1] 15-23-0100-02-04ab-nba-uwb-technical-framework-for-draft0
[2] 15-22-0381-02-04ab-nba-uwb-ranging-text-proposal-for-15-4ab-tfd

## Slide 4: Recap: Short-term operating parameters
During an NBA-MMS-UWB ranging session, an initiator and a responder shall use the parameters which are set or updated by the next higher layers as the long-term operating parameters.
An initiator may overwrite the long-term operating parameters of a range-measurement cycle by indicating a new set of short-term parameters during the ranging control phase.
  The short-term parameters only take effect in the current range-measurement cycle.
  The long-term operating parameters resume effective in the next range-measurement cycle unless overwritten again during the ranging control phase, of that range-measurement cycle.
  A responder may request short-term operating parameters for the next range-measurement during the ranging control phase. The initiator may serve the responder’s request in the next ranging cycle or ignore the request.
Initialization phase
MMS Ranging phase

## Slide 5: Problem
Protocol for negotiating short-term operating parameters during the MMS ranging phase is not clearly defined.

## Slide 6: Proposal (1)
Initiator may indicate a set of short-term operating parameters in the POLL message, which take effect in the current range-measurement cycle.
      NB Channel Select
      NB PHY Configuration
      NB MAC Configuration (e.g. ranging round duration, ranging block duration)
      UWB PHY Configuration (MMRS code index, MMRS gap size, RIF fragment length, N_MSR)
      UWB MAC Configuration (e.g. Number of RSF, Number of RIF)
Initiator may also request responder to suggest a set of short-term operating parameters for next range-measurement cycle.
      NB Channel Select
      NB PHY Configuration
      UWB PHY Configuration
      UWB MAC Configuration

## Slide 7: Proposal (2)
If a measurement report phase is not present in the current range-measurement cycle or if a measurement report is transmitted by initiator only in the measurement report phase, responder may recommend short-term operating parameters for the next range-measurement cycle in the RESP message.
If a measurement report is transmitted by responder in the measurement report phase, responder may suggest short-term operating parameters for the next range-measurement cycle in the REPORT message transmitted by the responder.
  Note: After the ranging phase in the current range-measurement cycle, the responder may have a better idea on whether or not to suggest short-term operating parameters for the next range-measurement cycle.

## Slide 8: Proposal: NB PHY Config for Control & Report Messages (1)
    If the NB PHY config is indicated in the POLL message, the RESP and REPORT messages are transmitted at the NB PHY config indicated in the POLL message. Otherwise, the RESP and REPORT messages are transmitted at long-term NB PHY config.

## Slide 9: Proposal: NB PHY Config for Control & Report Messages (2)
    The 1st POLL message is always transmitted at long-term NB PHY config (i.e., default NB PHY config, the NB PHY config negotiated during initiation and setup phase, or the NB PHY config set or updated by the higher layer.)
    If the initiator transmits the REPORT message which indicates NB PHY config and receives an acknowledgement from the responder, the POLL message in the following ranging round is transmitted at the NB PHY config indicated in the REPORT message. Otherwise, the POLL message in the following ranging round is transmitted at long-term NB PHY config.

## Slide 10: Proposal: NB PHY Config for Control & Report Messages (3)

## Slide 11: Summary
Protocol for negotiating short-term operating parameters during the MMS ranging phase was addressed.
  Short-term operating parameters which may be indicated by initiator in the POLL message and/or REPORT message
  Short-term operating parameters which may be suggested by responder in the RESP message and/or REPORT message
  NB PHY config used to transmit the POLL message
  NB PHY config used to transmit the RESP and REPORT messages