## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Round hopping and block assignment in hyper blocks – follow up
Date Submitted: May, 2023
Source: Rojan Chitrakar, Lei Huang, Kuan Wu, David Xun Yang (Huawei Technologies)
Email: rojan.chitrakar@huawei.com
Abstract: Follow up on the round hopping and block assignment in hyper blocks
Purpose: Resolve issues with round hopping and block assignment in hyper blocks.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
PAR Objective | Proposed Solution (how addressed)
Safeguards so that the high throughput data use cases will not cause significant disruption to low duty-cycle ranging use cases | 
Interference mitigation techniques to support higher density and higher traffic use cases | 
Other coexistence improvement | 
Backward compatibility with enhanced ranging capable devices (ERDEVs) | 
Improved link budget and/or reduced air-time | 
Additional channels and operating frequencies | 
Improvements to accuracy / precision / reliability and interoperability for high-integrity ranging | 
Reduced complexity and power consumption | 
Hybrid operation with narrowband signaling to assist UWB | 
Enhanced native discovery and connection setup mechanisms | 
Sensing capabilities to support presence detection and environment mapping | 
Low-power low-latency streaming | 
Higher data-rate streaming allowing at least 50 Mbit/s of throughput | 
Support for peer-to-peer, peer-to-multi-peer, and station-to-infrastructure protocols | Round hopping and block assignment issues in hyper block-based mode are resolved.
Infrastructure synchronization mechanisms | 

## Slide 3
Background: Hyper block
Hyper block concept that supports NBA-MMS-UWB ranging is introduced in [1].
A hyper block is a group of blocks.
Hyper block mode uses the time structure that is periodic
  Each hyper block consists of a whole number of blocks.
  different blocks may have different configuration for block duration, Round duration, and slot duration
[1] DCN 23-0059r0 (Jan 2023) “Hyper block concept for use of NBA-MMS”
Round
0
Round
1
Round
0
Round
1
Round
2
Round 5
Block 0
Block 1
Block 2
Hyper Block K
Round
0
……
Block 0
Block 1
Hyper Block K-1
Block 2
Block 0
Block 1
Hyper Block K
Block 2
Block 0
Block 1
Hyper Block K+1
Block 2
……
POLL
RESPONSE
1
1
REPORT
[NB] :
[UWB] :
One Ranging Round
POLL
RESPONSE
1
1
REPORT
2
2
3
3
4
4
POLL
RESPONSE
1
1
REPORT
2
2
3
3
4
4
POLL
RESPONSE
1
1
REPORT
POLL
RESPONSE
1
1
REPORT
2
2
3
3
4
4
5
5
6
6
One Ranging Round
One Ranging
Round
POLL
RESPONSE
1
1
REPORT
2
2
3
3
4
4
One Ranging Round
POLL
RESPONSE
1
1
REPORT
POLL
RESPONSE
1
1
REPORT
One Ranging
Round
One Ranging
Round

## Slide 4
Recap
In [2] we proposed that in the first and each subsequent allocated rounds, the Initiator informs the next assigned block and the Number of Rounds in the assigned block.
  Devices can save power by sleeping till the next assigned block
[2] DCN 15-23/0129r0 (Mar’23), Round hopping and block assignment in hyper blocks
A new IE, Enhanced Ranging Round IE (ERR IE) may be defined.
Octets: 1 | 1 | Bits: 0 | 1 - 15 | Octets: 2 | 0 or 1
Hyper Block Index | Relative Block Index | Hopping Mode | Round Index | Transmission Offset | Number of Rounds
ERR IE

## Slide 5
Error Handling (Issue)
We received queries about error handling if the frame carrying the “next assigned block” and the Number of Rounds is not received by the responder.
  How does the responder figure out its next assigned block?
X
X

## Slide 6
Block Assignment Advertisement (Proposal)
In a selected round(s) in each hyper block, for e.g., the first round of every block, the controller transmits a “special” HBS IE advertising the block assignment for all devices or networks participating in that hyper block.
If a device misses the message carrying the “next assigned block”, it can wake up for the “special” HBS IE and find its assigned block and calculate the number of rounds in the block.

## Slide 7
Block Assignment Advertisement (Proposal)
“Special” HBS IE: An HBS IE [3] carrying a Block Assignment List.
List of Block Assignments (Zero or more). Each Block Assignment carries a list of addresses of network or devices that are allocated a round in the block.
List of address of the network/devices that are allocated one or more round in the block. For network, short address is used.
Octets: 2 | 1 | 1 | variables
Hyper Block Index | Content Control | Ranging Block Description List Length | Ranging Block Description List
Octets: 1 | 1/2/3 | 0/1 | 0/2 | 1 | Variable
Block Index | Block Duration | Round Duration | Slot Duration | Block Assignment List Length | Block Assignment List
Block Description
Number of addresses in the Address List
HBS IE
Bits: 0 | 1 - 7 | Octets: Variable
Address Size | Address List Length | Address List
Block Assignment
Number of Rounds in the block = Block Duration / Round Duration
Size used for addresses in the Address List
0: Short Address (2 octets)
1: Extended Address (8 octets)
[3] 5-23/0155r2, Proposed Text for 4ab MAC - Hyper Block-based Mode

## Slide 8
Summary
We discussed the issue of block assignment and round hopping in hyper blocks.
We proposed:
  In the first and each subsequent allocated rounds, the Initiator informs the next assigned block and the Number of Rounds in the assigned block.
  In a selected round in each hyper block, the controller transmits a “special” HBS IE advertising the block assignment for all devices or networks participating in that hyper block.