## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Device Type Discussion]
Date Submitted: [May, 2023]
Source: [Chenchen Liu, Bin Qian, Lei Huang, David Xun Yang] Company [Huawei Technologies]
Address [Huawei Bantian Base, Longgang District, Shenzhen, 518129 China]
E-Mail:[liuchenchen1@Huawei.com]
Re: [Task Group 4ab: UWB Next Generation]
Abstract: [The Device Type and corresponding features are discussed]
Purpose: [ ]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Background
Many new interesting features have been proposed in 4ab，such as dynamic PHR， MMS， New Rates and LDPC
It is better to categorize the 4ab devices based on the feature set to reduce the complexity

## Slide 3: Device Categories Proposal
The data comm. device shall support dynamic PHR regardless the data rate and coding scheme
If OTA CIR report is supported, the sensing device shall support the dynamic PHR. Otherwise, it may not support dynamic PHR

## Slide 4: PPDU Configuration
PPDU Config | Ranging | Data | Sensing
0 | M | M | M
1 | M | M | M
2 | O | O | O
3 | M | M | M
4 | N/A | N/A | M
5 | N/A | N/A | O
6 | N/A | N/A | O
7 | N/A | M | CM
To reuse the MLME-STS.request primitive, the PPDU configuration can be numbered in the following order. The PPDU configs for each device type is also listed
M = mandatory.
O = optional.
CM = Mandatory if OTA CIR report is supported. Otherwise, optional.
N/A = not supported

## Slide 5: Main Features support by different device type
Features | Ranging | Data | Sensing
4z Mandatory Features | M | M | M
1.95M&62.4M | M | M | M
UWB only MMS | TBD | N/A | N/A
NBA-UWB MMS | TBD | N/A | N/A
SENS PPDU | N/A | N/A | M
124.8M | N/A | O | O
K=7 CC | M | M | M
LDPC | N/A | O | O
Frequency stitching | N/A | N/A | O
Dynamic PHR | N/A | M | CM
OTA CIR | N/A | N/A | O

## Slide 6: References
[1] 15-23-0177-00-04ab-some-thoughts-on-4ab-device-categories
[2] 15-23-0100-02-04ab-nba-uwb-technical-framework-for-draft0
[3] 15-23-0079-01-04ab-latest-consensus-on-uwb-sensing-for-802-15-4ab
[4] P802.15.4z, Draft Standard for Low-Rate Wireless Networks