## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [UWB-only Discovery and MMS]
Date Submitted: [May 16, 2023]
Source: [Pablo Corbalán, Riku Pirhonen, and Srivathsa M. Parthasarathi] Company [NXP Semiconductors]
Re: [Input to the Working Group]
Abstract: [Presentation, Discussion, UWB, Discovery, MMS]
Purpose: [Propose UWB-only solutions for Discovery, Session Establishment, and MMS.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
PAR Objective | Proposed Solution (how addressed)
Safeguards so that the high throughput data use cases will not cause significant disruption to low duty-cycle ranging use cases | 
Interference mitigation techniques to support higher density and higher traffic use cases | 
Other coexistence improvement | 
Backward compatibility with enhanced ranging capable devices (ERDEVs) | 
Improved link budget and/or reduced air-time | 
Additional channels and operating frequencies | 
Improvements to accuracy / precision / reliability and interoperability for high-integrity ranging | Ranging improvements based on UWB-only MMS compared to legacy ranging
Reduced complexity and power consumption | 
Hybrid operation with narrowband signaling to assist UWB | 
Enhanced native discovery and connection setup mechanisms | UWB-only alternative for discovery and session establishment
Sensing capabilities to support presence detection and environment mapping | 
Low-power low-latency streaming | 
Higher data-rate streaming allowing at least 50 Mbit/s of throughput | 
Support for peer-to-peer, peer-to-multi-peer, and station-to-infrastructure protocols | Multi-device discovery
Infrastructure synchronization mechanisms | 

## Slide 3: References
[1] A. Krebs et al. NBA-MMS-UWB ranging text proposal for 15.4ab TFD. IEEE 802.15 contribution with number P802.15-22-0381-02. February 2023. Link.
[2] X. Luo et al. NBA-UWB Technical Framework (for Draft0). IEEE 802.15 contribution with number P802.15-23-0100-02. March 2023. Link.

## Slide 4: Purpose
This slide deck presents a short overview at possible UWB-only solutions for discovery and multi-millisecond ranging (MMS) that could be considered by the working group.
The content of this slide deck proposes a UWB-only alternative to the NBA-MMS-UWB MAC techniques in [1].

## Slide 5: UWB-only Discovery & Session Establishment
Our main idea is to adopt the same scheme as in [1] but with a few modifications for UWB-only solutions:
Generic discovery mechanism for diverse sessions (ranging, MMS, data, sensing)
Exchange should be performed over the baseline (default) PHY/MAC configuration
UWB messages following IEEE MAC Frame Format
  IEs with the content of the ADV-POLL, ADV-RESP, and SOR messages
  Method to exchange UWB PHY-MAC capabilities to establish the session
  IEEE MAC primitives

## Slide 6: UWB-only Discovery & Session Establishment
Discovery Messages: following IEEE MAC Frame Format
Define different IEs for ADV-POLL, ADV-RESP, SOR
Use common table of UWB PHY/MAC Capabilities for the messages
ADV-POLL IE
ADV-RESP IE
SOR IE
Exploit common table of UWB PHY/MAC capabilities
Some fields can be omitted to reduce packet length

## Slide 7: UWB-only Discovery & Session Establishment
Capability List: TLV structure adding the possibility to report optimized structures for particular applications (e.g., MMS or low-latency data exchange) or individual parameters
Tag | Length | Value & Description
0x01 | 16b | UWB Channel: {b0: Ch0, b1: Ch1, … b15: Ch15}
0x02 | 32b | Preamble Codes: {b0: code 1, b1: code 2, …}
… | … | …
0xC0 | TBD | (optimized) Ranging Structure
0xC1 | TBD | (optimized) UWB-only MMS Structure
… | … | …
EXAMPLE
UWB-related content used in NB Compressed PSDU

## Slide 8: UWB-only MMS Extensions
1. Replace SYNC fragment with SP0 in case control information needs to be exchanged.
2. Use SP0 Measurement Report messages.