## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Discussion on re-purposing transmissions for sensing
Date Submitted: May 18, 2023
Authors: Aniruddh Rao Kabbinale, Ankur Bansal, Karthik Srinivasa Gopalan, Mingyu Lee (Samsung)
Abstract: This presentation is a discussion on re-use of transmission for sensing. Also provides updates to control message to enable re-use of transmissions for sensing.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Background
In this set of slides, we discuss use of “non-sensing” transmissions to perform sensing.
  Use of ranging packet formats for sensing
  Use of data comm packets to perform sensing
  Use of MMS ranging transmissions for sensing
Updates to control and scheduling information to enable simultaneous operation
Considering 2 scenarios
Scenario A Scenario B
Slide 2
Aniruddh et.al. (Samsung)
Device A
Device B
Device A
Device B
Device C
Single Tx from Device A
Sensing and Ranging response from Device B
Single Tx from Device A
Sensing response from Device C
Ranging response from Device B

## Slide 3: Use of ranging & data comm packets for Sensing
Sensing measurements to be made on SYNC preamble
  HPRF Ranging sequences of Ipatov 91, with L= 4 spreading to be used – agreed for sensing.
  Also BPRF sequences, ipatov 127 codes optionally supported for sensing
CIR reporting may also be done over other parts of packer – STS, Payload
Sensing packet transmissions are mostly from one requesting device where as ranging messages in TWR is from multiple devices.
  Ranging transmissions from one device to be used to perform sensing
  This is conveyed in scheduling information.
Slide 3
Aniruddh et.al. (Samsung)
Mandatory
Optional
SFD
SYNC
PHR
Payload
STS
SFD
SYNC
PHR
Payload
SYNC
SFD
STS
STS Packet configuration 0
SFD
SYNC
PHR
Payload
STS
Mandatory
Mandatory
STS Packet configuration 1
STS Packet configuration 2
STS Packet configuration 2

## Slide 4: MMS ranging fragments for sensing
Typical MMS ranging packet has RSFs and RIFs (DCN 23-0128)
  Optional l-91 ipatov codes with L=4 spreading to be used for MMRS in this operation
  SYNC fragments and RSF used for performing sensing on top of MMS ranging
MMS exchanges may be two way – MMS RSFs from one device used for sensing
Slide 4
Aniruddh et.al. (Samsung)

## Slide 5: sensing control information
Slide 5
Aniruddh et.al. (Samsung)
Application Control IE (AC IE) – (23-061r0, 23-021r1)
Sensing control updated as per DCN 23-0126. Proposal in DCN 23-178 accommodated, doesn’t need any update in this field.
“Re-purposed transmission for sensing” control field.
  If ranging is re-used for sensing, use configuration in ranging control for packet format and other details.
  If data comm is re-used for sensing, use configuration in data comm control
  If MMS tx is re-used, use configuration from MMS ranging control field?
  (0) Use ranging packet, (1) Use data comm packet, (2) Use MMS ranging packet
CIR from sync only or also other parts of packet to be indicated.
  0 – CIR report from SYNC only. (RSF only in MMS)
  1 – CIR report from SYNC and other fragments: STS (RIF for MMS ranging), PHY payload.
Octets: 2 | 0/4 | 0/1 | 0/1 | 0/2 | 0/TBD | 0/TBD | 0/TBD | 0/TBD
Content Control | Session ID | Block Duration | Round Duration | Slot Duration | Ranging Control | Data Comm Control | Sensing Control | TDoA Control
Bits: 0 | 1 | 2 | 3 | Bits: 0-1 | 2-3 | 4 | 5 | 6-7 | 0 | 1-4 | 5-6 | 7-8 | 9-10 | 11-15 | 0-1 | 2
Common Sensing Control Present | CIR Report Parameters Present | Frequency Stitching Parameters Present | Re-purpose transmission parameters present | Sensing mode | Sensing Packet format | Process CIR report for Range/Velocity | Process CIR report for AOA measurement | reserved | Frequency stitching direction | Base channel number or channel number | Carrier frequency grid configuration ID | Aggregated Bandwidth | Feedback control | reserved | Re-purposed transmission for sensing | Source of CIR report
Present if frequency stitching enabled

## Slide 6: Scheduling IE
Content of this slide is from DCN 23-063r0 and DCN 23-0136r1
The Scheduling IE is used by the controller to schedule slots to be used by intended device.
In scenario A –
  Activity would be ranging /data and “indicator for re-use of transmission” flag would be set to 1
In scenario B –
  Activity for Device B would be ranging and “Indicator for re-use of tx” flag would not be set.
  Activity for Device C would be sensing and “indicator for re-use of tx” flag would be set to indicate the packet used would be of ranging.
  For Device C “Re-purpose tx” in sensing control gives more details about packet used and other config.
Bits: 0–3 | 4-6 | 7 | 8 | 9-10 | 11 | 12-15 | Octets: variable
Scheduling List Length | Scheduling List Type | Address size | Receiver address present | Activity | Indicator for Re-use of transmission for sensing | Reserved | Scheduling List

## Slide 7: Sensing Packet Structure
Segments
  We agree that in the baseline mandatory mode, SENS field has one segment.
  We agree on optional support for 2, 3 and 4 segments in the SENS field.
Gap
  We agree that SENS field includes silent intervals called “gaps”
    When multiple segments are used, we agree to include gaps between segments.
    The duration of each gap interval is one SENS symbol.
    See next slides for figures
RMARKER
  We agree to have one RMARKER for sensing packets. The position of the RMARKER is at the peak of first pulse after SFD (as per 4z).
Slide 7
Aniruddh et.al. (Samsung)

## Slide 8: Sensing Packet Structure
Number of SENS Symbols
  Each symbol corresponds to one period of SENS sequence with spreading
  We agree to support 32, 64, 128 (Mandatory) 16, 256, 512 (optional) symbols per segment for SENS.
  Sequence selection
    We agree that when both SENS and SYNC use length 91 Ipatov sequence, they shall use same Ipatov code index.
CIR Report
  For sensing packets, we agree to support one CIR report per SENS segment per Rx.
Slide 8
Aniruddh et.al. (Samsung)

## Slide 9: Sensing Packet Fields
We agree on the following values for SYNC and SFD configs for sensing packets
  SYNC PSR: 32, 64 (mandatory), 16, 128, 256 (optional).
  SFD length: Same as 15.4z, as specified in table 15-7c.
  For sensing, we agree that fixed PSR is negotiated at higher layers, and the value does not change from packet to packet.
We agree to use 4z PHR, with payload data rates of 1.95, 7.8, 31.2, 62.4 (mandatory), and 124.8Mbps (optional).
  FEC: We agree on BCC K=7 as the FEC for SNES1 and SENS2 packets.
Slide 9
Aniruddh et.al. (Samsung)